## Slide 1: Channel Access Efficiency
Date: 2016-05-18
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP |  |  | khorov@frtk.ru
Anton Kiryanov | IITP |  |  | ant456@ya.ru
Sigurd Schelstraete | Quantenna |  |  | sigurd@quantenna.com
Huizhao Wang | Quantenna |  |  | hwang@quantenna.com

## Slide 2: Background
Trigger frames can schedule UL RUs for both deterministic and random channel access.
To send a Trigger frame, an AP shall contend for the channel with associated STAs and STAs from other BSSs. When the AP wins the contention, it allocates RUs for the STAs. However, when STAs use DCF (or EDCA), collision probability increases.
When the STAs which are given RUs for deterministic access try to send frames in RUs for RA, the contention increases.
What is the most efficient way to allocate channel resource: DCF (EDCA) or Trigger-based?

## Slide 3: Scenario Description
We consider 4 channel access methods
DCF without RTS/CTS
DCF with RTS/CTS
Trigger-based Random Access without RTS/CTS
Trigger-based Deterministic Access without RTS/CTS
In 3 and 4, the STAs can also try to send frames with DCF
All nodes are
in the RX range of each other
No hidden STAs
AP
N STAs

## Slide 4: Trigger-based Random Access without RTS/CTS
………………………………………..
………………………………………..
………………………………………..
………………………………………..
20 MHz
Collisions and empty RU are possible!
20 MHz
20 MHz
20 MHz
Trigger for
Random Access
M-STA
BlockACK
Data
26
SIFS
SIFS
DIFS+
backoff
Trigger for
Random Access
26
26
26
26
26
26
26
26
26
26
26
26
26
26
26
Collision
Success
Empty

## Slide 5: Trigger-based Deterministic Access without RTS/CTS
……………………...……………..
………………………………………..
20 MHz
No collisions,
no empty RUs!
20 MHz
20 MHz
20 MHz
Trigger
M-STA
BlockACK
Data
SIFS
SIFS
DIFS+
backoff
Trigger
N=37 STAs
………………………………………..
………………………………………..
26
26
26
26
26
26
26
26
26
26
26
26
26
26
26
26

## Slide 6: Scenario Parameters
Parameter | Value
Channel width | 80 MHz
Control frame MCS | MCS0
Data frame MCS | MCS5 (272 Mbps @80 MHz)
MSDU size | 1500 byte
Data frame | 1 MSDU 24 MSDUs
Traffic mode | Saturated

## Slide 7: Results (24 MSDUs)
Chart: Throughput
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100
DCF | 224.737 | 217.6683 | 209.9305 | 203.5224 | 198.3243 | 194.0419 | 190.4356 | 187.3383 | 184.6277 | 182.2153 | 180.0463 | 178.0776 | 176.2632 | 174.6027 | 173.0415 | 171.5877
DCF with RTS/CTS | 199.7921 | 202.7181 | 203.0972 | 202.96 | 202.6886 | 202.3877 | 202.0899 | 201.8053 | 201.5362 | 201.2816 | 201.0411 | 200.8134 | 200.5958 | 200.3902 | 200.1913 | 200.0012
Trigger Deterministic | 216.0922 | 231.1149 | 249.5379
Trigger Deterministic + DCF | 225.815 | 226.6552 | 222.7826
Trigger Deterministic + DCF with RTS/CTS | 204.1602 | 219.1509 | 226.4097
Trigger RA | 216.0922 | 115.5574 | 105.2738
Trigger RA + DCF | 225.815 | 169.9914 | 158.3845
Trigger RA + DCF RTS/CTS | 204.1602 | 164.3632 | 160.9632
Trigger RA #RU=4 | 54.023 | 93.5767 | 110.9057 | 105.2738 | 102.2107 | 100.2837 | 98.9591 | 97.9925 | 97.256 | 96.6761 | 96.2076 | 95.8213 | 95.4973 | 95.2216 | 94.9842 | 94.7776
* For Trigger Based Deterministic Access the throughput depends on the # RUs.
For long frames, Trigger-based Random access provides low performance,
while Trigger-based Deterministic access gives the highest throughput
#RUs = N *
#RUs = N = OCW
RU ~4.5ms

## Slide 8: Results (1 MSDU)
DCF provides the lowest performance because of relatively long headers, etc.
Trigger-based Deterministic access shows the best performance.
Trigger based Deterministic Access suffers from STAs which use DCF
Chart: Throughput
Trigger Deterministic | 37.7289 | 65.0072 | 129.5966 | 147.8799 | 175.3134 | 204.5265
Trigger Deterministic + DCF | 46.7625 | 65.34 | 76.3467 | 82.5013 | 80.6142 | 72.9641
Trigger Deterministic + DCF with RTS/CTS | 30.6207 | 44.1206 | 52.2082 | 58.1678 | 58.3297 | 54.0255
Trigger RA | 37.7289 | 32.5036 | 54.6736 | 76.2742
Trigger RA + DCF | 46.7625 | 49.005 | 54.2777 | 50.0873
Trigger RA + DCF RTS/CTS | 30.6207 | 33.0904 | 37.1167 | 37.0866
RU ~2ms

## Slide 9: Remarks
Since the cumulative UL throughput degrades when STAs use Trigger-based random access/DCF/EDCA, it makes sense to improve efficiency of the channel access by using deterministic Trigger-based channel access instead of Trigger-based Random Access/DCF/EDCA.
If STAs are not getting scheduled for a long time, they should have an option to use EDCA/Trigger-based RA as usual.

## Slide 10: Option 1. Limiting EDCA Usage
Those STAs which obtain scheduled RUs should have lower priority when access the channel with EDCA than the STAs which do not obtained RUs in Trigger-frames.
Currently in a BSS there can be only one set of EDCA parameters, which are broadcast in beacons.
We propose to use another set of EDCA parameters for those STAs which are granted scheduled RUs in the Trigger frames. By increasing CWmin and AIFSN, the AP can limit EDCA usage by these STAs, and thus reduce contention.
At the same time, the STAs which are not granted RUs for some time, may have higher priority to access the channel, and thus to notify the AP that they have traffic.
Which set of EDCA parameters shall be used is TBD. It can be defined by the AP explicitly or by the protocol rules, e.g. based on some timeout during which the STA obtains/does not obtain RUs.

## Slide 11: Option 2. Limiting Trigger-based RA usage
Changing EDCA parameters is not enough:
  They are applicable only for EDCA, not Trigger-based RA.
We propose to use similar approach, i.e. to define additional OCWmin for the STAs which have RUs in previous Trigger frames.

## Slide 12: Conclusion
In this presentation, we show that the usage of DCF, EDCA and Trigger-based random access by all STAs (including those which are given dedicated RUs by Trigger frames) decreases performance of the network.
We propose adding a mechanism that allows the AP to configure the usage of EDCA and Trigger-based random access by associated STAs which obtain RUs for transmission.

## Slide 13: Straw Poll #1
Do you agree to add the following text in SFD?
x.y.z The spec shall define a mechanism that allows an AP to assign another set of EDCA parameters to STAs being scheduled by the AP.
Note: For example, these STAs can be
  the STAs which were scheduled recently during some time interval or
  the STAs explicitly listed by the AP.
  Y
  N
  A

## Slide 14: Straw Poll #2
Do you agree to add the following text in SFD?
x.y.z The spec shall define a mechanism that allows an AP to assign another OCWmin to STAs being scheduled by the AP.
Note: For example, these STAs can be
  the STAs which were scheduled recently during some time interval or
  the STAs explicitly listed by the AP.
  Y
  N
  A