## Slide 1: Drop Eligibility Indicator (DEI) Discussion
Date: 2015-05-18
Authors:

## Slide 2: Abstract
802.11aa and 802.11ae introduced the notion of Drop Eligibility to indicate if the corresponding frame or frames belonging to the stream are Drop Eligible
A Drop Eligible frame (or frames of a Drop Eligible stream) might be dropped from further processing if the device has insufficient resources (determination of insufficient resource condition is out-of-scope)
Questions:
  What does Drop Eligibility mean?
  Should DEI be represented in Figures 5-1 and 5-2?
9.2.4.6.2,

## Slide 3: What does Drop Eligibility mean?
Under Insufficient Resources conditions:
Drop the received frame (but still acknowledge it, if it needs to be acknowledged)
Drop the frame from the transmit path
Do either of the above depending on when the Insufficient Resources condition occurs
Option 3 is probably the right one

## Slide 4: Where does DEI belong?
Address 1 address filtering
Block Ack Buffering and Reordering
Duplicate Detection
MPDU
Encryption (Tx)/Decryption(Rx) and Integrity (optional)
Scoreboarding
Null
SYNRA Receiver Filtering (Cl. 9.42)
Replay Detection (optional)
Packet Number Assignment
Do we need to include DEI in Figure 5-1 and Figure 5-2?
If so, where should DEI be in the Tx path and in the Rx Path

## Slide 5: Backup

## Slide 6: DEI Processing
10.3.2.9 Ack procedure has the note below:
  NOTE 2—The receiver STA performs the Ack procedure on all received frames requiring acknowledgment, even if an MSDU or A-MSDU is carried partly or wholly within the frame and is subsequently discarded due to drop eligibility (see DEI subfield in 9.2.4.5 (QoS Control field))
9.2.4.6.2 HT Variant has the following:
  The DEI subfield of the HT Control field(Ed) is 1 bit in length and is set by the transmitting STA to indicate the suitability of the corresponding MSDU or A-MSDU to be discarded if there are insufficient resources at the receiving STA. If there are insufficient resources, a STA that receives an MPDU whose DEI subfield is equal to 1 carrying all or part of an MSDU or A-MSDU should discard the MSDU or any MSDUs contained within the A-MSDU in preference to MSDUs carried in MPDUs whose DEI subfield is equal to 0. See 11.27.2 (SCS procedures). In an MMPDU, the DEI subfield is reserved. The mechanisms for determining whether the resources are insufficient or when to discard MSDUs or A-MSDUs are beyond the scope of this standard.