## Slide 1: Resolution for CID8284
Date: 2016-07-12
Authors:

## Slide 2: Abstract
CID 8284 raises the question of how Association IDs known from infrastructure BSSs are used in Mesh WLAN. Defined as 16 b value the effective range of AIDs is limited to [1 … 2007]. This limitation stems from the (Partial) Virtual Bitmap table in TIM beacon frames.
The present document addresses the comment and answers the question if REVmc/D6.0 needs to be modified.

## Slide 3: CID 8284
Comment | Proposed Change
What is the allowed range for mesh's AIDs? They are currently just described as being held in a 16-bit field | If they can be >2007, then need to change the wording that says that AIDs are in the range 1-2007 (for non-DMG)
In 802.11, the Association ID (AID) serves as shorthand to identify a STA in a BSS
Commenter asks for clarification regarding the permissible numeric range of AIDs in a Mesh BSS (MBSS)

## Slide 4: TIM transmissions in an MBSS
Clause 14.14.4 (TIM transmissions in an MBSS) in 802.11-REVmc/D6.0 explains the use of AIDs in the virtual bitmap of TIM beacon frames
Clause 14.14.4 refers to Clause 9.4.2.6 regarding the encoding of AIDs in TIM beacon frames
  Consequently, AID usage in mesh inherits constrains imposed on AIDs by virtual bitmap size

## Slide 5: AID use in o11s
The open80211s (o11s) [1] project implements 802.11’s mesh functionality in the Linux kernel
The below excerpt of the code [2] indicates that an important mesh STA/BSS implementation
/* TIM map only for LLID <= IEEE80211_MAX_AID */
if (sta->plink_state == NL80211_PLINK_ESTAB)
  has_buffered = ieee80211_check_tim(elems->tim, elems->tim_len,
  le16_to_cpu(sta->llid) % IEEE80211_MAX_AID);

## Slide 6: Recommendation
Adopt revised resolution:
Instruct the editor to modify the last paragraph (lines 35—41) in Clause 14.3.1 on page 2122 of REVmc/D6.0 as follows:
  “A mesh STA that receives and accepts a Mesh Peering Open frame (see 14.3.6.2 (Mesh Peering Open frame processing)) shall assign a unique AID among its neighbor peer mesh STAs to the transmitter of the frame. Since tThe AID is used in the encoding of the TIM element in the Beacon frame (see 9.4.2.6 (TIM element)) setting the AID value is constrained as described in 9.4.1.8 (AID field). AID 0 (zero) is reserved to indicate the presence of buffered group addressed MSDUs and MMPDUs (see 14.14.4 (TIM transmissions in an MBSS)).”

## Slide 7: References
TerraNetAB, “open80211s,” accessed 2016-07-12. [Online]. Available: http://www.o11s.org
GitHub, “mesh_ps.c,” Accessed 2016-07-12. [Online]. Available: https://github.com/o11s/open80211s/blob/master/net/mac80211/mesh_ps.c