## Slide 1: Resolution to CID 8291
Date: 2016-07-14
Authors:

## Slide 2: Abstract
The commenter criticizes that the current text in 9.6.17.3 misses a reference to a section that indicates when to include a
  PREQ,
  PREP,
  PERR, or
  RANN
  element into a HWMP Mesh Path Selection frame. This presentation provides a resolution to the comment.

## Slide 3: Recommendation
Adopt revised resolution:
  Instruct the editor to modify the sentence on lines 55—57 in Clause 9.6.17.3 on page 1217 of REVmc/D6.0 as follows:
    “The HWMP Mesh Path Selection frame contains one or more of the elements indicated in Table 9-372 (HWMP Mesh Path Selection frame Action field format). Usage of the HWMP Mesh Path Selection frame is described in 14.10.7 (Addressing of HWMP Mesh Path Selection frame).”
  Instruct the editor to modify the sentence on lines 63—64 in Clause 9.6.17.3 on page 1217 of REVmc/D6.0 as follows:
    “The PREQ element is set as described in 9.4.2.113 (PREQ element). It is present in a HWMP Mesh Path Selection frame as described in 14.10.9 (Path request (PREQ) mechanism).”

## Slide 4: Recommendation (continued)
  Instruct the editor to modify the sentence on lines 17—18 in Clause 9.6.17.3 on page 1218 of REVmc/D6.0 as follows:
    “The PREP element is set as described in 9.4.2.114 (PREP element). It is present in a HWMP Mesh Path Selection frame as described in 14.10.10 (Path reply (PREP) mechanism).”
  Instruct the editor to modify the sentence on lines 20—21 in Clause 9.6.17.3 on page 1218 of REVmc/D6.0 as follows:
    The PERR element is set as described in 9.4.2.115 (PERR element). It is present in a HWMP Mesh Path Selection frame as described in 14.10.11 (Path error (PERR) mechanism). ”
  Instruct the editor to modify the sentence on lines 22—23 in Clause 9.6.17.3 on page 1218 of REVmc/D6.0 as follows:
    The RANN element is set as described in 9.4.2.115 (PERR element). It is present in a HWMP Mesh Path Selection frame as described in 14.10.12 (Root announcement (RANN) mechanism).”