## Slide 1: 20MHz-only Device in 11ax
Date: 2016-07-25
Authors:
Name | Affiliation | Address | Phone | Email
Joonsuk Kim | Apple | 1 Infinite Loop Cupertino, CA 95014 USA | +1-408-862-3055 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com

## Slide 2
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvell..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Mingyue Ji |  |  |  | 
Vinko Erceg |  |  |  | 
Authors (continued)

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 4
Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 5
Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 6
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 7
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn
Authors (continued)

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 9: Authors (continued)

## Slide 10: Background
In dense networks, it becomes more important to support low power, low complexity devices, by avoiding busy channel access, e.g.,
  Wearable devices
  Home network connectivity
  Automation
  Medical equipments
Such devices do not need high bandwidth operation; only 20 MHz bandwidth with optimized power saving features would be necessary, which also eases overall network loads

## Slide 11: 802.11ax 20MHz-only Devices
We have to introduce 20MHz-only devices in 11ax, both in 2.4 GHz and 5 GHz band
  20MHz-only devices operate in the primary channel
  It can be a part of OFDMA operation of wider bandwidth
    Some RUs in 40/80/160 MHz OFDMA shall not be assigned to 20MHz-only devices, if those RUs are out of band in the Rx filter [1]
  Other mandatory features of 11ax are supported, such as DL/UL-OFDMA or full-BW DL-MU-MIMO

## Slide 12: M/O Bandwidth in 11ax
11ax AP shall not assume all non-AP STAs are 80 MHz operation capable
M: Mandatory
CM: Conditional Mandatory
O: Optional
X: Not Allowed
Frequency | BW [MHz] | RU in OFDMA | Non-AP | Non-AP (20MHz only) | Condition
In 2.4 Gz & 5 GHz | 20 | RU242 | M |  | 
 |  | RU106 |  |  | 
 |  | RU52 |  |  | 
 |  | RU26 |  |  | 
In 2.4 GHz | 40 | RU484 | O | X | 
 |  | RU242 | CM | O | For AP/Non-AP: RU484 with 40MHz
 |  | RU106 |  |  | 
 |  | RU52 |  |  | 
 |  | RU26 |  |  | 
In 5 GHz | 40 & 80 | RU996 | M | X | 
 |  | RU484 |  | X | 
 |  | RU242 |  | O | 
 |  | RU106 |  | M | 
 |  | RU52 |  |  | 
 |  | RU26 |  |  | 
 | 80+80, or 160 | 2xRU996 | O | X | 
 |  | RU996 | M | X | 
 |  | RU484 |  | X | 
 |  | RU242 |  | O | 
 |  | RU106 |  | M | 
 |  | RU52 |  |  | 
 |  | RU26 |  |  | 

## Slide 13: Other Mandatory Features in PHY
Other mandatory features of 80MHz capable non-AP devices are mandatory for 20MHz-only devices, e.g.,
  All preamble formats:
    Transmission/Reception of HE_SU, HE_MU, HE_EXT_SU and HE_TRIG_based preamble
    HE-STF, LTF & GI combinations
  Packet extension with capability
  DL/UL OFDMA & full-BW DL-MU-MIMO in 20 MHz
  SU Beamforming and sounding support
  BCC is mandatory, but LDPC is optional
  TxPwr control for UL-MU

## Slide 14: Other MAC Features
20MHz-only devices shall support other mandatory MAC features, e.g.,
  Basic variant of the trigger frame
  M-BA for acknowledgement of UL MU PPDU
  Responding with CTS to MU-RTS
  UL MU sensing rules

## Slide 15: Example of 11ax Operation
AP may choose the BW operation, with either
  One or multiple 20MHz-only STAs in 20 MHz SU/OFDMA, or
  80MHz capable STAs group, without 20MHz-only, or
  Mixed group of 20MHz-only and 80MHz-capable STAs, where 20MHz-only STAs are only in the primary channel
80 MHz Capable
20 MHz-only

## Slide 16: Summary
We make a definition of 20MHz-only devices
  Mainly cover bandwidth related topics
  All other M/O features for non-AP STA would be carried over

## Slide 17: Straw Poll #1
Do you support following Mandatory and Optional features on bandwidth?
  In 2.4GHz,
    20MHz is mandatory for AP and non-AP
    40MHz is optional for AP and non-AP [signaled in capability field]
  In 5GHz,
    20/40/80MHz is mandatory for AP
    Non-AP can be either 20MHz-only or 80MHz capable [signaled in capability field]
      SFD shall not allow STAs that are 40MHz capable but not 80MHz capable

## Slide 18: Straw Poll #2
Do you support 20MHz-only non-AP STAs operate in primary 20MHz channel as a mandatory mode?

## Slide 19: Straw Poll #3
Do you support 20MHz-only non-AP STAs support tone mapping of RU26, RU52, RU106 and RU242 for
  20 MHz OFDMA in 2.4GHz and 5GHz band
  40, 80, 80+80, 160 MHz OFDMA in 5GHz band*
  [Note*] Some of RUs are restricted for operation [1]

## Slide 20: Straw Poll #4
Do you agree to adopt the spec text change as shown in doc 11/16-0909r0?

## Slide 21: Reference
[1] 11-16-0906-00-00ax-RU-restriction-of-20MHz-operating-devices-in-OFDMA
[2] 11-16-0909-00-00ax-20MHz-only-devices-in-11ax-text