## Slide 1: History and Implementation of the IEEE 802 Security Architecture
Date: 2016-07-26
Authors:

## Slide 2
History and Implementation of the IEEE 802 Security Architecture
Meareg Abreha
San Diego, CA
July 2016
July 2016

## Slide 3
Background
Parameter as security gauges
IEEE 802 security protocols in terms of the chosen parameters
Challenges and Conclusion
Outline

## Slide 4
Background
Early security on IEEE 802:
  Gained attention in the wireless world
  Barely proof of concept for Number theory's application
Security protocols evolved due to:
  Thorough analysis
  Attacks
July 2016

## Slide 5
Parameters as Security Gauges
Parameters that provide the means to control clients and resources in a given network:
Data Access Control and Authentication
      Resource access and controls clients
Data Confidentiality and Integrity:
      Privacy and authenticity of data
July 2016

## Slide 6
Data Access Control and Authentication
Started out with 802.1x standard for port-based network Access control in 2001 - uses the PPP based EAP as its authentication mechanism.
802.1x contains three components and two logical ports.
Authenticator PAE enforces authentication via the uncontrolled port before opening the controlled port to allow supplicants access to resources.
July 2016
Notes: access to the resource is only upon a successful authentication
6

## Slide 7
A little more on 802.1x
802.1x was initially developed for IEEE 802.3 - since 2003, extended to 802.11.
It defines EAP-Over-LAN (EAPOL), a standard encapsulation method to adapt EAP messages sent over Ethernet or WLANs.
July 2016
Notes: 7

## Slide 8
The IEEE 802.11i Enterprise mode implements the 802.1x with authentication servers such as RADIUS
In IEEE 802.21, MIH SA is established either using TLS handshake, (D)TLS or EAP execution over the MIH protocol.
Data Access Control and Authentication on IEEE 802 standards currently
July 2016
Notes: 802.3 (Ethernet)
802.11 (Wi-Fi)
8

## Slide 9: Data Access Control and Authentication on IEEE 802 standards currently
IEEE 802.15.1 (Bluetooth) implements request-response based scheme where specific implementation is dependent on the application used.
In Zigbee (Upper layer extension on top of the IEEE 802.15.4) a trust center/coordinator requests a node for a valid shared network key before it can join the network.
The IEEE 802.16 (WiMAX) (MBWA) implements RSA based authentication function using x.509 certificates or EAP based authentication.

## Slide 10
IEEE 802.20 (MBWA – with Vehicular Mobility support) – has Basic EAP Support Protocol.
IEEE 802.21 (MIH) – uses target network's authentication mechanism before MIH frames exchange.
IEEE 802.22 (TVWS) – uses EAP-TLS or EAP-TTLS (using RSA or ECC based X.509 digital certificate profiles)
Data Access Control and Authentication on IEEE 802 standards currently
July 2016

## Slide 11
Data Confidentiality and Integrity
IEEE 802.3 (Ethernet) security
The IEEE 802.1AE defines a layer 2 security protocol called MACSec.
MACSec provides point-to-point security on Ethernet networks.
The 2010 revision of 802.1x integrated the MACSec with the EAPOL and the IEEE 802.1AR (Secure device identity) to support service identification.
July 2016

## Slide 12
IEEE 802.11 (WLANs) security
Popularity along medium vulnerability- led to a series of security protocols evolution.
The 1999 IEEE 802.11 standard introduced the first wireless protocol called WEP.
WEP uses RC4 algorithm for data encryption and integrity- also the reason for its vulnerability.
Data Confidentiality and Integrity
July 2016

## Slide 13
...WLANs security
IEEE Task Group I was formed to replace the WEP security protocol.
In 2003 the WPA security protocol (an interim protocol) replaced the WEP.
Final draft ratified on June 2004 as 802.11i (security protocol - WPA2)–included on the 2007 amendment of the 802.11.
Data Confidentiality and Integrity
July 2016

## Slide 14
...WLANs security
Wi-Fi Protected Access (WPA)
  TKIP (still RC4 though) for data encryption
  MIC (aka “Michael”) for data integrity
Data Confidentiality and Integrity
July 2016

## Slide 15
...WLANs security
Wi-Fi Protected Access Version 2 (WPA2)
  CCMP (AES based) for data encryption
  CBC-MAC for data integrity
Data Confidentiality and Integrity
July 2016
Notes: CCMP (CBC-MAC protocol)
15

## Slide 16
...WLANs security
WPA/WPA2 vulnerabilities include:
- GTK vulnerability (Hole 196)
- Dictionary based attacks on weak PTK etc.
Data Confidentiality and Integrity
July 2016

## Slide 17
...WLANs security
IEEE 802.1w
Is a 2009 amendment to the 802.11i for protecting management frames
Aims to avoid DoS caused by spoofed disconnect attacks (de-authentication and disassociation)
Data Confidentiality and Integrity
July 2016

## Slide 18
IEEE 802.15.1 (Bluetooth) security
Generates symmetric encryption key from a generated authentication key to encrypt data.
Encryption has three setting modes:
  No encryption
  Point-to-point only encryption – unicast
  Point-to-point and broadcast encryption - both
Data Confidentiality and Integrity
July 2016

## Slide 19
IEEE 802.15.4 (LR WPANs) security
Supports up to 128 symmetric keys based data encryption and authenticity (AES based) with varying degree of protection option for data.
Data Confidentiality and Integrity
July 2016

## Slide 20
IEEE 802.16 (WiMAX) security
Has two component protocols:
    Encapsulation Protocol – secures data across the fixed Broadband Wireless Access Network
    Key Management Protocol- Secure distribution of keying data from the Base Station to the Server Station
Data Confidentiality and Integrity
July 2016

## Slide 21
IEEE 802.20 (MBWA - Vehicular Mobility) security
AES for securing Radio Link Protocol packets
AES CMAC function is used for message integrity
Data Confidentiality and Integrity
July 2016

## Slide 22
IEEE 802.21 (MIHS) security
Keys negotiated during the TLS or EAP MIH SA establishment are used to secure the MIH PDU.
TKIP or CCMP to secure MIH PDUs between heterogeneous IEEE 802 as well as other systems.
Data Confidentiality and Integrity
July 2016

## Slide 23
WRANs (IEEE 802.22) security
Two security sub-layers:
  Sublayer 1 – targets non-cognitive functionalities
  Sublayer 2 – targets cognitive functionalities
Data Confidentiality and Integrity
July 2016

## Slide 24
In sublayer1, encapsulation protocol defines set of supported cryptographic suites.
AES in GCM (Galois Counter Mode) is supported
The cognitive targeting, sublayer 2, provides protection to the incumbents as well as to the 802.22 systems against DoS attack types targeted at that layer.
Data Confidentiality and Integrity
July 2016

## Slide 25
Challenges and Conclusion
Challenges
Weaknesses in security mechanisms
Increasing computing power
Cloud computing changing the way service is provided
Conclusion
Early IEEE 802 security started with simple cryptographic techniques and evolved to its current state.
Future security protocols need to consider the above factors and provide scalable solutions to existing weaknesses.
July 2016

## Slide 26
Thank You!
Questions and comments are welcome :-)
July 2016