## Slide 1: Considerations on WUR Design
Date: 24/07/2016
Authors:
Name | Affiliations | Address | Phone | Email
Igor Kim | ETRI | Korea | +82-42-860-5525 | ikim@etri.re.kr
Sunghyun Hwang | ETRI | Korea | +82-42-860-1133 | shwang@etri.re.kr
Seungkeun Park | ETRI | Korea | +82-42-860-5993 | seungkp@etri.re.kr
Ronny Yongho Kim | Korea National University of Transportation | Korea |  | ronnykim@ut.ac.kr
John (Ju-Hyung) Son | WILUS | Korea | +82-2-552-0110 | john.son@wilusgroup.com
Jin Sam Kwak | WILUS | Korea | +82-2-552-0110 | jinsam.kwak@wilusgroup.com

## Slide 2: Introduction
During 6 month of active discussions in LRLP TIG the final agreement on SG creation was not met
In [1] it has been decided that the WUR SG should be created
WUR SG will only consider low power and not long range
This contribution specifies the potential requirements that must be met during WUR design

## Slide 3: WUR Design Considerations
Extremely low power consumption
Minimum delay for wake-up
Range of wake-up signal should be sufficient
Minimum false positives and false negatives
Co-existence with other 802.11 non-WUR devices
Easy integration and cost
Group wake-up
Usage Scenarios

## Slide 4: Extremely Low power Consumption
Target power consumption should be less than 100 uW in the active state
  Simple modulation such as OOK can be used
  Very limited packet processing
    Careful design of WU frame is needed
    Reduce amount of unnecessary overhead
  Use narrow band transmission
  Use TWT for wake-up signal reception when it is possible
  Etc.

## Slide 5: Low Power vs. Delay Tradeoff
It is known that more sophisticated power saving schemes can result in longer delay
In time critical or emergency situations more attention should be paid to avoid unnecessary delays to bring the main radio up
Otherwise, in some scenarios where the battery replacement could take several years more stress should be given for power saving
The services that will use WUR should be clearly classified by their delay requirements

## Slide 6: Data Range and Wake-up Range
In case 1 AP cannot wake-up nomadic STA2 which moves to the area outside of wake-up range while sleeping
In case 2 AP2’s wake-up range is wider than data range causing unnecessary interference at STA3 associated with AP2
The case 3, when both ranges are equal, is optimal, i.e. the wake-up range should be equal with the data range considering lowest MCS
AP
STA1
STA2
Case 3
AP1
STA1
STA2
Case 2
AP2
STA3
AP
STA1
STA2
Case 1
Data range
Wake-up range

## Slide 7: False Positives and False Negatives
Reduce the likelihood of false positives (false alarm) and false negatives (missed detection)
False positives increase power consumption
False negatives increase delay of wake-ups
False alarm
Successful
detection
Correct rejection
Missed
detection
Wake-up signal
Detection
Present
Absent
Yes
No

## Slide 8: Coexistence with other 802.11 Non-WUR devices
Wake-up signal should start with the legacy preambles
Potential impact on the existing infrastructure should be studied
How much interference those signals will bring, especially to the overcrowded dense network situations?

## Slide 9: Easy Integration and Low Cost
Transmitter modifications should be minimal and easy integrated with the existing circuit
Standard components must be used for fast development and cost reduction
Hardware cost reduction should be realized through the sharing antenna with co-located main radio module
Balance between simplicity and reliability should be met

## Slide 10: Group Wake-Up
When group wake-ups are required?
  DL MU transmissions
  Multicast transmissions
  Broadcast transmissions
Efficient group wake-ups are needed, especially if the network size is large, to meet latency and energy constraints

## Slide 11: Usage Scenarios
 |  | Data Transmission | 
 |  | AP | STA
Wake-up Request | AP | Wake-up: DL Data: DL | Wake-up: DL Data: UL(w/ DL request)
 | STA | Wake-up: UL Data: DL(w/ UL request) (battery-powered AP) | Wake-up: UL Data: UL (battery-powered AP)
Four usage scenarios are possible according to the direction of wake-up request and data transmission

## Slide 12: References
[1] IEEE 802.11-16/0722r1, “Proposal for Wake-Up Receiver (WUR) Study Group”
[1] IEEE 802.11-15/1307r1, “Low-power wake-up receiver for 802.11”
[2] IEEE 802.11-16/0027r0, “LP-WUR (Low-Power Wake-Up Receiver): Enabling Low-Power and Low-Latency Capability for 802.11”
[3] IEEE 802.11-16/0341r0, “Low-power wake-up receiver follow-up”
[4] IEEE 802.11-16/0402r0, “LP WUR Wake-up Packet Identity Considerations”
[5] IEEE 802.11-16/0381r0, “Discussion of Wake-up Receivers for LRLP”
[6] IEEE 802.11-16/1446r12, “LRLP Output Report Draft”