## Slide 1: Bandwidth signaling for EDMG
Date: 2016-07-25
Authors:

## Slide 2: Content
Part 1:
Define channelization and BW/primary channel indication in EDMG header A
Part 2:
Define how to signal BW in RTS/CTS for channel bonding operation

## Slide 3: Part 1

## Slide 4: Bandwidth and primary channel indication
The SFD specifies that:
  An EDMG STA shall be able to determine the primary channel and occupied bandwidth from any EDMG PPDU it receives.
  The EDMG-HEADER-A field has:
    A bandwidth (BW) field that defines the bandwidth of the PPDU and the occupied channels
    A Primary Channel Number field that indicates which channel is the primary channel
We propose to define more precisely those fields
We start by clarifying channelization

## Slide 5: Channelization
We propose:
  To define channelization for up to 6 2.16 GHz channels, which accounts for the accepted expansion of the 60 GHz band in the US
    Ensure that we can further define up to 8 channels
  We propose to change the channelization from non-overlapping to overlapping
    Otherwise channel bonding cannot be used in some regulatory domains (e.g., China)
    Will need to be signaled in the BW field
    Will need to define some rules for primary channel selection
  we consider only 2.16GHz+2.16GHz and 4.32GHz+4.32GHz mode for channel aggregation
    Not support for 4.32+2.16, ..

## Slide 6: Channelization section
Add the following equations:
to describe the relationship between center frequency and channel numbers for 2.16, 4.32, 6.48, 8.64GHz.
We don’t assign channel numbers to an aggregation of non-contiguous channels
  Those are identified by two 2.16GHz channel segments

## Slide 7: Channelization
Channel starting frequency | Channel spacing | channel | Channel center frequency
56.16 | 2160 | 1 | 58.32
56.16 | 2160 | 2 | 60.48
56.16 | 2160 | 3 | 62.64
56.16 | 2160 | 4 | 64.80
56.16 | 2160 | 5 | 66.96
56.16 | 2160 | 6 | 69.12
56.16 | 4320 | 9 | 59.40
56.16 | 4320 | 10 | 61.56
56.16 | 4320 | 11 | 63.72
56.16 | 4320 | 12 | 65.88
56.16 | 4320 | 13 | 68.04
56.16 | 6480 | 17 | 60.48
56.16 | 6480 | 18 | 62.64
56.16 | 6480 | 19 | 64.80
56.16 | 6480 | 20 | 66.96
56.16 | 8640 | 25 | 61.56
56.16 | 8640 | 26 | 63.72
56.16 | 8640 | 27 | 65.88

## Slide 8: Channelization – annex E

## Slide 9: BW and primary channel fields
The SFD specifies 2 fields, one for BW, and one for primary channel.
We propose to add one bit “Channel aggregation” field to differentiate between bonded channels and aggregated channels
  Set to zero for channel bonding or single 2.16GHz
  Set to one for channel aggregation
We propose that the “BW”, “channel bonding” and “primary channel” fields are designed the same way for inclusion in EDMG-Header-A field and in control trailer

## Slide 10: Primary channel indication
We consider 6 channels
  And ensure that we can scale up to 8 channels
We propose to use 3 bits to encode the 3 LSBs of the (channel number -1) corresponding to the primary channel

## Slide 11: Bandwidth field
Proposal: simple 8 bits bitmap
  The “BW” field is 8 bits long:
    Bit 1-8 corresponds to channel 1-8
    For each channel, the corresponding bit is set to 1 if modulated and to 0 if not modulated
With this solution, we can:
  Scale up to 8 channels if more channels become available
  Encode all the bandwidth combinations that we are interesting in

## Slide 12: Part 2

## Slide 13: Motivation
Channel bonding is a pivotal feature for 802.11ay.
Duplicated RTS/CTS must carry the bandwidth information for efficient channel bonding operation.
Control trailer is a good approach for enabling EDMG information to be carried on control PHY messages, including RTS/CTS
  The bandwidth field in the control trailer should then be the same as in EDMA-A header (8 bit bitmap)

## Slide 14: Motivation [cont.]
Control trailer requires additional 2us overhead.
  It increases RTS/CTS overheads by 12%. =2usec/(14usec + 3usec)
  Dense deployments are more sensitive to this overhead, since the RTS/CTS is sent multiple times.
DMG devices can not read this information.
  There is no software upgrade that will enable DMG STAs to read the control trailer. Only new hardware can do that.

## Slide 15: Proposal
We propose to signal a compressed BW field using bits 22-23 in DMG Control Header and the scrambler seed
  This compressed BW field only signals the main channel bonding modes
Side benefit:
  Current SFD defined that bits 22-23 of DMG control header signals both EDMG-Header-A and control trailer [3.1.1 and 6.2.3.2.2].
  This is ambiguous. Our proposal correct that ambiguity

## Slide 16: Proposal
When reserved bits 22-23 are set to 1, use the following codes to signal the following in the scrambler seed:
  [0 0 X X]: indicates the presence of a control trailer
  [0 1 X X]: indicates the presence of an EDMG-Header A
  [1 B1 B2 B3]: in case of RTS/CTS, B1-B3 are used for compressed bandwidth signaling. For other frames, B1-B3 are reserved
Compressed bandwidth is signaled by the scrambler seed.
  Define only commonly used options for this compressed signaling.
  Suggested usage of a 3 bits bandwidth signaling field is relegated to the backup.
Use control trailer on other DMG control mode frames and/or to signal additional bandwidth combinations

## Slide 17: Straw poll #1
Do you agree to change channelization section 6.2.4 of the SFD to include overlapping channels, with the following figure and with the changes proposed in slide 4 and 6.

## Slide 18: Straw poll #2
Do you agree to add to the SFD:
1 bit “channel aggregation” field is added in EDMG-Header-A for SU and MU PPDU
  Set to zero for channel bonding or single 2.16GHz channel
  Set to one for channel aggregation
the “BW” field is 8 bits long:
  Bit 1-8 corresponds to channel 1-8
  For each channel, the corresponding bit is set to 1 if modulated and to 0 if not modulated
The spec shall only allow the following combinations for channel aggregation:
  2.16GHz + 2.16GHz
  4.32GHz + 4.32GHz
the “Primary Channel” field is 3 bits long and contains the 3 LSBs of (channel number-1) corresponding to the primary channel of the BSS.
the format of the BW and Primary Channel fields are the same for inclusion in the EDMG-Header-A field and in the control trailer.

## Slide 19: Straw poll #3
Do you agree to add to the SFD the following and update section 6.2.3.2.2:
When reserved bits 22-23 are set to 1 in the PHY header of a Control mode PPDU, the Scrambler Initialization field shall be formatted as follows [X means that the value for this bit is reserved]:
  [0 0 X X]: indicates the presence of a control trailer (see 3.1.1)
  [0 1 X X]: indicates the presence of an EDMG-Header A.
  [1 B1 B2 B3]: in case of RTS/CTS, B1-B3 are used for bandwidth signaling. For other frames, B1-B2 are reserved."
Y/N/A

## Slide 20: Annex

## Slide 21: Suggested options
In case 3 bits are used to signal BW in scrambler seed
Enumeration of [3 bits] | Signaled CH_BANDWIDTH |  |  | 
0 | CH1+CH2 | CH3+CH4 | CH5+CH6 | Bonded/Aggregated
1 | CH2+CH3 | CH4+CH5 |  | Bonded/Aggregated
2 | CH1+CH2+CH3 | CH4+CH5+CH6 |  | Bonded
3 | CH2+CH3+CH4 |  |  | Bonded
4 | CH3+CH4+CH5 |  |  | Bonded
5 | CH1+CH2+CH3+CH4 |  |  | Bonded
6 | CH2+CH3+CH4+CH5 |  |  | Bonded
7 | CH3+CH4+CH5+CH6 |  |  | Bonded