## Slide 1
AP access procedure for UL MU operation
Date: 2016-07-25
Authors:

## Slide 2: Introduction
An AP could determine its trigger frame transmission
  MU UL decision maker determines its UL transmission
  MU UL decision maker design could be either an implementation issue or a standard issue
  MU UL decision maker might be related to BSR information
After decision making, the AP could transmit trigger frame with several possible solutions of Trigger Frame channel access
  Depending on logical place and time of decision making, possible procedures vary
  Trigger Frame channel access is considered in this submission

## Slide 3: Channel Access of Legacy 802.11[1]
EDCA or DCF (Internal collision in EDCA)
  DIFS or AIFS sensing time after successful transmission
  DIFS or AIFS + back-off after failed transmission
Channel Access after SIFS duration
  Response frames (e.g., Ack frame, CTS, poll, etc.)
  Subsequent frames of fragment burst
  Subsequent frames in PSMP sequence
PIFS based channel Access
  TXOP holder’s frame after first transmission success in an EDCA TXOP
  For some management frames (e.g., TIM, PSMP, etc.)
  PIFS sensing for secondary channels in wideband operation

## Slide 4: Channel Access of Trigger Frame
An AP could determine access category of Trigger Frame channel access
  Allow the AP to choose any access category for contending to send the trigger frame • The chosen AC may give to the AP higher priority in accessing the channel compared to its associated STAs [2][3]
What does “Allow the AP to choose any access category for contending to send the trigger frame” mean?
  Specific procedures need to be determined for Trigger Frame Channel Access as legacy 802.11 standards have defined
  The specific procedures should be specified in 25.5.2.2.3 ‘AP access procedure for UL MU operation’ of Draft 2.0[4]

## Slide 5: Channel Access of Trigger Frame
Unclear points regarding Trigger Frame channel access in SFD
  Does an AP put trigger frame to any queue of chosen AC? (Trigger Frame is considered as a data frame from a channel access point of view)
  Or does an AP transmit Trigger Frame anytime by using AIFS sensing during TXOP duration of chosen AC? (similar to certain management frames)
  Or is independent back-off counter needed for Trigger Frame channel access procedure?
  Is internal contention used for Trigger Frame? (EDCA modification for Trigger Frame channel access)
  Etc.

## Slide 6: Opt 1. Queue Trigger Frame into queue of determined AC
After an AP determined to perform UL MU procedure, the AP determines AC of the Trigger Frame and queues the Trigger Frame in the queue of chosen AC
Contents of Trigger Frame could not be modified after it is queued

## Slide 7: Opt 1. Queue Trigger Frame into queue of determined AC
Time gap between Trigger Frame transmission and Trigger Scheduling could be severe (Validity of UL Schedule)
Easy to implementation
Fairness problems could occur
  Fairness between DL and UL (If an AP queues too many Trigger Frames in its queues of each)
  Fairness between HE and Legacy
Although fairness problem could be solved by nice implementation, UL schedule validity is the problem that cannot be solved

## Slide 8: Opt 2. xIFS sensing based Trigger Frame transmission
Sensing time of PIFS or AIFS(Method of selecting AC is TBD) after Trigger Interrupt is required for an AP to transmit a Trigger Frame

## Slide 9: Opt 2. xIFS sensing based Trigger Frame transmission
If decision maker decide to transmit a Trigger Frame, an AP stops its EDCA procedure and sense its channel during xIFS duration.
If the channel is idle during xIFS, an AP transmits its Trigger Frame without back-off and resumes EDCA

## Slide 10: Opt 2. xIFS sensing based Trigger Frame transmission
Give a extremely high priority on Trigger Frame
Trigger Frame transmission cannot be harmonized with conventional EDCA procedure
AC of Trigger Frame could affect AIFS and TXOP only (no CW value)
Fairness problems could occur
  Fairness between DL and UL
  Fairness between an AP and non-AP STAs
  Fairness among BSSs
  Fairness between HE and Legacy

## Slide 11: Opt 3. Trigger Frame transmission with Separate Back-off procedure
Similar to AIFS sensing based Trigger Frame transmission but an AP performs back-off procedure based on its AC
Method of selecting AC is TBD

## Slide 12: Opt 3. Trigger Frame transmission with Separate Back-off procedure
If decision maker decides to transmit a Trigger Frame, an AP stops its EDCA procedure and performs back-off procedure based on its AC of the Trigger Frame
After Back-off procedure, AP transmits its Trigger Frame and resumes EDCA

## Slide 13: Opt 3. Trigger Frame transmission with Separate Back-off procedure
Concept of CSMA/CA is sustained on Trigger Frame transmission
AC of Trigger Frame affects its channel access more relatively
Trigger Frame transmission cannot be harmonized with conventional EDCA procedure
Cannot provide fairness between DL EDCA Frame and Trigger Frame for UL
  No internal contention between DL EDCA and Trigger Frame

## Slide 14: Opt 4. Winning AC based Trigger Frame transmission
After performing conventional EDCA procedure, an AP determines to transmit its DL Frame with winning AC(internal contention winner) or Trigger Frame

## Slide 15: Opt 4. Winning AC based Trigger Frame transmission
After back-off value goes to 0 based on conventional EDCA, Decision Maker decides to transmit its DL frame of winning AC or a Trigger Frame
If Decision Maker has decided to transmit a Trigger Frame, a DL frame of winning AC needs to participate in internal contention again

## Slide 16: Opt 4. Winning AC based Trigger Frame transmission
AC of Trigger Frame follows winning AC of DL internal contention
Trigger Frame transmission is based on conventional EDCA procedure
Cannot provide fairness between DL EDCA Frame and Trigger Frame for UL
  No internal contention between DL EDCA and Trigger Frame
UL transmission cannot occur if there are no DL frame in AP queue

## Slide 17: Opt 5. Internal contention based Trigger Frame transmission
An AP generates back-off value for Trigger Frame channel access
Based on generated back-off values, Trigger Frame contends with other DL frames of conventional ACs to get TXOP

## Slide 18: Opt 5. Internal contention based Trigger Frame transmission
If Decision Maker decide to transmit Trigger Frame, AP generates its Back-off value of Trigger Frame and participates in internal contention
When AC of Trigger Frame wins internal contention, AP transmits its Trigger Frame

## Slide 19: Opt 5. Internal contention based Trigger Frame transmission
Parameters of Trigger Frame AC might follow parameters of conventional ACs
Trigger Frame transmission is harmonized with conventional EDCA procedure
Provides fairness between DL EDCA Frame and Trigger Frame for UL
Immediate Trigger Frame transmission is hardly supported

## Slide 20: Conclusions
Queueing Trigger Frame in AC queue is simple to implement but there are issue scheduling validity
If trigger scheduling (decision maker design) is implementation issue, second(xIFS sensing based) and third(Separate Back-off for Trigger Frame) options cannot prevent Trigger Frame Spamming
Winning AC based method is not so hard to implement but UL MU cannot be performed if there are no DL data in AP
Last option provides a opportunistic scheduling between DL and UL but it requires modification on EDCA virtual contention

## Slide 21: References
[1] Draft P802.11REVmc_D5.0
[2] 11-16/0662r02 “Further consideration on channel access rule to facilitate MU transmission opportunity”
[3] 11-15/0132r17 “Spec Framework”
[4] Draft P802.11ax_D0.2

## Slide 22: Straw poll 1
Do you think that ‘AP access procedure for UL MU operation’(, i.e., Trigger Frame channel access) needs to be defined in the standard?
  Y
  N
  Abstain

## Slide 23: Straw poll 2
Which option do you prefer? (Vote can be casted multiple times)
  Opt 1. Queue Trigger Frame into queue of determined AC (Y/N/A)
  Opt 2. xIFS sensing based Trigger Frame transmission (Y/N/A)
  Opt 3. Trigger Frame transmission with Separate Back-off procedure (Y/N/A)
  Opt 4. Winning AC based Trigger Frame transmission (Y/N/A)
  Opt 5. Internal contention based Trigger Frame transmission (Y/N/A)

## Slide 24: Straw poll 3 (Opt. 1)
Do you agree to add the following text to 802.11ax Draft?
  25.5.2.2.3 AP access procedure for UL MU operation
    When the AP decides to get UL MU TXOP, the AP generates a Trigger Frame and put the Trigger Frame into the queue of the chosen AC.
  Yes
  No
  Abstain

## Slide 25: Straw poll 3 (Opt. 2)
Do you agree to add the following text to 802.11ax Draft?
  25.5.2.2.3 AP access procedure for UL MU operation
    When the AP decides to get UL MU TXOP, the AP starts its Trigger Frame transmission after CS mechanism determines that the medium is idle for xIFS(PIFS or AIFS, TBD)
  Yes
  No
  Abstain

## Slide 26: Straw poll 3 (Opt. 3)
Do you agree to add the following text to 802.11ax Draft?
  25.5.2.2.3 AP access procedure for UL MU operation
    When the AP decides to get UL MU TXOP, the AP stops its EDCA back-off procedure and starts a new back-off procedure for Trigger Frame based on the chosen AC. After the Trigger Frame transmission, the AP resumes DL EDCA procedure.
  Yes
  No
  Abstain

## Slide 27: Straw poll 3 (Opt. 4)
Do you agree to add the following text to 802.11ax Draft?
  25.5.2.2.3 AP access procedure for UL MU operation
    When the AP get an opportunity to transmit a DL PPDU as a result of EDCA procedure, the AP could transmit a Trigger Frame instead of the DL PPDU.
  Yes
  No
  Abstain

## Slide 28: Straw poll 3 (Opt. 5)
Do you agree to add the following text to 802.11ax Draft?
  25.5.2.2.3 AP access procedure for UL MU operation
    When the AP decides to get UL MU TXOP, the AP generates a back-off value based on the chosen AC of Trigger Frame. The AP decreases the generated back-off value together with the back-off values of other access categories simultaneously. If the generated back-off value of the Trigger Frame becomes 0, then the AP shall transmit the Trigger Frame for UL MU operation.
  Yes
  No
  Abstain