## Slide 1: Channel Bonding Block size
Date: 2016-07-26
Authors:

## Slide 2: Abstract
This presentation defines the block size for channel bonding of 2 and 4 channels

## Slide 3: Channel Bonding SC block format
Channel bonding FFT block size – 1024 chips
  Otherwise, we either loose efficiency on a GI which take a larger part of the time or settle for channels with lower delay spreads
  A shorter GI may be defined later for all bandwidths
For CB 4 – FFT block sizes of 2048 chips.

## Slide 4: Strawpolls:
Insert into section 6.4 of the SFD: “in channel bonding 2, the SC block size is 1024.”
Insert into section 6.4 of the SFD: “in channel bonding 4, the SC block size is 2048.”

## Slide 5: References
11-15-1358-04-00ay-specification-framework-for-tgay