## Slide 1: Relay Enhancement
Date: 2016-09-09
Authors:

## Slide 2: Abstract
This submission highlights the importance of relays in mobile offloading use case in public space.
Some issues in 11ad relaying are discussed.

## Slide 3: Background
Mobile operators focus on 5G cellular for coming 2020. It is very attractive for such operators to offload 5G cellular traffic to 11ad/ay which has lager bandwidth than 11ax, especially in dense environments.
WFA also highlighted “mobile offloading” as the 2nd main stream use case. It potentially has a big market. [1][2]
However, mmWave communication has issues like small coverage, blocking, lack of stability, etc.

## Slide 4: Deployment Scenarios
The issues will be compensated by deploying multiple APs.
However, 11ay APs can cover limited areas. Sometimes 11ay STAs may be out of the coverage area due to STAs being out of range or blocking by human bodies/other obstacles.
Station
blockage
blockage
AP
AP
out of range
out of range

## Slide 5: Alternative Scenarios
Station
AP
AP
Relay will be an alternative scenario to compensate insufficiencies in 11ay coverages for offloading.
relay
relay

## Slide 6: Backhaul Scenario
Station
AP
AP
AP w/o BH
wired BH
wired BH
Relay may also be used for AP w/o wired (or wireless) BH.

## Slide 7: Use case of range extension with relay
It could be applicable in case of low mobility use cases (ex: Stadium, Station).
Stadium
Station
Blockage by human body
Blockage by pole

## Slide 8: Problems with 11ad Relaying
Ref. [3] indicated the following problems in 11ad relaying:
  Lack of support for relay setup between STAs that are outside mutual transmission range (Slide 12).
  Lack of coverage extension procedures (Slide 13).
  Retransmission inefficiency due to lack of scheduling flexibility of fixed First and Second Periods (Slide 14).
  Lack of support for multi-hop relaying (Slide 15).

## Slide 9: Conclusion
Relay for range extension is an important feature for mobile offloading scenario.
Some issues should be examined and resolved for 11ay relay applications.

## Slide 10: Straw Poll
Do you agree to add the following text into 11ay SFD?
The 11ay spec shall include relay enhancement to enable range extension.
Y/N/A =

## Slide 11: References
[1] IEEE 802.11ay Usage Scenarios, 11-15/625r3 (Sep. 2015)
[2] 20150707 Wi-Fi Alliance feedback on 802.11 Task Group AY usage models, 11-15/934r0 (Jul. 2015)
[3] Relays for 11ay, 11-16/337r0 (Mar. 2016)

## Slide 12: Backups

## Slide 13: Problems with 11ad Relaying (1/4)
Lack of support for relay setup between STAs that are outside mutual transmission range.
  Both Source (S-REDS) and Destination (D-REDS) nodes must be part of the BSS/PBSS, and have a direct link setup between them before initiating relay link setup.
Copy from [3]

## Slide 14: Problems with 11ad Relaying (2/4)
Lack of coverage extension procedures.
  Both Source (S-REDS) and Destination (R-DEDS) nodes must be part of the BSS/PBSS before initiating relay link setup.
Copy from [3]

## Slide 15: Problems with 11ad Relaying (3/4)
Retransmission inefficiency due to lack of scheduling flexibility of fixed First and Second Periods.
Copy from [3]

## Slide 16: Problems with 11ad Relaying (4/4)
Lack of support for multi-hop relaying.
  Two 11ay usage models assume multi-hop relays [1]:
    Usage Model 4: Data Center
    Usage Model 8: Wireless Backhauling
  Another usage model could potentially benefit from (multi-hop) relays:
    Usage Model 7: Mobile Fronthauling
Copy from [3]