## Slide 1: Duplicated Control Mode PPDU for 802.11ay
Date: 2016-09-10
Authors:

## Slide 2: Motivation
The 11ay specification shall support multi-channel transmission[1]
  Channel bonding of at least two 2.16 GHz
  Contiguous and non-contiguous channel aggregation of no more than two 2.16 GHz channels or two 4.32GHz channels
As 11ac, wide bandwidth protection may be needed by using RTS and DMG CTS
  RTS and DMG CTS should be sent in 2.16GHz duplicated mode in order to let DMG STAs can decode the duration info and update its NAV.
  The duplicated BW info can be carried in Scrambler Initialization or control trailer field in RTS/DMG CTS.[2]
This contribution discuss the 2.16GHz duplicated mode for 11ay and related issues .
  2.16GHz duplicated mode for DMG control mode.
  Dynamic bandwidth operation for 11ay.
  Control info carried in control trailer field.

## Slide 3: Proposed 2.16GHz duplicated mode
2.16GHz duplicated mode only apply to DMG control mode PPDUs.
  Consists of two or more 2.16GHz DMG control mode transmission in multiple channels.
2.16GHz duplicated mode only carry control frames.
  Has little benefit to carry data or management frame in 2.16GHz duplicated mode
  The most useful case for duplicated mode is wide bandwidth protection by using RTS/DMG CTS.
Phase shift may be applied in each 2.16GHz channel to reduce PAPR—same as 11ac.
  4.32GHz or 2.16GHz+2.16GHz: [1, j]
  6.48GHz: [1, -1,-1]
  8.64GHz or 4.32GHz+4.32GHz: [1, -1,-1,-1]

## Slide 4: Dynamic/Static bandwidth operation
Dynamic/static bandwidth operation is proposed in IEEE 802.11ac
  The RTS/CTS exchange is used to determine the potentially channel width for subsequent transmissions.
  Dynamic bandwidth operation allows narrower bandwidth transmission on the idle channels if some of the channels are sensed idle.
  For static bandwidth operation, if one or more sensed channels are busy, then all the channels will not be used.
  BW and dynamic/static indication are carried in Scrambler Initialization field for 11ac.
11ay can use the similar Dynamic/static bandwidth operation as 11ac
  11ay also support multiple channels transmission, and the RTS/DMG CTS exchange will be used instead of RTS/CTS.
  BW indication has been carried in Scrambler Initialization field or control trailer field for RTS/DMG CTS frame.

## Slide 5: Proposed dynamic/static indication for 11ay
We may need one more bit for dynamic/static indication for 11ay
  We already have BW indication in Scrambler Initialization field or Control Trailer
  Dynamic/static indication is carried in PHY Scrambler Initialization field in 11ac
RTS/DMG CTS without control trailer
  BW indication is carried in Scrambler Initialization field
  Dynamic/static indication can be carried in the reserved bit in Frame Control field or using the I/G bit in TA field as 11ac.
RTS/DMG CTS with control trailer
  Dynamic/static indication can be carried in control trailer field as BW indication, primary channel number indication etc.

## Slide 6: Other proposed change to control trailer
In now SFD, control trailer does not have a CRC field, it’s better to add a 16 bits CRC
  Same as the checking sequence of PHY header field.
  Avoid the receiver using the control info without checking the info’s validity.
For 2.16GHz duplicated RTS/DMG CTS, the meaning of Channel Aggregation subfield in control trailer is not clear.
  In order to let legacy STAs can receive the RTS/DMG CTS, 2.16GHz duplicated PPDU sent in multiple channels can be treated as channel aggregation not channel bonding.
  The Channel Aggregation subfield carried in duplicated RTS/DMG CTS can be used to indicate the channel aggregation/bonding mode of the transmission following the RTS/DMG CTS frame.

## Slide 7: Summary
2.16GHz duplicated transmission on multiple channel is discussed, we proposed the following change to the SFD.
  Define a 2.16GHz duplicated mode for DMG control mode.
  Using the Dynamic bandwidth operation in 11ay.
  Some change to control trailer field or other field in RTS/DMG CTS .
    Add one bit for Dynamic/static indication in RTS/DMG CTS frame, it can be in control trailer, frame control, TA or other field.
    Add a 16 bits CRC checking sequence in control trailer.
    Explain the meaning of the channel aggregation field in control trailer.

## Slide 8: References
11-15-1358-04-00ay-specification-framework-for-tgay
11-16-0954-00-00ay-bandwidth-signaling-for-edmg

## Slide 9: Straw poll/Motion 1
Do you agree to add the following text to the SFD:
A 2.16GHz duplicated mode shall be included in the 11ay specification
  Y/N/A

## Slide 10: Straw poll/Motion 2
Do you agree to add to the SFD:
16 bits “CRC” field is added in control trailer field
Y/N/A

## Slide 11: Straw poll 3
Do you agree to add to the SFD:
If the Channel Aggregation subfield is carried in a control trailer field, it’s meaning the channel aggregation/bonding mode of the transmission following the completion of RTS/DMG CTS that carried the control trailer field.
Y/N/A