## Slide 1: Simulation-based evaluation of OBSS_PD-based SR default parameters
Date: 2016-September
Authors:

## Slide 2: 1. Context
OBSS_PD-based-SR
  Increase SR by using OBSS_PD i.e.:
    For an intra-BSS PPDU, keep using the legacy threshold
    For an inter-BSS PPDU, use OBSS_PD threshold (OBSS_PDThreshold) generally higher
  At the same time, the transmission power (TX_PWR) is adjusted for even greater SR
[1] proposed default parameters for OBSS_PD-based SR
In this submission we,
  Investigate the performances of OBSS_PD-based SR default values for the reference scenario used to test SR [2] and for the enterprise scenario [3]
  Propose a simple method to compute OBSS_PDThreshold based on beacon RSSI
  Highlight the fact that there is trade-off between maximum throughput reachable and fairness
September 2016

## Slide 3: 2. OBSS_PD-based SR mode
How does it work?
  Proportional rule between TX_PWR and OBSS_PDThreshold and boundaries
September 2016
  [1] sets the following default parameters for 80MHz
  OBSS_PDThreshold_min = -76dBm
  OBSS_PDThreshold_max = -56dBm
  TX_PWRref = 23dBm
OBSS_PDThreshold= max
OBSS_PDThreshold_min
OBSS_PDThreshold_min + (TX_PWRref – TX_PWR)
OBSS_PDThreshold_max
min
TX_PWR = TX_PWRRef – (OBSS_PDThreshold – OBSS_PDThreshold_min)
Minimum
Maximum
Adaptation zone
Chart: OBSS_PDThreshold and TX_PWR computed
| 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | -76 | -76 | -76 | -76 | -76 | -76 | -76 | -76 | -75 | -74 | -73 | -72 | -71 | -70 | -69 | -68 | -67 | -66 | -65 | -64 | -63 | -62 | -61 | -60 | -59 | -58 | -57 | -56 | -56 | -56 | -56
OBSS_PDThreshold_max
OBSS_PDThreshold_min
Zone 1
Zone 2
Zone 3

## Slide 4: 3. Reference scenario (1/3)
Topology
Main parameters
  STAs send UDP traffic to their AP in saturation condition
  MCS used for transmission is fixed to 5 (around 200Mbps)
  OBSS_PD-based SR: Naïve approach => Vary TX_PWR (and thus OBSS_PDThreshold) from 1 to 21dB
  Measure BSSs aggregated throughput (throughput observed at AP1+AP2)
  Simulator: ns-3
Goals
  Check on a simple scenario if OBSS_PD-based SR allows to increase SR
  Check if OBSS_PD-based SR boundaries (OBSS_PDThreshold_min and OBSS_PDThreshold_max) fits to the reference scenario
September 2016
30m
3m
3m
AP1
AP2
STA2
STA4
STA1
STA3
BSS2
BSS1

## Slide 5: 3. Reference scenario (2/3)
Results
Observation
  Zone 1: No throughput – TX_PWR used is too weak for allowing frame to be decoded
  Zone 2: BSSs throughput is almost twice than the MCS throughput – Both BSS are able to transmit at the same time – Increase of SR
  Zone 3: BSSs throughput is equal to MCS throughput – No Increase of SR
  Boundaries: OBSS_PDThreshold_max = -56dBm which corresponds to a TX_PWR of 3dBm and reference scenario configures STA to transmit with 15dBm => OBSS_PD-based SR corresponds to zone 2
Conclusions
  OBSS_PD-based SR allows SR increase and default parameters work fine for the reference scenario
  Reference scenario = Simple symmetric scenario => Naïve approach: Use the same TX_PWR for all STAs
    More complex scenarios: Need to have a method to dynamically adapt to the network conditions
September 2016
Chart: BSSs throughput vs TX_PWR
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
 | 0 | 0 | 386.661 | 386.517 | 386.841 | 386.268 | 386.698 | 386.41 | 386.136 | 386.761 | 386.484 | 386.382 | 386.662 | 386.821 | 386.642 | 206.683 | 206.453 | 206.241 | 206.697 | 206.964 | 206.964
Zone 1
Zone 2
Zone 3

## Slide 6: 4. OBSS_PDThreshold or TX_PWR?
We have the relationship between OBSS_PDThreshold and TX_PWR are but one is needed to compute the other
  How to obtain one of them and which one to use is implementation dependent
  In this submission, we define a simple method to obtain OBSS_PDThreshold
How to obtain OBSS_PDThreshold?
  Use of a margin OBSS_PDmargin
  When receiving a beacon, a STA keeps its RSSI and compute OBSS_PDThreshold in the following way:
    OBSS_PDThreshold = BeaconRSSI – OBSS_PDmargin
    Then, compute the associated TX_PWR
September 2016

## Slide 7: 5. Enterprise scenario (1/6)
Topology
  Single floor office building,
    8 offices: 4 APs per office i.e. 32 APs
    64 cubicles per office
    Each cubicle has 4 STAs so 8*64*4 = 2048 STAs
8 offices
1 Office = 64 cubicles
1 Cubicle = 4 STAs
September 2016

## Slide 8: 5. Enterprise scenario (2/6)
Channel allocation: 5GHz
  Four 80MHz channels (Ch1 to Ch4)
Main parameters
  STAs send UDP traffic to their AP in saturation condition
  MCS used for transmission is fixed to 5 (around 200Mbps)
Four 80MHz channels
AP
Channel
1
2
3
4
September 2016

## Slide 9
Observations
  3 zones
    Zone 1: Aggregated throughput is less than the legacy one (around 30% of decrease) => TX_PWR computed is too weak for furthest away STAs – Confirmed by the 5th percentile throughput result
    Zone 2: Increase of aggregated throughput around 55% - 5th percentile throughput per STA is close to the average per STA (20% of difference)
    Zone 3: Increase of aggregated throughput up to 80% - However, 5th percentile throughput results tend to be very different from the average per STA one (up to 74% of difference)
Conclusions
  OBSS_PDMargin highly affects OBSS_PD-based SR performances
  OBSS_PD-based SR default values allow to increase aggregated throughput and to obtain a good fairness
Results: Throughput
Chart: Aggregated Throughput vs OBSS_PDMargin
| Legacy | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
 | 1768.5394 | 1242.9937 | 1240.3699 | 1240.1761 | 1243.0661 | 1242.8572 | 1241.5797 | 1244.0653 | 1241.7942 | 2737.0137 | 2759.4912 | 2763.0052 | 2753.4434 | 2763.4571 | 2818.672 | 2887.996 | 2971.8462 | 3112.5799 | 3183.5149 | 3172.9881 | 3140.1837 | 3138.5966 | 3127.2151 | 3148.591 | 3180.7524 | 3230.883
Zone 1
Zone 2
Zone 3
September 2016
5. Enterprise scenario (3/6)
Chart: Per-Sta Average Throughput and 5th percentile CDF throughput
| Legacy | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Default 5th percentile | 0.52639 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.98612 | 1.014 | 1.0193 | 1.0334 | 1.0102 | 0.95595 | 0.81506 | 0.66089 | 0.52028 | 0.44714 | 0.36968 | 0.34215 | 0.34328 | 0.34334 | 0.34301 | 0.37127 | 0.39476
Default Average | 0.85866 | 0.58332 | 0.58287 | 0.58245 | 0.58311 | 0.58305 | 0.58304 | 0.58364 | 0.58328 | 1.286 | 1.2924 | 1.295 | 1.2894 | 1.2969 | 1.3209 | 1.3523 | 1.3935 | 1.4606 | 1.4914 | 1.4879 | 1.4719 | 1.4698 | 1.4671 | 1.4763 | 1.4952 | 1.5163
Zone 1
Zone 2
Zone 3

## Slide 10: 5. Enterprise scenario (4/6)
Observations:
  Zone 1: Either a GR ratio of 1 or 0 => System is unfair
  Zone 2: Very homogenous GR (between 0.35 and 0.55) – All STA are experiencing the same fairness => System is fair
  Zone 3: Very heterogeneous GR with some STA experiencing a GR close to 0 while others are close to 0.9 => System is unfair
Conclusion:
  Best margin values depend from the objective: for best fairness, an OBSS_PDMargin between 16 and 20dBm is recommended
How is materialized concretely every zone? Goodput Ratio
  Goodput ratio GR: STA Goodput Ratio: GRi = #APUDPReceivedi / #STAUDPSenti
Zone 1
Zone 2
Zone 3
September 2016
Chart: Per-Sta Average Throughput and 5th percentile CDF throughput
| Legacy | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Default 5th percentile | 0.52639 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.98612 | 1.014 | 1.0193 | 1.0334 | 1.0102 | 0.95595 | 0.81506 | 0.66089 | 0.52028 | 0.44714 | 0.36968 | 0.34215 | 0.34328 | 0.34334 | 0.34301 | 0.37127 | 0.39476
Default Average | 0.85866 | 0.58332 | 0.58287 | 0.58245 | 0.58311 | 0.58305 | 0.58304 | 0.58364 | 0.58328 | 1.286 | 1.2924 | 1.295 | 1.2894 | 1.2969 | 1.3209 | 1.3523 | 1.3935 | 1.4606 | 1.4914 | 1.4879 | 1.4719 | 1.4698 | 1.4671 | 1.4763 | 1.4952 | 1.5163

## Slide 11: 5. Enterprise scenario (5/6)
OBSS_PD-based SR is working
  [1] is proposing to use different OBSS_PDTreshold_min – Test -72, -69 and -66 values
  Results for aggregated throughput
Observation
  Changing OBSS_PDThreshold_min does not allow to increase maximum aggregated throughput
  It may gives better results for fairness?
Chart: Aggregated Throughput
| 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Default | 1242.9937 | 1240.3699 | 1240.1761 | 1243.0661 | 1242.8572 | 1241.5797 | 1244.0653 | 1241.7942 | 2737.0137 | 2759.4912 | 2763.0052 | 2753.4434 | 2763.4571 | 2818.672 | 2887.996 | 2971.8462 | 3112.5799 | 3183.5149 | 3172.9881 | 3140.1837 | 3138.5966 | 3127.2151 | 3148.591 | 3180.7524 | 3230.883
72 | 2945.8859 | 2947.2156 | 2933.7266 | 2932.9309 | 2844.2041 | 2834.1912 | 2813.7674 | 2802.6767 | 2798.0463 | 2809.9072 | 2838.7791 | 2901.4194 | 3036.28 | 3118.3864 | 3176.4962 | 3218.4358 | 3219.1084 | 3217.8934 | 3223.4007 | 3218.9386
69 | 2940.9249 | 2933.6576 | 2926.4629 | 2914.7174 | 2897.4412 | 2888.6457 | 2875.7599 | 2893.608 | 2913.7625 | 3009.2888 | 3074.9687 | 3102.7704 | 3127.4088 | 3138.116 | 3133.5118 | 3133.7203 | 3134.9725 | 3136.018
66 | 3040.5661 | 3033.5481 | 3016.9455 | 3011.9031 | 3015.7582 | 3028.8442 | 3083.8932 | 3116.2506 | 3127.7487 | 3138.6881 | 3137.4805 | 3128.009 | 3138.3633 | 3144.9622 | 3119.9552
September 2016
Best aggregated throughput

## Slide 12: 5. Enterprise scenario (6/6)
September 2016
  Results for throughput per STA
Observation
  Changing OBSS_PDThreshold_min does not allow to to obtain better throughput per STA/5th percentile throughput
Conclusion
  OBSS_PD-SR based default value for OBSS_PDThreshold_Min value seems to be optimal for enterprise scenario in order to obtain the best throughput/fairness ratio
Chart: 
| 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Default 5th percentile | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.98612 | 1.014 | 1.0193 | 1.0334 | 1.0102 | 0.95595 | 0.81506 | 0.66089 | 0.52028 | 0.44714 | 0.36968 | 0.34215 | 0.34328 | 0.34334 | 0.34301 | 0.37127 | 0.39476
Default Average | 0.58332 | 0.58287 | 0.58245 | 0.58311 | 0.58305 | 0.58304 | 0.58364 | 0.58328 | 1.286 | 1.2924 | 1.295 | 1.2894 | 1.2969 | 1.3209 | 1.3523 | 1.3935 | 1.4606 | 1.4914 | 1.4879 | 1.4719 | 1.4698 | 1.4671 | 1.4763 | 1.4952 | 1.5163
72 5th percentile | 0 | 0 | 0 | 0 | 0.79572 | 0.87992 | 0.87535 | 0.90998 | 0.92832 | 0.9472 | 0.93516 | 0.82291 | 0.76748 | 0.62803 | 0.56655 | 0.49712 | 0.47 | 0.40415 | 0.3967 | 0.32538
72 average | 1.3817 | 1.3826 | 1.3765 | 1.3756 | 1.3326 | 1.3285 | 1.3212 | 1.3154 | 1.3103 | 1.3177 | 1.3312 | 1.3623 | 1.4249 | 1.4618 | 1.49 | 1.5079 | 1.5099 | 1.509 | 1.5124 | 1.5092
69 5th percentile | 0.38057 | 0.36677 | 0.44489 | 0.69032 | 0.8518 | 0.87025 | 0.89446 | 0.87009 | 0.83555 | 0.75851 | 0.67225 | 0.59827 | 0.54737 | 0.45853 | 0.48203 | 0.47706 | 0.41197 | 0.41332
69 average | 1.3793 | 1.3759 | 1.3702 | 1.3672 | 1.3593 | 1.3561 | 1.3498 | 1.3561 | 1.3684 | 1.4141 | 1.4434 | 1.4549 | 1.4666 | 1.4711 | 1.4696 | 1.4697 | 1.4666 | 1.4706
66 5th percentile | 0.35779 | 0.42091 | 0.51746 | 0.7042 | 0.76558 | 0.81982 | 0.60743 | 0.60294 | 0.52357 | 0.46792 | 0.50257 | 0.4167 | 0.40458 | 0.43287 | 0.43837
66 average | 1.4245 | 1.4207 | 1.4159 | 1.4132 | 1.4143 | 1.4198 | 1.4467 | 1.4602 | 1.4678 | 1.4718 | 1.4685 | 1.4671 | 1.4714 | 1.4731 | 1.462

## Slide 13: 6. Conclusions/next steps
  Preliminary results for OBSS_PD-based SR
    OBSS_PD-based SR works and default parameters seem correct for both SR and enterprise scenario.
  Simple method to compute OBSS_PDThreshold
    Parametrization is of crucial importance: A margin between 16 and 20 dBm is recommended
    Could be improved in many ways to obtain better results (cross-layer information such as ETX, or MCS)
  Compute the TX_PWR based on the network conditions instead of OBSS_PDThreshold

## Slide 14: 7. References
Laurent Cariou et al., 11-16-0945-01 Clarification for OBSS_PD-based SR parameters
Masahito Mori et al., 11-15-0801-00 DCCA/DSC Reference Simulation Results Improvements with Channel selection and Dynamic Sensitivity Control
TGax group, 11-14-0980-16 TGax Simulation Scenarios

## Slide 15: 8. Annex

## Slide 16: Reference scenario
Results
September 2016
Reception power when STA from one BSS transmit to STA in the other BSS
OBSS_PDThresold
Chart: Why Zone 1 is happening?
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
 | -57.2774 | -56.2774 | -55.2774 | -54.2774 | -53.2774 | -52.2774 | -51.2774 | -50.2774 | -49.2774 | -48.2774 | -47.2774 | -46.2774 | -45.2774 | -44.2774 | -43.2774 | -42.2774 | -41.2774 | -40.2774 | -39.2774 | -38.2774 | -37.2774
 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56 | -56
RX sensitivity is reached when the STA is transmitting with a TX_PWR >= 3dBm
RX_PWR at AP when a STA sends to its AP
AP RX sensitivity (-56dBm)
Chart: BSS throughput vs TX_PWR
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
 | 0 | 0 | 386.661 | 386.517 | 386.841 | 386.268 | 386.698 | 386.41 | 386.136 | 386.761 | 386.484 | 386.382 | 386.662 | 386.821 | 386.642 | 206.683 | 206.453 | 206.241 | 206.697 | 206.964 | 206.964
Chart: Why Zone 2 and 3 are happening?
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
 | -82.3769 | -81.3769 | -80.3769 | -79.3769 | -78.3769 | -77.3769 | -76.3769 | -75.3769 | -74.3769 | -73.3769 | -72.3769 | -71.3769 | -70.3769 | -69.3769 | -68.3769 | -67.3769 | -66.3769 | -65.3769 | -64.3769 | -63.3769 | -62.3769 | -61.3769 | -60.3769
 | -54 | -55 | -56 | -57 | -58 | -59 | -60 | -61 | -62 | -63 | -64 | -65 | -66 | -67 | -68 | -69 | -70 | -71 | -72 | -73 | -74
Zone 1
Zone 2
Zone 3
Channel sensed Free
Channel sensed Busy
RX_PWR is becoming higher than OBSS_PDThreshold

## Slide 17: Enterprise scenario parameters
Parameters | Values
Traffic type | UDP CBR uplink transmissions in saturation conditions
MPDU size | 1538 Bytes (from SSD) (1544 Bytes in total incl. all overhead)
Aggregation | Aggregation: 32 MPDUs with 4-byte MPDU delimiter per A-MPDU No A-MSDU Implicit immediate BA
PPDU of Data frame | VHT PPDU (MCS 5, fixed)
Guard Interval | Short
OBSS_PD-based SR | OBSS_PDThreshold_min = -76dBm OBSS_PDThreshold_max = -56dBm TX_PWRref = 23dBm
Simulator | ns-3
September 2016

## Slide 18: Influence of the margin?
  Small margin values result in having furthest away node with a high OBSS_PDThreshold i.e. OBSS_PDThreshold_max and thus the minimum allowed transmission power (risky?)
  High margin results in closest nodes having the smallest OBSS_PDThreshold i.e. OBSS_PDThreshold_min and thus the maximum allowed transmission power (not efficient?)
  A good margin value is probably in-between – Try to find the optimal margin value for the enterprise scenario
September 2016