## Slide 1: CW value after UL MU procedure
Date: 2016-MM-DD
Authors:

## Slide 2: Recap: UL MU EDCA backoff procedure
STA resumes it EDCAF after UL MU regardless of success or failure

## Slide 3: EDCA rules after UL MU
SU
After UL MU, STA could use the remaining BO timer for SU transmission as usual
  The BO timer will decrease as soon as the channel gets idle
  The value of BO counter and CW of the corresponding AC will follow the general EDCA rules
    When the BO counter reaches zero,
TF
TID1
TID3
M-BA
AIFS
BO[VO]: 4
AC VO
empty
Resume EDCA after UL MU
BO[VO]: 4
BO[VO]: 0
AC VO

## Slide 4: CW value after UL MU
If every MSDUs of an AC are successfully transmitted in UL MU, EDCAF will run for empty queue
  The BO timer will decrease as soon as the channel gets idle
  The EDCAF will turn into idle state
    When the BO timer reaches to zero
The CW value may not be initialized appropriately after UL MU
TF
TID1
TID3
M-BA
AIFS
BO[VO]: 4
CW[VO]:127
Idle
AC VO
empty
Resume EDCA after UL MU
BO[VO]: 4
CW[VO]:127
AC VO
BO[VO]: 0
CW[VO]:127

## Slide 5: CW value after UL MU
It is necessary to define rules and conditions for CW initialization after UL MU procedure
  It is better to initialize CW[AC] value when the EDCAF enters into the idle state
  Unless, the STA may draw longer BO counter when the EDCA backoff procedure is invoked by new MSDUs
TF
TID1
TID3
M-BA
AIFS
BO[VO]: 4
CW[VO]:127
Idle
AC VO
empty
Resume EDCA after UL MU
Busy
AC VO
empty
BO[VO]: 4
CW[VO]:127
AC VO
BO[VO]: 67
CW[VO]:127

## Slide 6: Proposal
We propose to initialize CW[AC] when the remaining BO counter reaches zero and the channel gets idle and the EDCA queue[AC] is empty after UL MU procedure
  If any leftover or new MSDUs are enqueued, then EDCAF follows the baseline backoff procedure
TF
TID1
TID3
M-BA
AIFS
AC VO
BO[VO]: 4
CW[VO]:127
Idle
AC VO
empty
Reset CW to CWmin
Busy
AC VO
empty
BO[VO]: 4
CW[VO]:127
BO[VO]: 0
CW[VO]: CWmin[VO]
BO[VO]: 9
CW[VO]: CWmin[VO]

## Slide 7: Conclusion
In this contribution, we have addressed an issue on CW values of non-AP STAs after UL MU procedure
we proposed to define a rule for initializing CW values after UL MU procedure

## Slide 8: Strawpoll
Do you agree to adopt the spec text change as below:
10.22.2.2 EDCA backoff procedure
  When an HE STA successfully receives the corresponding acknowledgement frame in response to the MPDU sent in HE trigger based PPDU, the backoff for the associated EDCAF resumes the backoff counter countdown. If the remaining backoff counter reaches to zero and no data exists for that AC, the CW[AC] value shall be set to CWmin[AC]
  Y/N/A