## Slide 1: CW value after UL MU procedure
Date: 2016-09-13
Authors:

## Slide 2: Recap: UL MU EDCA backoff procedure
STA resumes its EDCAF after UL MU procedure regardless of success or failure

## Slide 3: EDCA rules after UL MU
SU
After UL MU, STA could use the remaining BO timer for SU transmission as usual
  The BO timer will decrease as soon as the channel gets idle
  The value of BO timer and CW of the corresponding AC will follow the general EDCA rules
    The CW and BO timer will be reconfigured depending on the result of SU
TF
BE
VI
M-BA
AIFS
BO[BE]: 4
AC BE
empty
Resume EDCA after UL MU
BO[BE]: 4
BO[BE]: 0
AC BE
STA1
EDCA queue[BE]
BO[BE]

## Slide 4: CW value after UL MU
If every MSDUs of an AC are successfully transmitted in UL MU, EDCAF will resume for the empty queue
  The BO timer will decrease as soon as the channel gets idle
  The EDCAF will turn into idle state
    Unless any additional MSDUs are enqueued before the BO timer reaches zero
The CW value may not be initialized appropriately after UL MU
  No description exists for CW value
  Such situation happens rarely in the existing 802.11
TF
BE
VI
M-BA
AIFS
BO[BE]: 4
CW[BE]:127
Idle
AC BE
empty
Resume EDCA after UL MU
BO[BE]: 4
CW[BE]:127
AC BE
BO[BE]: 0
CW[BE]:127
STA1
EDCA queue[BE]
BO[BE]

## Slide 5: CW value after UL MU
It is necessary to define rules and conditions for CW initialization after UL MU procedure
  It is better to initialize CW[AC] value when the EDCAF enters into the idle state
  Unless, the STA may draw longer BO timer when the EDCA backoff procedure is invoked by new MSDUs
    Such AC is hardly expected to be scheduled at the subsequent UL MU as they reported its BSR as empty
TF
BE
VI
M-BA
AIFS
BO[BE]: 4
CW[BE]:127
Idle
AC BE
empty
Resume EDCA after UL MU
Busy
AC BE
empty
BO[BE]: 4
CW[BE]:127
AC BE
BO[BE]: 67
CW[BE]:127
STA1
EDCA queue[BE]
BO[BE]

## Slide 6: Proposal
We propose to initialize CW[AC] when the remaining BO timer reaches zero and the channel gets idle and the EDCA queue[AC] is empty after UL MU procedure
TF
BE
VI
M-BA
AIFS
AC BE
BO[BE]: 4
CW[BE]:127
Idle
AC BE
empty
Reset CW to CWmin
Busy
AC BE
empty
BO[BE]: 4
CW[BE]:127
BO[BE]: 0
CW[BE]: CWmin[BE]
BO[BE]: 9
CW[BE]: CWmin[BE]
STA1
EDCA queue[BE]
BO[BE]

## Slide 7: Conclusion
In this contribution, we have addressed an issue on CW values of non-AP STAs after UL MU procedure
we proposed to define a rule for initializing CW values after UL MU procedure

## Slide 8: Strawpoll
Do you agree to adopt the spec text change as below:
10.22.2.2 EDCA backoff procedure
  When an HE STA successfully receives the corresponding acknowledgement frame in response to the MPDU sent in HE trigger based PPDU, the backoff for the associated EDCAF resumes the backoff timer countdown. If the remaining backoff timer reaches zero and no data exists for that AC, the CW[AC] value shall be set to CWmin[AC]
  Y/N/A