## Slide 1: Preliminary 11ax PAR Verification
Date: 2016-09-12
Authors:
Name | Affiliation | Address | Email
Hongjia Su | Huawei Technologies | No.200 Jinsu Road, Jinqiao, Pudong, Shanghai | suhongjia@huawei.com
Jiyong Pang |  |  | pangjiyong@huawei.com
Jun Zhu |  |  | zhujun75@huawei.com
Jiayin Zhang |  |  | zhangjiayin@huawei.com
Chixiang Ma |  |  | machixiang@huawei.com

## Slide 2: Introduction
As required in the PAR document [1], 11ax targets to achieve at least four times improvement of average throughput per station compared to 11ac.
Companies had put a lot of efforts into the joint system-level simulation calibration based on [2, 3].
In this presentation, we provide our initial performance comparison between 11ac (OFDM) and 11ax (OFDMA) in scenarios 1&2&3 defined in [2] based upon the evaluation methodology described in [3].
The performance gain varies greatly from scenario to scenario and more group works are encouraged to verify the PAR requirement.

## Slide 3: Simulation Scenario
Standard 11ax scenarios are used as defined in [2]
SS1 – Residential
  5 floor, 20 rooms per floor, 10 STAs per room
  Reuse 3 randomly
  Full buffer
SS2 – Enterprise
  8 offices, 64 cubicles per office, 4 STAs per cubicle
  4 Aps per office with non-overlapping channels
  Mixed traffic model (with traffic ID NO. D1/D2/D3/D4 [2], i.e., DL only)
SS3 – Indoor
  19 BSSs, 30 STAs per BSS
  Full buffer

## Slide 4: Simulation Parameters
Main parameters are subject to the SSD [2] and EMD [3]
20MHz channel at 5G
  For 11ac, EDCA, SU OFDM
  For 11ax, SU OFDMA is applied on 9 26RUs for both DL and UL
1*1 antenna (No MIMO): 20dBm AP Tx power, 15dBm (-2dBi) STA Tx power
CCA PD level: -82dBm
  For 11ax, no CCA after trigger for UL OFDMA
MCS based on link adaptation
RTS/CTS is on for both 11ac and 11ax (MU-CTS)
The used 11ax scheduler is illustrated below
  All UL transmission is based on AP’s trigger
  The DL/UL ratio in one TXOP is fixed in one scheduling window (4 windows per TXOP)
    For DL+UL case, DL:UL = 3:2
    For DL only case, DL:UL = 5:0
    For UL only case, DL:UL = 0:5

## Slide 5: Simulation Result – SS1
Mixed DL+UL is simulated where 21% gain is achieved
DL-portion throughput is significantly improved due to more Tx opportunity at AP side
UL-portion throughput is limited by predefined DL:UL channel occupation in scheduler
Chart: SS1 average throughput per STA (Mbps)
| DL | UL | DL+UL
802.11ac | 0.20133 | 1.7163 | 1.9176
802.11ax | 1.4937 | 0.82496 | 2.3187

## Slide 6: Simulation Result – SS2
Mixed DL Only traffic is simulated where 188% gain is achieved
Traffic model for each AP |  |  |  |  |  | 
Sim Traffic Identifier | Source/Sink | Traffic Model1 | Traffic Model Class Identifier2 | Directional3 | Number of Traffic Services Assigned to STAs in Sim Population (Source/Sink)4 | AC
D1 | AP/STA | Buffered Video Streaming | BV6 | Asymmetric Bi-directional | 2/2 | VI
D2 | AP/STA | Buffered Video Streaming | BV3 | Asymmetric Bi-directional | 6/6 | VI
D3 | AP/STA | VDI | VDI | Asymmetric Bi-directional | 48/48 | VI
D4 | AP/STA | VoIP | VOIP | Symmetric Bi-directional | 10/10 | VO
Chart: SS2 average throughput per STA (Mbps)
| DL
802.11ac | 0.063838
802.11ax | 0.18388

## Slide 7: Simulation Result – SS3
For DL only case, 63% gain is achieved
  mainly from frequency selectivity
For UL only case, 278% gain is achieved (almost 4x)
  mainly from few contention overhead
For mixed DL+UL case, 182% gain is achieved
Chart: SS3 average throughput per STA (Mbps)
| DL Only | UL Only | DL+UL
802.11ac | 0.30458 | 0.19123 | 0.18904
802.11ax | 0.49781 | 0.66792 | 0.5336

## Slide 8: Conclusion
4x gain could almost be achieved in SS3 uplink-only case.
The gain of OFDMA over OFDM is mainly from MU diversity in frequency, lower contention overhead in UL and more transmission opportunity in DL (for mixed DL+UL case).
Additional gain could be obtained by applying more 11ax features such as enhanced DL MU-MIMO, UL MU-MIMO as well as spatial reuse.
We suggest more companies to contribute to the 11ax PAR verification in future
  using standard 11ax scenarios as much as possible
  based on a common 11ac baseline
  trying to align the 11ax MAC mechanism (especially the scheduler)

## Slide 9
References
[1] 11-14-0165-01-0hew-802-11-hew-sg-proposed-par
[2] 11-14-0980-16-00ax-simulation-scenarios
[3] 11-14-0571-12-00ax-evaluation-methodology