## Slide 1: Considerations on CR for 2665, 2719
Date: 2016-09-15
Authors:

## Slide 2: Abstract
Some comments (CIDs 2665, 2719) are concerned with how to adjust the backoff counter during color code based CCA.
We agree with the commenters in principle and suggest that comment resolutions should be carefully considered combining MAC and PHY for supporting color code based CCA.
  So far, color code based CCA rules are specified in MAC (section 25.9), while HE PHY receive procedure in case of inter-BSS PPDU is specified in PHY (section 26.3) of TGax draft D0.4 [1].
  We propose to add texts which clarify how to adjust backoff counter during the period of time that is taken by the receiving STA to validate the PPDU and behave after BUSY state in section 25.9.2 color code based CCA rules.
  Meanwhile, we propose to consider more details about HE PHY receive procedure (section 26.3) in case of inter-BSS PPDU for supporting color code based CCA.

## Slide 3: Background
So far, color code based CCA rules are specified in TGax D0.4
  A STA should regard an inter-BSS PPDU with a valid PHY header and that has receiving power/RSSI below the OBSS_PD level used by the receiving STA and that meets additional TBD conditions, as not having been received at all (e.g., should not update its NAV), except that the medium condition shall indicate BUSY during the period of time that is taken by the receiving STA to validate that the PPDU is from an inter-BSS, but not longer than the time indicated as the length of the PPDU payload.

## Slide 4: Background (con’t)
Also, HE PHY receive procedure in case of inter-BSS PPDU is specified in section 26.3.18 HE receive procedure.
  …… If the BSS color doesn’t contain an intended value, the PHY entity shall set PHY_RXSTART.indication(RXVECTOR) then set PHY_RXEND.indication (Filtered). The PHY entity shall receive HE-STF for 4us after HE-SIG-A. The PHY entity shall maintain PHY-CCA.indication(BUSY, channellist) primitive for the predicted duration of the transmitted PPDU, as defined by RXTIME in Equation (21-106), for all supported modes, unsupported modes, Reserved HE-SIG-A Indication, and invalid HE-SIG-A CRC. ……

## Slide 5: Background (con’t)
PHY receive state machine in current draft (only inter-BSS PPDU filtered out related part)

## Slide 6: Issue
Based on color code based CCA rules in MAC, the HE STA should regard the inter-BSS PPDU as not having been received at all in the case of that the PPDU is inter-BSS PPDU & SR_disallowed (no) & receiving power below the OBSS_PD level after receiving and checking the contents of HE-SIG-A.
Incoming Frame ( -72dBm)
Time
The STA decodes SIG-A, checks BSS color and SR field in HE-SIG-A.
Channel busy
In case of inter-BSS PPDU & SR_disallowed(no) & receiving power below the OBSS_PD level (e.g. -62dBm), the HE STA should regard the inter-BSS PPDU as not having been received at all, and resume the backoff countdown process after the medium is idle for the duration of a AIFS period. Otherwise continue to suspend the countdown process.
Channel sensing detection in 4us
MAC SR behavior
STA transmits its frame
Countdown counter = 0`
Channel idle
E.g.

## Slide 7: Issue (con’t)
However current HE PHY receive procedure specified in TGax D0.4 doesn’t support color code based CCA feature yet.
Incoming Frame ( -72dBm)
Time
Channel busy
In case of inter-BSS PPDU & SR_disallowed(no) & receiving power below the OBSS_PD level (e.g. -62dBm), the HE STA is not allowed to regard the inter-BSS PPDU as not having been received at all, and resume the countdown process, because the PHY entity shall maintain PHY-CCA.indication(BUSY) primitive for the predicted duration of the transmitted PPDU.
Channel sensing detection in 4us
MAC SR behavior
Channel idle
PHY behavior
PHY-CCA.indication (BUSY)
PHY-CCA.indication (IDLE)
STA transmits its frame
Countdown counter = 0`
The STA decodes SIG-A, checks BSS color and SR field in HE-SIG-A.
E.g.

## Slide 8: Issue (con’t)
Should we provide addition to PHY procedure clause to support color code based CCA rules?
  Besides BSS color, other factors, such as OBSS_PD level, SR_disallowed[2], and SR_delay[3], should be taken into account to filter out inter-BSS PPDU.

## Slide 9: Proposal
we propose that
  The baseline backoff procedure is maintained during the period of time that is taken by the receiving STA to validate the PPDU.
When an inter-BSS PPDU arrives at a STA,
  The backoff procedure of that STA is suspended if the channel is indicated as BUSY at the beginning of preamble based on the legacy CCA rules.
  Then, after receiving HE-SIG-A / MAC header successfully,
    If the channel is determined to be IDLE using color code based CCA rules (inter-BSS frame & SR_disallowed(no) & the receive power below OBSS_PD level) for the duration of an AIFS, then the backoff procedure is allowed to be resumed.
    If the channel is determined to be BUSY using color code based CCA rules, the receiving process continues and the backoff procedure is still suspended.

## Slide 10: Proposal (con’t)
Meanwhile it is also necessary to carefully consider the HE PHY receive procedure to support color code based CCA.
  Besides BSS color, we propose to take SR_disallowed & OBSS_PD level & SR_delay into account to filter out inter-BSS PPDU as the following cases.
    Case A: BSS color matched (no) & SR_disallowed (no) & RX power below
    OBSS_PD level & SR_delay (no)
    Case B: BSS color matched (no) & SR_disallowed (no) & RX power below
    OBSS_PD level & SR_delay (yes)
    Case C: BSS color matched (no) & SR_disallowed (no) & RX power above
    OBSS_PD level & SR_delay (yes or no)
    Case D: BSS color matched (no) & SR_disallowed (yes) & RX power
    below or above OBSS_PD level & SR_delay (yes or no)

## Slide 11: Proposal (con’t)
Meanwhile it is also necessary to carefully consider the HE PHY receive procedure to support color code based CCA.
  We propose the following receive procedure to each corresponding case
    Case A: Filtered out: Set PHY-RXSTART.indication(RXVECTOR) then set
    PHY_RXEND.indication(Filtered). Then set PHY-CCA.indication(IDLE).
    Case B: Filtered out: Set PHY-RXSTART.indication(RXVECTOR) then set
    PHY_RXEND.indication(Filtered). Then set PHY-CCA.indication(IDLE)
    when predicted duration based on RXTIME has elapsed. (TGax D0.4 )
    Case C: not filtered out.
    Case D: not filtered out.

## Slide 12: Proposal(con’t)

## Slide 13: Proposal (con’t)
Additional discussion: when does PHY entity know how to adjust OBSS_PD level accompanying by TX power?
  It would be better to add interactions between PHY and MAC during color code based CCA.
    Option 1: (may suit to OBSS_PD-based SR mode)
      The PHY can adjust OBSS_PD level accompanying by the TX power which is included in the latest TXVECTOR from the MAC.
      Option 1 may not suit to SRP-based SR mode cause the TX power and OBSS_PD threshold may be adjusted per PPDU.

## Slide 14: Proposal (con’t)
Additional discussion: when does PHY entity know how to adjust OBSS_PD level accompanying by TX power?
  Option 2:
    Define a PHY SAP inter-(sub)layer service primitives to deliver OBSS_PD level from the MAC to the PHY, e.g. define a new PHY-SR (OBSS_PD level) primitive or reuse the existing primitive such as PHY-CONFIG primitive.
    PHY receive procedure using PHY-SR(OBSS_PD level) primitive as an example
      When an inter-BSS PPDU comes
      …… if the BSS color doesn’t match & SR is allowed (SR_disallowed(no)), the MAC adjust OBSS_PD threshold based on the reported information from the PHY, then the MAC issues PHY-SR(OBSS_PD level) primitive to the PHY.
      The PHY updates its OBSS_PD level using the value indicated in PHY-SR(OBSS_PD level) primitive. Then the PHY compares RX signal power with the updated OBSS_PD level.
      The PHY may issue a PHY-RXEND.indication (Filtered) primitive if RX power below OBSS_PD level then set PHY-CCA.indication (IDLE) in case A or when the predicted RXTIIME elapsed in case B of which examples are in the following slides.

## Slide 15: Proposal(con’t)
  Case A: BSS color matched (no) & SR_disallowed(no) & RX power below OBSS_PD level & SR_delay (no)

## Slide 16: Conclusion
We proposed to add texts which clarify how to adjust backoff counter during the period of time that is taken by the receiving STA to validate the PPDU and behave after BUSY state in section 25.9.2 color code based CCA rules.
Meanwhile, we propose to take BSS color & SR_disallowed & OBSS_PD level & SR_delay into account to filter out inter-BSS PPDU for supporting color code based CCA.
Additional discussion: when does PHY entity know how to adjust OBSS_PD level accompanying by TX power
Note: The proposed comment resolution is contained in 11-16/1025r2

## Slide 17: References
Draft P802.11ax_D0.4, August, 2016
11-16-0947-04-00ax-proposed-text-changes-for-obss-pd-based-sr-parameters
11-16-1121-00-00ax-spec-texts-spatial-reuse-indication-for-trigger
11-16-0920-03-00ax-phy-comment-resolution-for-cid-1659-493-494
Draft P802.11REVmc_D8.0