## Slide 1
MU mode EDCA control
Date: 2016-09-11
Authors:

## Slide 2: Introduction
Modification of back-off value after trigger frame was discussed and specified[1][2]
  When an HE STA successfully receives the corresponding acknowledgement frame in response to the MPDU sent in HE trigger based PPDU, the backoff for the associated EDCAF resumes the backoff counter countdown.
  When an HE STA does not receive the corresponding acknowledgement frame in response to the MPDU sent in HE trigger based PPDU, the backoff for the associated EDCAF resumes the backoff counter count-down.
Longer SU Back-off would enhance BSS performance[3]
  Frequent MU transmission could occur
  Small channel access delay achieves large channel utilization

## Slide 3: New EDCA set for MU opportunity
New EDCA set[4]
  MU EDCA set is a new EDCA parameter set that it lowers STAs’ channel access opportunity
  MU EDCA set could be used for enhancing 11ax efficiency
  When MU EDCA is indicated, HE non-AP STAs shall use MU EDCA parameters for its SU channel access
  MU EDCA indication might be performed by Trigger Frame
    For some HE STAs or all the HE STAs
    For each AC or all ACs
    SU EDCA indication is possible, also (Return to conventional EDCA)
  As a result of MU EDCA set, STAs would transmit HE trigger-based PPDUs rather than other SU PPDUs

## Slide 4: MU mode EDCA from new EDCA set
If UL MSDU is arrived after EDCA mode change indication (in Trigger Frame), MU EDCA parameters for the MSDU can be applied - No problem

## Slide 5: Issue for MU mode EDCA
But if each STA already have back-off counter for SU UL transmission and have performed SU EDCA procedure, what kind of procedure needs to be performed by the STA?
  Sustain existing back-off value or get new back-off from MU EDCA set immediately?

## Slide 6: Issue for MU mode EDCA
Does retransmission count affect its new back-off procedure of MU EDCA?
  If retransmission occurred, how new EDCA CW would be applied to its exist channel access procedure?(CW_MU_min? or more larger one? or doubled CW of SU EDCA parameter?)

## Slide 7: Possible solutions for MU mode EDCA
Option 1-1 (Reset back-off and CW doubling)
  Reset its back-off number based on a changed EDCA set
  Retransmission history is not considered(CWmin_mu for ReTx)
Option 1-2 (Reset back-off but CW based on # of ReTx)
  Reset its back-off number based on a changed EDCA set
  Using CW value considering retransmission(2^(n-1)* CWmin_mu)
Option 2-1 (Sustain back-off for last frame)
  Sustain last EDCA procedure until transmission success or retransmission limit (MU mode is applied after EDCA procedure of last frame)
Option 2-2 (Sustain back-off for last frame once)
  Sustain last EDCA procedure only once
  Whether the transmission is success or not, next transmission follows option 1(Do not reset back-off number but applying new CW immediately)

## Slide 8: Further considerations
‘No EDCA’ also indicated by AP
If STAs receive ‘No EDCA’ indication, STAs stop its EDCA procedure and just wait trigger frame for its UL transmission
Using ‘No EDCA’ also has similar options of previous slide
‘No EDCA’ could be used for very frequent and light traffic pattern from multiple devices
Adopting ‘No EDCA’ requires more discussions

## Slide 9: Conclusions
Because TG determined “EDCA back-off value is not changed after its trigger frame reception and transmission of HE Trigger based PPDU”, we prefer to apply this concept for MU mode EDCA, too.
In other words, we prefer option 2 rather than option 1.
Retransmission contention windows need to be considered
  CWmin_mu for first retransmission after MU mode indication
  2^(n-1)* CWmin_mu for first retransmission after MU mode indication where n is number of retransmission

## Slide 10: References
[1] Draft P802.11ax_D0.4
[2] 11-16/0880r2 “UL MU Transmission Rules - EDCA backoff”
[3] 11-16/0684r2 “Channel access efficiency”
[4] 11-16/0998r1 “2 sets of EDCA parameters”