## Slide 1: PKEX issue in 802.11ai
Date: 2016-09-13
Authors:

## Slide 2: Abstract
This presentation discusses the PKEX issues.

## Slide 3: PKEX Exchange
Intended to allow two parties to exchange a “raw” public key for use with FILS public key authentication
Uses a password to authenticate the exchange and encrypt the exchanged public keys

## Slide 4: PKEX Exchange
sB
PB = sB*G
sA PA = sA*G
Pwe = F(pw)
mA = H(macA)
CA = PA + mA*Pwe
CA
CB
m’B = H(macB)
P’B = CB - m’B*Pwe
if (min(nonceA, nonceB) == nonceA
x = H(nonceB|| nonceA)
k = Kdf(x, "PKEX Key Confirmation",
CB || CA || macB || macA || F(S))
else
x = H(nonceA || nonceB)
k = Kdf(x, "PKEX Key Confirmation",
CA || CB || macA || macB || F(S))
checkA = HMAC(k, PA || P’B ||
macA|| macB)
checkA
After the exchange: - Alice has Bob’s public key PB and has validated its ownership to that of the owner of the shared secret
- Bob has Alice’s public key PA and has validated its ownership to that of the owner of the shared secret
Bob
Alice
shared secret pw
Pwe = F(pw)
mB = H(macB)
CB = PB + mB*Pwe
m’A = H(macA)
P’A = CA - m’A*Pwe
if (min(nonceB, nonceA) == nonceB
x = H(nonceA || nonceB)
k = Kdf(x, "PKEX Key Confirmation", CA || CB || macA || macB || F(S))
else
x = H(nonceB|| nonceA)
k = Kdf(x, "PKEX Key Confirmation", CB || CA ||
macB || macA || F(S))
checkB = HMAC(k, PB || P’A || macB|| macA)
checkB
Validate
checkB == HMAC(k, PB || PA || macB|| macA)
Validate
checkA == HMAC(k, PA || P’B || macA|| macB)

## Slide 5: What’s the Problem?
Only truly secure when the same public key is not used in multiple PKEX runs
Running PKEX multiple times with the same public key opens up two attacks:
  Off-line dictionary attack to determine the password(s) used
  Man-in-the-middle attack to insert an adversary’s public key

## Slide 6: Off-line Dictionary Attack
Adversary watches two exchanges in which she knows that the same public key was used both times (let’s say from “Alice”)
CA1 = PA + QA1 = PA + (mA*Pwe1)
CA2 = PA + QA2 = PA + (mA*Pwe2)
Therefore, adversary knows CA1 - CA2 = QA1 - QA2
Adversary can go offline and check all N2 password combinations where N is number of possible passwords
Birthday paradox makes this an O(N) attack not O(N2)

## Slide 7: Off-line Dictionary Attack
If the adversary learns the password after the exchange is over the so what? Keys are exchanged, nothing is subverted
If dictionary attack can be done in real-time though, the exchange can be subverted by inserting the adversary’s public key into the exchange
Dictionary attacks are getting faster and faster

## Slide 8: Man-in-The-Middle Attack
Adversary knows that the same key is being used a second time (let’s say by “Bob”)
Adversary gets C1, modifies C2 = C = PB + QB by determining QB (knows PB) and inserts adversary’s key
But adversary cannot decrypt PA to complete attack because she doesn’t know QA
To determine QA, it is necessary to take a discrete logarithm from an unknown root
  An Nth root equation where N is the number represented by the hash of the MAC address
  Extremely unlikely this compute power is readily available
But the fix is easy, add the password to the KDF

## Slide 9: Man-in-The-Middle Attack
There is an easier attack but it requires both parties to exchange the same key multiple times
There is really no reason why people would do PKEX twice with the same keys– if they exchanged their keys once what’s the point?
Somewhat of a contrived attack, but the fix is the same, add the password to the KDF

## Slide 10: Conclusion
The Man-In-The-Middle attack is an easy fix
The dictionary attack is more severe
802.11 has a history of releasing security protocols with flaws– PSK mode, WEP
It is possible to replace PKEX with something that does not suffer from the problems presented here
PKEX is not critical to FILS, it’s optional and it’s still possible exchange “raw” public keys in a manner outside the scope of the standard.
Let’s just get rid of PKEX

## Slide 11: References