## Slide 1: What should 802.11 WG do about the ED related request from 3GPP RAN1?
14 Sep 2016
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: 3GPP RAN1 & IEEE 802 are having an ongoing discussion related to LAA’s ED threshold
  The IEEE 802 review of LAA Rel. 13 resulted in IEEE 802 requesting 3GPP RAN1 to make LAA more sensitive to 802.11 transmissions:
    See Comment 3 in 19-16-0037-09 for details (March 2016)
  3GPP RAN1 rejected the request on the basis that they have had considerable debate and have agreed there is not a problem, but without responding to the particular issues raised by IEEE 802
    See Response 3 in R1-166040 (June 2016)
  IEEE 802 responded by noting that 3GPP RAN1’s assertions are based on invalid assumptions about common 802.11 deployments and asking 3GPP RAN1 to rerun their simulations with more realistic assumptions
    See IEEE 802 liaison to 3GPP RAN (August 2016)
  The issue is currently still open and unresolved …

## Slide 3: 3GPP RAN1 are now requesting that 802.11 also adopt a lowered ED threshold of -72dBm
  In R1-166040 (June 2016), 3GPP RAN1 further suggested that 802.11 be redefined to also use an ED of -72dBm in the future ...
  … rather than the currently defined ED of -62dBm (and PD of -82dBm)
  Such a change would mean that 802.11 would defer to LAA (and 802.11) at the same ED threshold that LAA currently defers to 802.11
RAN1 respectfully requests future IEEE 802.11 technologies to align the energy detection threshold used with other technologies operating in the same unlicensed band, e.g., -72 dBm.
An energy detection threshold of -72 dBm has been chosen by 3GPP for Rel-13 LAA also with an interest in aligning with other technologies in the future.

## Slide 4: IEEE 802 have not yet responded to 3GPP RAN1’s request for 802.11 to use ED threshold of -72dBm
  In July 2016, IEEE 802.19 focused on responding to 3GPP RAN1’s responses on the twelve open issues in IEEE 802’s March 2016 liaison
    It did not respond to 3GPP RAN1’s request for ED = -72dBm
  In Sept 2016, a thought piece was presented to IEEE 802.19 WG that discussed some possible responses to 3GPP RAN1’s request
    See 19-16-0110-00 (by Andrew Myles, the author of this summary)
  After discussion in the IEEE 802.19 WG, there was consensus that the request really needs to be considered by IEEE 802.11 WG
    It is probably of particular interest to IEEE 802.11 Tgax from a technical perspective
  A timely response probably requires IEEE 802 to develop a response out of the Nov 2016 plenary
    Although it was suggested by an 802.19 participant that IEEE 802 could simply ignore the request

## Slide 5: There are many related issues that need to be addressed before responding to 3GPP RAN1
Some potential related (mostly technical) issues
  What is the effect of ED = -72dBm on billions of legacy devices?
  Does an ED = -72 dBm make sense when 802.11ax is focusing on improved frequency reuse?
  Should IEEE 802 continue recommending that LAA should be more sensitive to 802.11 transmissions?
  Should IEEE 802 recommend that LAA adopt 802.11 ED/PD levels?
  Should IEEE 802 recommend that LAA use 802.11 preambles (or CTS-to-self wrappers) to make it easier for 802.11 to detect LAA?
  How should IEEE 802 deal with related proposals in ETSI BRAN that the next revision of EN 301 893 specify an ED = -72dBm?
  …

## Slide 6: How should IEEE 802.11 WG consider the issues related to 3GPP RAN1’s request for a new 802.11 ED?
Some options for IEEE 802.11 WG action (out of Nov plenary?)
  Do nothing
  Leave it to IEEE 802.19 WG
  Ask IEEE 802.11 TGax to consider the request
    And associated issues
  Establish an IEEE 802.11 WG ad hoc to consider the request
    And associated issues
  … others?