## Slide 1: DL MU-MIMO Hybrid BF w/o CSI Feedback for 11ay
Date: 2016-11-xx
Authors:

## Slide 2: Introduction
In [1], DL MU-MIMO scheme and CSI feedback for 802.11ay was introduced.
DL MU-MIMO throughput might be degraded due to CSI feedback overhead.
When AP can form multiple sharp beams, it enables DL MU-MIMO w/o CSI feedback.

## Slide 3: Overall Flow of MU-MIMO[1]
Step 3:
TX-RX Pairing (MID) (combined TXSS + R-RXSS after TX sector reductin)
Step 5:
MU-MIMO Transmission
Step 1:
I-TXSS for TX Sector reduction,
Step 2:
Collect multiple TX sector feedbacks from STAs
RX typically in Omni
Step 4:
Collecting CSI feedbacks from STAs
CSI feedback from STAs
AP
STA
STA
STA

## Slide 4: CSI Feedback in 11ad
CSI can be reported in Channel Measurement Feedback element of BRP frame in 11ad
  Payload size of the frame is calculated as
    MAC Header(28) + FCS(4) + Body(14 + x) = 46 + x [octets]
    x: Channel Measurement Feedback Element size
Element ID
Length
SNR
Channel Measurement
Tap Delay
Sector ID Order
Nmeas
2NtapsNmeas
Ntaps
Nmeas
1
1
Octets
Category
Unprotected DMG Action
Dialog Token
BRP Request field
DMG Beam Refinement element
Channel Measurement Feedback element
1
1
1
4
7
x
Octets
Frame Control
Duration
Address 1
2
2
6
Octets
Address 2
6
Address 3
6
Sequence Control
2
HT Control
4
Frame Body
0-2328
FCS
4
BRP frame
Nmeas: number of measurements
Ntaps: number of taps
CSI

## Slide 5: CSI Feedback Overhead
CSI feedback consumes about 3us ~ 4us per STA when each STA reports SNR & Channel measurement with MCS4 in 11ad
  STF + CEF + Header : 2.5us
  Payload length: 0.4 ~ 1.7us
    Payload size: 46 + x octets
    Channel Measurement Feedback element size(x): 2 + Nmeas + 2Nmeas octets (Nmeas: up to 64) (when Ntaps = 1)
    MCS4 (Single Carrier): data rate is 1152Mbps
Total duration of CSI feedback from all STAs in MU-MIMO operation is estimated as several us or more.
Thus, DL MU-MIMO operation that cause little interference between STAs w/o CSI feedback is preferred.
Element ID
Length
SNR
Channel Measurement
Nmeas
2Nmeas
1
1
Octets
Channel Measurement Feedback element

## Slide 6: DL MU-MIMO w/o CSI
When AP forms broad beams for DL MU-MIMO operation,
  large interference occurs between beams
  CSI is important to mitigate interference
But when AP forms sharp beams for DL MU-MIMO operation,
  large interference does not occur between beams
  CSI feedback (Step4) is not needed
STA
AP
STA
STA
AP
STA
  large interference
  little interference
  MU-MIMO with broad beam
  MU-MIMO with sharp beam

## Slide 7: Conclusions
CSI feedback overhead in DL MU-MIMO operation is evaluated.
When AP forms sharp beams, DL MU-MIMO can be performed w/o CSI feedback.

## Slide 8: STRAW POLL 1
Do you agree to insert the following text into the SFD “11ay supports MU-MIMO BF with or without CSI feedback.“
  Yes
  No
  Abstain

## Slide 9: Reference
[1] IEEE 802.11-16/0405r1, “11ay DL MU-MIMO BF Training and User Selection”