## Slide 1: Verifying 11ax’s PAR by UL MU-MIMO
Date: 2016-10-25
Authors:

## Slide 2: Introduction
Four times throughput gain is promised in the PAR of 802.11ax.
In previous results [1-4], the four times throughput gain is shown in some scenario by using some features in 802.11ax, e.g., OFDMA, spatial reuse.
This presentation is to verify the four times throughput gain by UL MU-MIMO

## Slide 3: Simulation Assumptions
Scenario: Indoor, single BSS
Channel model: Channel-D
Bandwidth: 20MHz @ 5GHz
Antenna number:
  AP: 4 ; non-AP STA: 1
Transmit Power:
    AP: 20dBm ; non-AP STA: 15dBm
Traffic model: full buffer, UL only
Packet size: 1460 bytes
Access protocol:
  802.11ac: EDCA
  802.11ax: Trigger + UL MU-MIMO + MBA (EDCA disabled)
STA position: random (uniform distribution) within a certain BSS range
Simulation variable:
  STA number; BSS Range; Scheduling algorithm
BSS Range

## Slide 4: Simulation Results
STA number | Throughput gain
5 | 4.06
15 | 4.46
50 | 5.1
100 | 6
200 | 7.05
500 | 8.83
Setting:
  BSS range = 10 m
  STA number increases from 5 to 500
  Random scheduling
Conclusion:
  Throughput gain can be more than 4 times
  The gain increases with STA number
Chart: STA Number
| 5 | 15 | 50 | 100 | 200 | 500
802.11ac | 72.3 | 65.8 | 57.55 | 48.77 | 41.5 | 33.1
802.11ax | 293.3 | 293.6 | 293.3 | 292.4 | 292.4 | 292.4

## Slide 5: Simulation Results
Setting:
  STA number = 15
  BSS range increases from 10 to 50
  Random scheduling
BSS Range | Throughput gain
10 | 4.41
20 | 3.35
30 | 1.98
40 | 1.97
50 | 2.77
Conclusion:
  Using random scheduling, 4 times throughput is only achievable when STAs are deployed near to the AP
Chart: BSS Range (m)
| 10 | 20 | 30 | 40 | 50
802.11ax | 293.3 | 211.3 | 118.4 | 83.3 | 60.1
802.11ac | 66.5 | 63 | 59.8 | 42.3 | 21.7

## Slide 6: Simulation Results
Setting:
  STA number = 15,
  BSS range increases from 10 to 50
  Scheduling algorithm:
    Nearest STAs (always schedule the nearest 4 STAs)
    K best STAs (randomly select from the K best STAs, K=8 in this simulation)
BSS Range | Throughput gain (nearest STAs) | Throughput gain (K best STAs)
10 | 4.41 | 4.41
20 | 4.52 | 3.85
30 | 4.46 | 2.9
40 | 4.79 | 3.33
50 | 4.82 | 3.9
Conclusion:
  By improving the scheduling algorithm, 4 times throughput gain is still achievable when the BSS range is becoming larger
Chart: BSS Range (m)
| 10 | 20 | 30 | 40 | 50
802.11ac | 66.5 | 63 | 59.8 | 42.3 | 21.7
802.11ax (nearest STAs scheduling) | 293.5 | 284.8 | 266.8 | 202.8 | 104.7
802.11ax (K best STAs scheduling) | 293.4 | 243 | 173.9 | 141 | 84.7

## Slide 7: Conclusion
Through system level simulation, we demonstrate that 4 times throughput gain can be achieved by using UL MU-MIMO
The denser the STAs are deployed, the more gain is obtained
The throughput gain is more obvious when STAs are deployed closer to the AP
Improving scheduling algorithm can increase the throughput gain

## Slide 8: References
[1] 11-15-1095-10-00ax-ofdma-performance-in-11ax
[2] 11-16-1143-01-00ax-11ax-par-verification
[3] 11-16-1198-03-00ax-preliminary-11ax-par-verification
[4] 11-16-1166-00-00ax-meeting-par-requirements-with-ul-ofdma