## Slide 1: NAV Update Rule Considering UL MU Operation
Date: 2016-11-07
Authors:

## Slide 2: Introduction
The UL MU operation and the CS mechanism during the UL MU operation cause the situation which has not existed in the conventional WLAN.
The proper NAV update rule is required considering the UL MU operation.

## Slide 3: Recap: UL MU Operation [1]
“The UL MU operation allows an AP to solicit simultaneous immediate response frames from one or more non-AP STAs.”
UL MU CS mechanism
  Although an HE STA is solicited by a Trigger frame by an AP, the HE STA may not respond to the Trigger frame.
    “If the CS Required subfield in a Trigger frame is set to 1, the STA shall consider the status of the CCA and the virtual carrier sense (NAV) before UL MU transmission in response to the Trigger frame.”

## Slide 4: Recap: NAV Update Rule [1]
The current intra-BSS NAV update rule
  “A STA shall update the intra-BSS NAV with the duration information indicated by the received frame in a PSDU if and only if all the following conditions are met
    The frame is identified as intra-BSS
    The indicated duration information is greater than the STA’s current intra-BSS NAV value
    The STA is not solicited an immediate response by the PPDU carrying the frame”
Thus, if a STA is solicited an immediate response, the STA does not update the NAV.

## Slide 5: Problem
Unwanted transmission by the STA which has not updated its NAV
  Since STA3 is solicited by a Trigger frame, STA3 does not update its NAV.
  The CCA indicates busy and STA3 does not respond to the Trigger frame.
  STA3 may give an interference to the intra-BSS.
Trigger
Frame
Soliciting immediate responses from STA1, STA2, and STA3
AP
STA1
HE trigger-based PPDU
HE trigger-based PPDU
STA2
STA3
STA3 CS: Busy
HE SU PPDU
transmitted by STA3

## Slide 6: Proposal
In case that a STA is solicited an immediate response, but the STA is not able to respond, the STA shall update its NAV.
Trigger
Frame
Soliciting immediate responses from STA1, STA2, and STA3
AP
STA1
HE trigger-based PPDU
HE trigger-based PPDU
STA2
STA3
STA3 CS: Busy
NAV

## Slide 7: Conclusion
The current NAV update rule needs a modification following the UL MU CS mechanism.
If a STA is not able to respond to the frame soliciting an immediate response from the STA, then the STA shall update its NAV.

## Slide 8: References
[1] Draft P802.11ax D0.5

## Slide 9: Straw Poll
Do you agree to make the change below and include it to the next revision of the TG draft?
(Clause 25.2.2 in page 118 of D0.5)
A STA shall update the intra-BSS NAV with the duration information indicated by the received frame in a PSDU if and only if all the following conditions are met:(#164)
— The frame is identified as intra-BSS according to the rule described in 25.2.1 (Intra-BSS and inter-BSS frame detection)(#164)(#1466)
— The indicated duration information is greater than the STA's current intra-BSS NAV value(#164)
— Either Tthe STA is not solicited an immediate response by the PPDU carrying the frame.(#2905) or the STA is solicited an immediate response by the PPDU carrying the frame but the STA is not able to respond to the frame.
  Y
  N
  A