## Slide 1: Quasi-deterministic Channel Model for a Server Room at 60 GHz
Date: 2016-11
Authors:
Name | Affiliations | Address | Phone | email
Peter Papazian | NIST | Boulder, CO, USA | +1 (303) 497-7078 | peter.papazian@nist.gov
Jae-Kark Choi | NIST | Gaithersburg, MD, USA | +1 (301) 975-6049 | jae-kark.choi@nist.gov
Ruoyu Sun | NIST | Boulder, CO, USA | +1 (303) 497-6698 | ruoyu.sun@nist.gov
Jian Wang | NIST | Gaithersburg, MD, USA | +1 (301) 975-8012 | jian.wang@nist.gov
Jelena Senic | NIST | Boulder, CO, USA | +1 (303) 497-6166 | jelena.senic@nist.gov
Camillo Gentile | NIST | Gaithersburg, MD, USA | +1 (301) 975-3685 | camillo.gentile@nist.gov
Yeh Lo | NIST | Boulder, CO, USA | +1 (303) 497-669 | yeh.lo@nist.gov
Kate Remley | NIST | Boulder, CO, USA | +1 (303) 497-3652 | kate.remley@nist.gov

## Slide 2: Abstract
This document presents the parameters of the Quasi-deterministic (QD) channel model for a server room at 60 GHz, in support of the IEEE 802.11ay data-center usage case. The channel sounder, measurement campaign, and parameter-extraction methods are also presented.

## Slide 3: 60 GHz Channel Sounder
One measurement over all 8 TX antennas x 16 RX antennas takes 262 µs to sweep
Can extract AZ / EL AoD and AZ / EL AoA
60.5 GHz center frequency / 2 GHz bandwidth
TX ARRAY MOUNTED ON TRIPOD
8 antennas, gain = 18.1 dBi, beamwidth = 22.5º
azimuth / elevation field-of-view = 180º / 45º
TX power = 20 dBm
RX ARRAY MOUNTED ON ROBOT
16 antennas, gain = 18.1 dBi, beamwidth = 22.5º
azimuth / elevation field-of-view = 360º / 45º

## Slide 4: Server-room Environment
FLOOR PLAN
(generated through laser-guided robot,
each grid square = 1 m2)
Rx
In support of IEEE 802.11ay data-center usage case 4 (doc. 802.11-2015/0625-03)
Rack heights are 1.96 – 2.0 m
Walls and columns are covered with drywall
Dropped ceiling at 2.56 m height made from acoustic tiles
Dimensions of server room are 18 m x 18 m
IEEE 802.11ay DATA-CENTER USAGE CASE
NOAA SERVER ROOM
(Boulder, CO)
COLUMNS
RACKS

## Slide 5: Measurement Campaign
RX
TX
TX and RX antenna centers aligned at 19 cm above racktop
Single TX location
8 RX locations:
  3 intra-rack (RX1 - RX3) : 4.8 m – 6.1 m
  5 inter-rack (RX4 – RX8) : 6.4 m – 12.5 m
  At each RX position, 8 measurements were taken within λ spacing (5 mm) by moving the RX on a positioner
RX1
RX2
RX3
RX4
RX5
RX6
RX7
RX8
TX
FLOOR PLAN
TX
RX
SIDE VIEW
ANGLE VIEW

## Slide 6: Multipath-component Clustering
For each RX location, the multipath components (MPCs) are extracted
MPCs are indexed according to path loss, delay, and angle (AZ / EL x AoD / AoA)
The MPCs from the 8 measurements are then combined then automatically clustered
Rx
PATH LOSS MPCs
CLUSTERED MPCs
(each cluster shown as separate color)
AZ AoA (deg)
delay (ns)
AZ AoD (deg)
AZ AoD (deg)
AZ AoA (deg)
delay (ns)
AZ AoA (deg)
AZ AoA (deg)
delay (ns)
delay (ns)

## Slide 7: Classification: Ceiling and Racktop Reflections
RX
TX
CEILING REFLECTION
RACKTOP REFLECTION
TX and RX antenna elements are pointed at 0º and 22.5º in elevation so that both of these reflections can be seen
RACKSIDE FRONT VIEW
RACKTOP VIEW
RX

## Slide 8: Classification: Curtain Reflection
RACKTOP VIEW
RX1
RX2
RX3
RX4
RX5
RX6
RX7
RX8
TX
CURTAIN
SUPERCOMPUTER RACK
Air curtain made from conductive material (to concentrate cooling) placed close to supercomputers
Average reflection loss of curtain is 0.1 dB
Creates strong reflections in environment (some examples shown)
FLOOR PLAN
AIR CURTAIN

## Slide 9: Classification: Wall Reflection and Column Reflection
Having AoD information in addition to AoA is very useful when associating measured MPCs to raytraced MPCs
Walls and columns are grouped into the same class because they are both covered with drywall
RX1
RX2
RX3
RX4
RX5
RX6
RX7
RX8
TX
WALL
REFLECTION
COLUMN
REFLECTION
BACKWALL
COLUMN
RX

## Slide 10: Classification: Rackside Reflection
Given that the racks are below the TX-RX heights, specular reflections from racksides do not exist
However clusters of diffuse components from racksides still detectable, even though the average reflection loss is large (15.9 dB)
Often there are multiple clusters from the same rack given the complex side profiles (caged door on front side and open back side with dense cabling) and variety of devices inside
RACKSIDE
FRONT VIEW
RACKSIDE
BACK VIEW
RX1
RX2
RX3
RX4
RX5
RX6
RX7
RX8
TX
FLOOR PLAN

## Slide 11: Reduction of QD* Cluster Parameters
Power (dB)
delay (ns)
cursor
(dominant
component)
diffuse
components
1/
K-factor =
Power (dB)
Angle (deg.)
RMS spread
Cursor reflection loss
Ricean K-factor (pre- / post-cursor)
Power-delay decay constant () (pre- / post-cursor)
Intra-cluster arrival rate (λ) (pre- / post-cursor)
RMS angle spread (AZ / EL x AoA / AoD)
Reflection loss
*“Quasi-deterministic Approach to mmWave Channel Modeling in Non-stationary Environment,” Maltsev, Pudeyev, Karls,
Bolotin, Morozov, Weiler, Peter, Keusgen, Globecom 2014.
pre-cursor
post-cursor

## Slide 12: Summary of Parameter-extraction Steps
  CLUSTERING:
    Measured MPCs at each location are clustered
  2. REDUCTION:
  QD parameters of each cluster are reduced
  CLASSIFICATION:
    Delay, AoA, and AoD of the cluster cursor is compared to raytraced reflections in order to classify reflection type (ceiling, racktop, curtain, wall, column, or rackside)
  4. AGGREGATION:
    Clusters are assigned reflection type associated with their cursor and their statistics aggregated accordingly
Over 40 clusters from 8 RX locations used to aggregate data

## Slide 13: Comprehensive QD Model Parameters
 | Ricean K-factor (dB) |  |  |  | γ, power-delay decay constant (ns) |  |  |  | λ, intra-cluster arrival rate (1/ns) |  |  |  | RMS angle spread** (deg.) |  | Reflection loss (dB) | 
 | pre-cursor |  | post-cursor |  | pre-cursor |  | post-cursor |  | pre-cursor |  | post-cursor |  |  |  |  | 
Reflection Type | µ | σ | µ | σ | µ | σ | µ | σ | µ | σ | µ | σ | µ | σ | µ | σ
Ceiling |  |  | 12.4 | 6.2 |  |  | 0.74 | 0.53 |  |  | 1.93 | 1.96 | 2.5 | 1.6 | 7.6 | 2.6
Racktop* |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.8 | 1.1
Curtain |  |  | 7.3 | 4.4 |  |  | 0.95 | 0.58 |  |  | 1.17 | 0.34 | 3.6 | 1.2 | 0.1 | 1.2
Wall / Column | 8.2 | 6.2 | 7.9 | 3.7 | 0.37 | 0.52 | 0.89 | 0.70 | 2.54 | 1.57 | 1.41 | 1.06 | 3.2 | 1.7 | 7.4 | 1.3
Rackside | 8.5 | 4.6 | 7.8 | 5.3 | 2.50 | 3.51 | 3.33 | 1.97 | 0.75 | 0.64 | 1.05 | 1.11 | 3.7 | 1.4 | 15.9 | 4.3
* Valid only for intra-rack TX-RX configurations
** Average over AZ / EL x AoA / AoD
Only first-order reflections considered in this model
Diffuse components in racktop clusters too few in number to reduce intra-cluster parameters from them (seem to be insignificant)
Power-delay decay constant of rackside clusters significantly larger than other classes due to highly rich scattering environment

## Slide 14: Surveyed Environments
What is the priority for IEEE 802.11ay?
AUDITORIUM
OPEN-SQUARE AREA
LOBBY
LIBRARY