## Slide 1: 3GPP R4 164767 LS on RSSI accuracy test cases
Date: 2016-09-07
Authors:
Notes: July 2007

## Slide 2: Abstract
This document gives background review for 802.11 response to 3GPP R4 164767 LS on RSSI accuracy test cases

## Slide 3: Prior related 3GPP RAN4 IEEE 802.11 activity
RSSI measurements
BeaconRSSI measurements 15/1429r1
  https://mentor.ieee.org/802.11/dcn/15/11-15-1429-01-0000-liaison-response-to-3gpp-r4-156870.docx
Measure RSSI on other frames 15/1430r2
  https://mentor.ieee.org/802.11/dcn/15/11-15-1430-02-0000-liaison-response-to-3gpp-r4-156886.docx

## Slide 4: Text of LS R4-164767
1. Overall Description:
In order to verify E-UTRAN-WLAN measurement reporting delay, RAN4 has agreed two test cases: one for E-UTRAN FDD-WLAN interworking case another one for E-UTRAN TDD-WLAN interworking case [3GPP R4-163519]. These tests will be introduced in 3GPP TS 36.133, Rel-13. The corresponding conformance tests will be defined by RAN5 in their conformance test specifications.
Another set of test cases to define WLAN RSSI measurement accuracy tests were presented for approval in [3GPP R4-163518]. But due to lack of consensus in RAN4, these tests cases were not agreed. However RAN4 recommends that WLAN RSSI accuracy tests are defined in at least IEEE 802.11 specifications.
RAN4 therefore requests IEEE 802.11 WG and WIFI Alliance to specify WLAN RSSI measurement accuracy test cases in their specifications.
2. Actions:
To IEEE 802.11 and WiFi Alliance:
ACTION: RAN4 kindly requests IEEE 802.11 WG and WIFI Alliance to specify WLAN RSSI measurement accuracy test cases in their specifications.
Notes: July 2007

## Slide 5: 3GPP TS References
TS 36.133
9.7.1 WLAN RSSI
NOTE: This measurement is for access network selection and traffic steering between E-UTRAN and WLAN.
The requirements in this clause are valid for terminals supporting this capability.
WLAN RSSI defined in sub-clause 5.1.16 of [4] shall meet the performance requirement defined in [32].
[4] 3GPP TS 36.214: "Evolved Universal Terrestrial Radio Access (E-UTRA); Physical layer; Measurements"
[32] IEEE Standard 802.11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications.
Notes: July 2007

## Slide 6: 3GPP R4-163519 Table A.8.25.1.1-1
Parameter |  | Unit | Value | Comment
Active cell |  |  | Cell 1 | Cell 1 is on E-UTRA RF channel number 1.
Neighbour cell |  |  | Cell 2 (AP) | Cell 2 (WLAN AP) is on WLAN RF channel number 1.
CP length |  |  | Normal | Applicable to cell 1
E-UTRA RF Channel Number |  |  | 1 | One E-UTRA FDD carrier frequency is used.
WLAN Channel Number |  |  | 1 | One WLAN carrier frequency is used.
WLAN measurement quantity |  |  | WLAN RSSI | 
WLAN beacon frame transmission period |  | ms | 102.5 | 
DRX |  |  | OFF | 
W1 | Threshold WLAN RSSI | dBm | -70 | Actual WLAN RSSI threshold for event W1. Needs to take absolute accuracy tolerance in section 9.7.1 into account plus margin.
W3 | Threshold WLAN RSSI | dBm | -65 | Actual WLAN RSSI threshold for event W3. Needs to take absolute accuracy tolerance in section 9.7.1 into account plus margin.
T1 |  | s | 5 | During this time the cell1 shall be known to the UE; but cell2 shall be unknown to the UE.
T2 |  | s | ≤ 40 | UE should report Event W1 for cell2 within 30 s.
T3 |  | s | 3 | UE should report Event W3 for cell2 within 0.5 s.

## Slide 7: 3GPP R4-163519 8.1.2.4.19.2.1
WLAN RSSI measurement configuration |  | TWLAN_RSSI [seconds]
Type of Measurement | Minimum number of APs measured during TWLAN_RSSI | 
Measurement of serving AP | 1 | 0.5
Measurement of known neighbor AP on a single channel | 1 | 5
Measurement of multiple unknown neighbor APs | 3 | 30
The WLAN RSSI measurement accuracy for all measured access points shall be fulfilled according to the accuracy as specified in the sub-clause 9.7.1.
The UE shall be capable of performing WLAN RSSI measurements for certain minimum number of APs during TWLAN_RSSI as defined in table 8.1.2.4.19.2.1-1 provided that the beacon frame of the measured AP is available at the UE at least once every 102.4 ms. The UE physical layer shall be capable of reporting WLAN RSSI measurements to higher layers with the measurement period of TWLAN_RSSI.
8.1.2.4.19.2.1 E-UTRAN FDD – WLAN measurements when no DRX is used

## Slide 8: 3GPP R4-163518 A.9.10.1 E-UTRAN FDD – WLAN RSSI Measurement Accuracy
Parameter | Unit | Cell 1 | Cell 2 (WLAN AP)
WLAN RSSI Note 4 | dBm/20 MHz | N/A | -70
WLAN SNR | dB | N/A | -3.35
Propagation condition | - | AWGN | AWGN
Antenna Configuration | - | 1x2 | -
Timing offset to Cell 1 | ms | - | 3
Note 1: OCNG shall be used such that both cells are fully allocated and a constant total transmitted power spectral density is achieved for all OFDM symbols. Note 2: Interference from other cells and noise sources not specified in the test is assumed to be constant over subcarriers and time and shall be modelled as AWGN of appropriate power for Noc1 to be fulfilled. Note 3: Interference from other cells and noise sources not specified in the test is assumed to be constant over the bandwidth and time and shall be modelled as AWGN of appropriate power for Noc2 to be fulfilled. Note 4: Es/Iot, RSRP, Io and WLAN RSSI have been derived from other parameters for information purposes. They are not settable parameters themselves. Note 5: RSRP minimum requirements are specified assuming independent interference and noise at each receiver antenna port. |  |  | 
Table A.9.10.1.2-1: E-UTRAN FDD-WLAN RSSI measurement accuracy test parameters
A.9.10.2.3 Test Requirements
The WLAN RSSI measurement accuracy shall meet the requirements in clause 9.7.1.

## Slide 9: 802.11.2 Draft Recommended Practice for the Evaluation of 802.11 Wireless Performance
https://mentor.ieee.org/802.11/documents?is_dcn=DCN%2C%20Title%2C%20Author%20or%20Affiliation&is_group=000t
Draft 1.0 was removed from the IEEE store after the project was terminated. Some documents speak to the difficulty of testing spatial modulations in Calibrated Over the Air Tests:
https://mentor.ieee.org/802.11/dcn/07/11-07-2551-05-000t-recommendations-for-comments-on-coat-section.doc
https://mentor.ieee.org/802.11/dcn/07/11-07-2909-00-000t-compromiseotadrafttext.doc

## Slide 10: Recommended Response to LS
Thanks for asking for test specifications
The 802.11 standard specifies performance requirements, but not test cases.
The most recent attempt to specify test cases was for IEEE 802.11.2 Draft Recommended Practice for the Evaluation of 802.11 Wireless Performance, and that started in Sept 2004 and was concluded in June 2008. It failed to raise sufficient interest to do the work and reach approval.