## Slide 1: Privacy Issues in 802.11 Networks
Date: 2016-11-08
Authors:
Name | Affiliations | Address | Phone | email
Mathieu Cunche | Univ. Lyon, INSA Lyon, Inria, CITI |  |  | mathieu.cunche@insa-lyon.fr
Juan Carlos Zuniga | SIGFOX |  |  | j.c.zuniga@ieee.org
Mathy Vanhoef | KU Leuven |  |  | mathy.vanhoef@cs.kuleuven.be
Célestin Matte | Univ. Lyon, INSA Lyon, Inria, CITI |  |  | celestin.matte@insa-lyon.fr

## Slide 2: This presentation in a nutshell
Tracking of 802.11 devices is easy
  There are growing market and population concerns about privacy issues with connected devices
MAC randomization has been proposed to prevent tracking - but it is not enough !
  Other information contained in frames can be used for tracking

## Slide 3: 802.11 and privacy
Many individuals carry a 802.11 enabled device, e.g. smartphone
802.11 station are exposed to passive tracking
  Unique identifier: MAC address
  Available in clear-text in every frame
Active service discovery
  Probe requests broadcast by unassociated stations
  Up to 3/min [1]

## Slide 4: Physical tracking using 802.11
Rise of physical tracking systems based on 802.11
  Set of monitoring nodes collecting identifiers
  Applications of physical tracking :
      Physical analytics (frequency and duration of visits)
      Road monitoring (travel time estimation)
      Surveillance
Growing concern of civil society
  FTC – Nomi (US)1, CNIL – JCDecaux (France)2
Problem known since mid 2000's [2][3] but not addressed until now ...
1. https://www.ftc.gov/news-events/press-releases/2015/04/retail-tracking-firm-settles-ftc-charges-it-misled-consumers
2. http://marketinglaw.osborneclarke.com/advertising-regulation/jc-decauxs-pedestrian-tracking-system-blocked-by-french-data-regulator/

## Slide 5: MAC address Randomization (theory)
MAC address Randomization in WLAN [3]:
  Periodically change the MAC address to a random value (pseudonym)
Potential problems with random MAC
  MAC address is supposed to be globally unique
  Risk of identifier collision
  May disrupt other services/protocols
OK for service discovery mode
  Collisions will have little impact
  No other services/protocols
Possibly difficult for associated stations
  Collisions are rare but problematic
  Changing MAC address require to re-auth
  Might exhaust resources (DHCP)

## Slide 6: MAC Address Randomization (practice)
MAC address randomization adopted by the industry
  iOS1, Android2, Linux3, Windows 104
  Random MAC only used in probe requests
    Except for Windows 10
Field experiments at IETF for associated mode [5]
Ad-hoc implementation since no specification
1 B. Misra. iOS 8 MAC randomization – analyzed! http://blog.airtightnetworks.com/ios8-mac- randomization-analyzed/
2 Android 6.0 changes. Retrieved from https://developer.android.com/about/versions/
marshmallow/android-6.0-changes.html, 2015.
3 E. Grumbach. iwlwifi: mvm: support random MAC address for scanning. Linux commit effd05ac479b.
4 W. Wang. Wireless networking in Windows 10. In Windows Hardware Engineering ommunity
conference (WinHEC), Mar. 2015.

## Slide 7: Attacker model
Capabilities : passive monitoring of 802.11 channels
  Active attacks are possible
Objective: track individuals over time
  Group together frames with distinct MAC address pseudonym but belonging to the same device
  Using frame contents and timing

## Slide 8: Other means to track 802.11 devices
Content-based attacks
  Information Elements
  WPS UUID
  Predictable fields
    Sequence number
    Scrambler seed
Active attacks
  Fake AP (Karma attack)
  Hotspot2.0
Timing attacks

## Slide 9: Results from academic research
“Why MAC Address Randomization is Not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms” [5]
“How talkative is your mobile device?: an experimental study of Wi-Fi probe requests“ [1]
“The scrambler attack: A robust physical layer attack on location privacy in vehicular networks” [9]
“Defeating MAC Address Randomization Through Timing Attacks Timing attacks” [10]

## Slide 10: Information Elements (IEs)
Information Elements (Tags or Tagged parameters)
  Embedded in 802.11 frames
  Not mandatory
  Used to advertise support of functionalities
  Ex: Supported Rates, High Throughput capabilities …
Study of IE in the wild [5]
  Analysis of IE found in 3 datasets (160 000+ devices)
IE based fingerprinting
  Large number of IE embedded in frames
  IEs with multiple parameters
  IEs provide enough entropy to uniquely identify a device within a large group
160 000

## Slide 11: Information Elements (IEs)
HT Capabilities information element
160 000

## Slide 12: Information Elements (IEs)
Identifying information provided by IE in considered datasets
160 000

## Slide 13: Information Elements : WPS UUID
WPS Information Element
  WPS (Wi-Fi Protected Setup) protocol simplifies device pairing
  WPS compatible devices can include a WPS IE
  WPS IE includes a UUID field
Tracking threat of WPS UUID [5]
  UUID is by definition a unique identifier: can be used for tracking
  UUID is computed by hashing the MAC address [6]
    Can be reversed back to the real MAC address
    Brute-force attack led to successful reversing in 92% of cases

## Slide 14: Predictable fields
Predictable field : non constant field whose value can be predicted from the previous frames
  Example : sequence number field
    Frame counter included in 802.11 header
    Predictable : simple increment
Sequence number field in iOS random MAC
  Counter not reset upon MAC address change [1]
  Can be used to defeat MAC randomization
Source: J. Freudiger

## Slide 15: Predictable fields: scrambler seed
802.11 PHY Scrambler seed [7]
  Embedded in OFDM frames
  Seed used to initialize PRNG generating the scrambling sequence
  No specification on how to generate the seed sequence
    “the initial state of the scrambler shall be set to a pseudorandom nonzero state” (18.3.5.5)

## Slide 16: Predictable fields: scrambler seed (cont’d)
Collecting scrambler seeds
  Part of the PHY layer: not available at the MAC layer
  Standard hardware not helpful here
  Solution: use Software Defined Radio
    Implementation of 802.11 based on Gnuradio + USRP + Faraday Room
Inria FIT CortexLab

## Slide 17: Predictable fields: scrambler seed (cont'd)
The scrambler seed : a predictable field
  Observed patterns in real world implementations [9][5]
    Freewheeling : state of the LFSR at the end of a frame is reused for the next frame
    Constant seed (or limited to a small set)
    Incremental: seed value is incremented by one at each frame
  Scrambler seeds can be used to track 802.11 transmitters

## Slide 18: Active attacks
Karma attack [5]
  Stations switch back when their real MAC address when attempting to associate with the AP
  Attack : Create a fake AP with popular SSID
    Collect real MAC address of STA attempting to associate
Hotspot 2.0 based attack [5]
  HS2.0 (802.11u)[8]: protocol allowing roaming
    STA sends ANQP queries to AP to retrieve list of available services
    STA switches back to their real MAC address when querying
    Query also contains predictable counter that might help tracking
  Attack : create AP advertising HS2.0 capabilities
    Collect real MAC address of querying STAs

## Slide 19: Timing attacks
Timing in active service discovery
  Probe sent at regular interval
Timing features of probe requests
  Interval between probe requests within a burst
  Interval between bursts
Observed timing of probe requests can be used for tracking [10]
Channel order could also be exploited [11]

## Slide 20: Summary
MAC randomization is a good protection against privacy issues but can currently be defeated by advanced attacks
  Presented list of attacks is not exhaustive
Other privacy issues in 802.11 specifications
  Identifying implementation-specific usage of multiple optional parameters in frames
  Identifying implementation-specific generation of (pseudo-)random parameters
  Correlating state changes of different parameters between themselves, and/or with incremental counters
Too much freedom in specification can lead to implementation fingerprinting, which opens up privacy and security issues

## Slide 21: Further thoughts
How often should identifiers be changed (frequency)?
Should we provide recommendation on how to generate (pseudo-)random parameters? e.g.
  MAC address,
  scrambler seeds,
  Unlinkability of consecutive values

## Slide 22: Straw Poll
Do you think 802.11 specifications should include privacy recommendations about the usage of its protocols and parameters?
  Y:
  N:
  A:

## Slide 23: References
[1]J. Freudiger, “How talkative is your mobile device?: an experimental study of Wi-Fi probe requests,” in Proceedings of the 8th ACM Conference on Security & Privacy in Wireless and Mobile Networks, 2015, p. 8.
[2]J. Pang, B. Greenstein, R. Gummadi, S. Seshan, and D. Wetherall, “802.11 User Fingerprinting,” in Proceedings of the 13th Annual ACM International Conference on Mobile Computing and Networking, New York, NY, USA, 2007, pp. 99–110.
[3]M. Gruteser and D. Grunwald, “Enhancing location privacy in wireless LAN through disposable interface identifiers: a quantitative analysis,” Mobile Networks and Applications, vol. 10, no. 3, pp. 315–325, 2005.
[4] C. J. Bernardos, J. C. Zúńiga, and P. O’Hanlon, “Wi-Fi internet connectivity and privacy: Hiding your tracks on the wireless Internet,” in 2015 IEEE Conference on Standards for Communications and Networking (CSCN), 2015, pp. 193–198.

## Slide 24: References
[5]M. Vanhoef, C. Matte, M. Cunche, L. S. Cardoso, and F. Piessens, “Why MAC Address Randomization is Not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms,” in Proceedings of the 11th ACM on Asia Conference on Computer and Communications Security, New York, NY, USA, 2016, pp. 413–424.
[6]P. Leach, M. Mealling, and R. Salz. A universally unique identifier (UUID) URN namespace. RFC 4122 (Proposed Standard), July 2005.
[7]IEEE Std 802.11-2012. Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, 2012.
[8] IEEE Std 802.11u. Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications: Amendment 9: Interworking with External Networks, 2011.

## Slide 25: References
[9]B. Bloessl, C. Sommer, F. Dressier, and D. Eckhoff, “The scrambler attack: A robust physical layer attack on location privacy in vehicular networks,” in 2015 International Conference on Computing, Networking and Communications (ICNC), 2015, pp. 395–400.
[10]C. Matte, M. Cunche, F. Rousseau, and M. Vanhoef, “Defeating MAC Address Randomization Through Timing Attacks,” in Proceedings of the 9th ACM Conference on Security & Privacy in Wireless and Mobile Networks, New York, NY, USA, 2016, pp. 15–20.
[11]O. Waltari and J. Kangasharju, “The Wireless Shark: Identifying WiFi Devices Based on Probe Fingerprints,” in Proceedings of the First Workshop on Mobile Data, New York, NY, USA, 2016, pp. 1–6.

## Slide 26: Backup

## Slide 27: Datasets
Datasets of probe requests