## Slide 1: An unified 802.11az Protocol
Date: 2016-11-08
Authors:
Nov 2016

## Slide 2: Motivation
Propose a mechanism that allows for a STA to
  Scan the environment to assess the ranging capabilities of responders within range,
  Select a protocol that best fits the capabilities of the responders within range and the requirements of the application(s) executing in the STA,
  Select a subset of the responders within range and negotiate parameters to use for ranging with each of the responders, and
  Perform corresponding ranging protocol with each of the responders in the selected subset in order to triangulate the STA’s position.
Nov 2016

## Slide 3: Terminology
  Capabilities
    FTM Responder – the device can play the role of a responder for all supported ranging protocols – indicated by setting bit-70 of the Extended Capabilities element
    FTM Initiator – the device can play the role of an initiator for all supported ranging protocols – indicated by setting bit-71 of the Extended Capabilities element
  Ranging Protocols – Time of Flight (ToF) measurement; may be extended for others (needs more discussion)
    REVmc D8.0 Fine Timing Measurement Prototocol (FTM)
    VHT NDP Sounding-based .11az protocol (VHTz)
    HEW NDP Sounding-based .11az protocol (HEWz)
Nov 2016

## Slide 4: Determining Ranging Capabilities
Passive Scanning
  Listen to beacons from responders within range and discover ranging capabilities from the Extended Capabilities element
Active Scanning
  Send a wildcard addressed Probe Request and discover ranging capabilities from the Extended Capabilities element in the received Probe Responses
Others
  Via Neighbor Reports
  Out-of-band techniques
Nov 2016

## Slide 5: Extended Capabilities Element
 |  |  |  | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 |  |  |  | 
 |  |  |  |  |  |  | R |  |  | R | R | R | R | R | R | R | R | R | R |  |  |  | 
FTM Responder
FTM Initiator
Use the FTM Responder and FTM Initiator bits to indicator corresponding capability for any (FTM, VHTz, HEWz, etc.) Ranging protocol.
Add a new bit to the Extended Capabilities element to indicate .11az capability (.11az Capability)
  .11az Capability = 1 && FTM Responder == 1 .11az Responder
  .11az Capability = 1 && FTM Initiator == 1 .11az Initiator
Need more discussion on the possibility of adding more bits to the Extended Capabilities element and if that would render the protocol more optimal
Nov 2016

## Slide 6: Discovering Ranging Capabilities
Discovery:
  Listen to Beacons
  Send wildcard addresses Probe Request and listen to corresponding Probe Responses
  Send unicast Probe Requests and listen to corresponding Probe Responses
  Others
The STAs need to know the ranging capabilities of the APs
The APs need not explicitly determine the STAs Measurement phase protocol capabilities but learns of it implicitly when the STA sends an initial FTM Request to the AP
PASSIVE
ACTIVE
Nov 2016

## Slide 7: Negotiation
From among the discovered Responders, the STA selects a subset (Rn) for negotiation
To each of the member of Rn, the STA sends an initial FTM request (iFTMR) which includes:
  A FTM Parameters element as described in REVmc D8.0 which is a set of parameters that the STA proposes to use if it executes the FTM ranging protocol with the corresponding responder, and optionally
  A VHTz Parameters element which is a set of parameters that the STA proposes to use if it executes the VHTz ranging protocol with the corresponding responder, and optionally
  A HEWz Parameters element which is a set of parameters that the STA proposes to use if it executes the HEWz ranging protocol with the corresponding responder.
Nov 2016

## Slide 8: Negotiation (cont’d)
The initiator indicates one of the following:
  No preference for the ranging protocol (the responder selects one based on its current operating conditions)
  A preferred ranging protocol (the responder may select a different ranging protocol if it has no resources to support the preferred one)
The responder
  Chooses one of the ranging protocols and responds with the corresponding {FTM, VHTz, HEWz} parameters element in the initial FTM (in response to the initial FTM request), or
  Rejects the initial FTM request and optionally includes {FTM. VHTz and/or HEWz} parameters element indicating the parameter set that it can potentially support, if requested
Nov 2016

## Slide 9: Initial FTM Request/Initial FTM Exchange
 | Category | Public Action | Trigger+ Preference | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) | VHTz Parameters (optional) | HEW Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11 | <tbd> | <tbd>
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16
Nov 2016

## Slide 10: REVmc D8.0 FTM Parameters Element
 | Status Indication | Value | Reserved (0) | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved (00) | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16
Nov 2016

## Slide 11: VHTz Parameters Element (TBD)
 | Status Indication | To be defined | Reserved (0) | To be defoned |  | 
Bits | 2 | 5 | 1 | 32 |  | 
 | To be defined |  |  |  | Reserved (01) | To be defined
bits | 8 |  |  |  | 2 | 22
 | Status Indication | Value |  | To be defined
Bits | 2 | 5 |  | 
 | To be defined |  |  | 
bits |  |  |  | 
Nov 2016

## Slide 12: HEWz FTM Parameters Element (TBD) (clone details from a .11ax Negotiation Protocol that the group agrees on)
 | Status Indication | Value | To be defined
Bits | 2 | 5 | 
 | To be defined |  | 
bits |  |  | 
Nov 2016

## Slide 13: Status and Value fields (from REVmc D8.0)
Status: 2 bits
  0: Reserved
  1: Successful
  2: Incapable forever
  3: Incapable for the duration in Value field
Value: 6 bits
  Valid only when the Status field is set to 3
Nov 2016

## Slide 14: .11az Negotiation
Initial FTM Request (the inclusion of FTM Parameters element is mandatory in this frame)
    VHTz Parameters element -- .11az will define the contents of VHTz Parameters element
    HEWz Parameters element -- .11az defines the contents of HEWz Parameters element
    Etc.
The Trigger + Preference field
  Trigger set to 1
  Preference set to 0 (indicates no preference) or a value indicating the preferred Ranging Protocol
Initial FTM frame includes one of FTM, VHTz or HEWz Parameters element
  Optionality of FTM Parameters element is new in .11az
Use this exchange to pick a protocol to be used for Ranging
  In a different submission
Nov 2016

## Slide 15: .11az Negotiation
Performed with one of more members of the subset Rn
Initial FTM Request contains:
  Trigger+Preference field describing the preferred ranging protocol
  FTM [, VHTz, HEWz] Parameters element contain proposed parameters to execute FTM and [VHTz, HEWz] Ranging protocols
Initial FTM frame contains
  Responder’s LCI, location civic and/or Neighbor List
  A Neighbor List from the Responder’s perspective
  {FTM, VHTz, HEWz} Parameters to execute the Ranging protocol chosen by the responder
    This behavior is different from the legacy FTM behavior
Nov 2016

## Slide 16: Ranging
Once the negotiation is complete, the subset Rn is partitioned into
  A Rr which contains the set of peers with which the negotiation was successful – both the ends agreed on a set of parameters to use fot ranging
  Rn – Rr which contains the set of peers with which the negotiation failed
the range measurement protocol is executed with one of more members of the subset Rr using the parameters negotiation in the initial FTM request/initial FTM exchange
  Details in a separate submission
Nov 2016

## Slide 17: How does all this work? -- an example
STA discovers ranging capability of the environment (R)
  STA listens to Beacons from a set of Responders
  STA selects a subset (Rn) based on the ranging capabilities supported by each of the Responders
STA initiates Negotiation with one or more members of the set Rn
  Negotiation successfully completes with Rr (a subset of Rn)
STA executes the negotiated Ranging protocol with one or more members of Rr.
Rr ⊆ Rn ⊆ R
Nov 2016

## Slide 18: Motion
Move to approve
  the proposed 802.11az protocol (as exemplified in slide-17) and
  develop corresponding FRD/SFD text for future discussion and approval
Moved: Ganesh Venkatesan
Seconded: Manish Kumar
Yes: 8
No: 4
Abstain: 8
Motion fails
Nov 2016

## Slide 19: The intent of the failed motion …
Agree on a .11az protocol that involves discovery, negotiation and range measurement
Allow for optimizations to skip or add new steps, as needed
Extend REVmc D8.0 iFTMR/iFTM to define the negotiation step
  How to extend is open for discussion
Develop SFD content. review/improve and approve for inclusion in the SFD document
Nov 2016

## Slide 20: Motion
Move to approve inclusion of the following in the 802.11ax Spec Framework Document (SFD); and instruct the SFD Editor to incorporate it in the next version of the 802.11az SFD and grant the SFD editor editorial license:
  The .11az protocol shall define the following phases
    a capability discovery,
    a Time of Flight (ToF) measurement parameter negotiation and
    a set of ToF measurement exchanges
  Note: Other protocol phases may be defined as needed and is <TBD> based on more discussion(s)
  The .11az protocol shall extend the REVmc iFTMR/iFTM for .11az ToF measurement parameter negotiation
Moved: Ganesh Venkatesan Seconded: Santosh Pandey
Yes: 9 No: 0 Abstain: 8
Result: Motion Passes
Nov 2016