## Slide 1: FTM Frame Exchange Authentication
Date: 2016-11-08
Authors:

## Slide 2: Background
The need for security in FTM protocol:
Prior contributions to 11az emphasized the need for Security for FTM frame exchange
Proposals addressed the solution for the case when the devices are Associated
    11-16-1256r1 Functional requirement for secure ranging
    11-16-1020r0 Security Enhancement to FTM
Discussion focused on the need for a common solution for both Associated and un-associated case

## Slide 3: Need for both FTM Frame, ACK Authentication
It is possible that the Responder STA can be impersonated in the example here:
Responding STA: User with Mobile Device
Car: Requesting STA
Car is computing the Range with the User
Once the FTM Request and Response sequence is done, a snooping device can send the FTM Frame 1 and the Car after receiving measurements from FTM Frame 2 can assume the user is near by and can accidentally open the car
Solution: Authenticate the FTM Frame as well
There will be signaling in FTM Request Frame to allow for: Authenticate Responder, Requester, or both
User With Mobile Device
Car
FTM Request
ACK
FTM Response
ACK
FTM Frame_1
ACK (Authenticated)
FTM Frame_2
ACK (Autheticated)
FTM Frame_3
ACK (Authenticated)
FTM Frame_4
ACK (Authenticated)
Requesting STA
Responding STA

## Slide 4: Straw Poll
Need for authenticating FTM Responder
  Yes
  No
  Abstain

## Slide 5: Outline of the Solution 1/2
Requesting STA
Responding STA
FTM Request
ACK
FTM Response
ACK
FTM Frame_1: Encrypt ToA/ToD fields or use content from FTM Response
ACK (FTM Response)
FTM Frame_2
ACK (FTM Frame_1)
FTM Frame_3
ACK (FTM Frame _2)
FTM Frame_4
ACK (FTM Frame _3)
Set up Security Key
Setup Security Key: Diffie Hellman
FTM Request frame: Diffie Hellman Group (prime numbers), and also the Public Key from Requesting STA
FTM Response frame: Includes the Public Key from Responding STA
Both Requesting and Responding STA generate shared-secret Key from the Shared Public key from the Peer and the Diffie Hellman Group

## Slide 6: Outline of the Solution 2/2
Requesting STA
Responding STA
FTM Request
ACK
FTM Response
ACK
FTM Frame_1: Encrypt ToA/ToD fields or use content from FTM Response
ACK (FTM Response)
FTM Frame_2
ACK (FTM Frame_1)
FTM Frame_3
ACK (FTM Frame _2)
FTM Frame_4
ACK (FTM Frame _3)
Set up Security Key
Using the Shared-secret key:
Authenticating FTM Frame:
  Encrypt ToA, ToD fields with shared key (or) Generate an Authentication code based on the content of the last successfully frame transmitted by Responding STA (Content + Key = Authentication code)
Authenticating ACK Frame:
  The Shared-secret key is used to generate the Authentication code to be included in the ACK frame and verified at the Responding STA
  ACK frame carries Authentication Information based on the content of the previous FTM frame received + Security Key

## Slide 7: Protocol Usage for FTM Burst 1/2
Requesting STA sends Trigger frame to initiate FTM Burst
  ACK to the FTM Trigger frame from FTM Initiator is not Authenticated
After the Trigger frame, Responding STA transmits FTM frame which is Acknowledged by Requesting STA
The Authenticity of FTM frame when not encrypting ToA and ToD fields:
  Authentication code is generated based on last successfully transmitted frame from by the Responding STA to Initiator STA.
    FTM Frame_1: Content of FTM Response Frame + Key
    FTM Frame_2: Content of FTM Frame_1 + Key
When encrypting ToA and ToD fields:
  the first FTM frame (measurement frame) does not carry any valid ToA, ToD values, so
    First FTM frame is not Authenticated
    the measurements made during the transmission of the frame are sent in the following FTM frame which is authenticated
  The initiator determines that the Responder is authentic if the ToA, ToD values yield a RTT value with in certain boundaries
Requesting STA
Responding STA
FTM Request
ACK
FTM Response
ACK
FTM Frame_1
ACK (FTM Trigger frame)
FTM Frame_2
ACK (FTM Frame_1)
FTM Frame_3
ACK (FTM Frame _2)
FTM Frame_4
ACK (FTM Frame _3)
FTM Trigger
ACK

## Slide 8: Straw Poll
Authenticating FTM frame:
  Encrypting ToA and ToD Fields
  Adding an Authentication code as shown in earlier slide
  No option

## Slide 9: Protocol Usage for FTM Burst 2/2
The Authenticity of ACK frame
  ACK to First FTM frame after Trigger frame is computed based on the content of the FTM Trigger frame + Key
  ACK to subsequent FTM frames, use the content of the previous FTM frames i.e., ACK to FTM Frame_n use the content of FTM Frame_n-1 + Key
Requesting STA
Responding STA
FTM Request
ACK
FTM Response
ACK
FTM Frame_1
ACK (FTM Trigger frame)
FTM Frame_2
ACK (FTM Frame_1)
FTM Frame_3
ACK (FTM Frame _2)
FTM Frame_4
ACK (FTM Frame _3)
FTM Trigger
ACK

## Slide 10: Straw Poll
Authenticating ACK frame behavior as proposed in previous slide i.e., include Authentication code in ACK frame based on the content on the previously successfully received FTM frame
  Yes
  No
  Abstain

## Slide 11: Error Scenario
Requesting STA
Responding STA
FTM Request
ACK
FTM Response
ACK
FTM Frame_1
ACK (FTM Response)
FTM Frame_2
ACK (FTM Response/FTM Frame_1)
FTM Frame_3
ACK (FTM Frame _2)
FTM Frame_4
ACK (FTM Frame _3)
X
X
Loss of frame can be:
FTM Frame which would mean: missing FTM frame at Requesting STA and a missing ACK frame at Responding STA
ACK frame which would mean: missing ACK frame at Responding STA
Loss is detected in all cases by Responding STA
The responding STA today transmits the next FTM frame with the same values in ToA, ToD, Dialog Token field (as the last FTM frame)
On the same lines, the responding STA ignores the measurement on the first successful exchange after loss of frame and the measurement continues from there on.
  In the Figure, Responding STA will not make measurements on FTM Frame_2, and it will make measurements on the second successfully transmitted frame after the lost frame (in the adjacent Figure it would be FTM Frame_3)

## Slide 12: Straw Poll
Support for error scenarios behavior as proposed in previous slide i.e., take measurements on the second successfully transmitted FTM frame after the frame (or sequence of frames in error)
  Yes
  No
  Abstain

## Slide 13: Encoding of Authentication Content
FTM Request/Response: Separate IE to signal Diffie Hellman Parameters and security setup for the FTM Session
FTM Frame Authentication: Possible options
  Encrypt ToA/ToD fields with Shared-secret: The difference in the RTT estimates from one measurement to the other will help the requesting STA determine that the Responding STA is the wrong STA
  Carry the Authentication code in FTM frame: New field
ACK Frame Authentication:
  Carry the Authentication code in RA field

## Slide 14: Authenticating the Responder
Requesting STA
Responding STA
FTM Request
ACK
FTM Response
ACK
FTM Frame_1: Encrypt ToA/ToD fields or use content from FTM Response
ACK (FTM Response)
FTM Frame_2
ACK (FTM Frame_1)
FTM Frame_3
ACK (FTM Frame _2)
FTM Frame_4
ACK (FTM Frame _3)
Set up Security Key
This Exchange is not Authenticated

## Slide 15: Authenticating During FTM Setup
Man in the middle attack: Potentially man in the middle can respond to FTM Request and hence the STA is communicating with the wrong end device
Solution: Applicable to both Associated and Un-associated STAs
    If the STA was associated earlier with the AP, derive an PMK key from the earlier association and use it to
      Authenticate the Responder
      Encrypt the public key (DH Public Key) with preconfigured key (i.e. PMK) and sent out over-the-air while receiver decrypts to get the actual public key for deriving the shared secret
    Out of band key established: If both Responder and Requester have established a key out-of-band, the key is used to authenticate the Responder
    Third party public key verification technique: the given public key is sent out in clear and peer can validate via third party
    Authenticating Responder STA:
    FTM Response includes an Authentication Code based on the PMK Key / Key established out-of-band and the Content of FTM Request frame (Ex: CRC …etc)
      Requesting STA will match the Authenticating Code to determine the validity of the Responder STA

## Slide 16: Straw Poll
Add a 11az SFD requirement to support Security in FTM protocol to support both Associated and Un-Associated STAs