## Slide 1: Additional requirements for 11ay for supporting 60GHz high resolution location
Date: 2016-November-08
Authors:
Name | Company | Email
Alecsander Eitan | Qualcomm | eitana@qti.qualcomm.com
Assaf Kasher | Qualcomm | akasher@qti.qualcomm.com

## Slide 2: General
We want to support the following protocols/scenarios in 60GHz:
  Single AP positioning using both AOA and range.
  Provide orientation angle to the mobile device.
  Multiple AP (2 and more) AP positioning using range and AOA.
  3 or more APs using range measurement only.
We would like to define the 11ay (11ad) list of features required to support 11az (high resolution location)

## Slide 3: What is needed – simple changes (#1)
Change the FTM protocol to enable measuring T1 and T2 in reference to the end of the packet
  May be done in 11ay
  May need PHY changes to be effective
    Require last TRN field or last CE field to use message BF (AWV)
    Adding a CE field at the end of TRN fields.

## Slide 4: What is needed – simple changes (#2)
Extend the FTM protocol and messages to support AOA (and AOD) measurement
  In 60GHz AOA (and AOD) can be done by adding BRP training fields (TRN fields) to FTM packets. (11ad already supports any PHY frame to include TRN fields for beam tracking purposes)
  AP AOA is mainly for STA location
  STA AOA is mainly for orientation (of the STA)
  AOD is less preferred relative to AOA since it is more complex, time consuming and dependent on both stations accuracy.

## Slide 5: What is needed – simple changes (#3)
Add AOA (and AOD) request negotiation and report to FTM frames
  In global coordinates or device coordinates
  Each should have an accuracy estimate
Add LOS/NLOS likelihood estimate to FTM frames
  Add field for LOS/NLOS likelihood estimation
  An estimate of whether set of measurements has been performed on a LOS link

## Slide 6: What is needed – simple changes (#4)
Accurate Timed TXSS
  Transmit the TX Sector Sweep packets at accurate times, to enable LOS sector selection at receiving STAs
Support for non-associated FTM in 60GHz
  Need to resolve non-associated beamforming training to enable the FTM messaging.
  Enable switching to another channel for un-associated FTM measurements.

## Slide 7: Advanced procedures
Passive location in 60GHz Different and more challenging than sub-6GHz passive location due to the directional nature of transmissions.
  AOD based
  AOA based
  DTOA based
Inter-band cooperation
  Use sub 6GHz bands to coordinate between a 60GHz device and a 60GHz AP.
  Publish existence of 60GHz location services at a specific location
  Synchronize between devices.

## Slide 8: Summary
This presentation details several suggested changes to the 11ay/11ad specifications to facilitate high resolution location.
  Extend FTM protocol to support AOA (and AOD) measurements.
  Improve existing 11ad/11ay TXSS, RXSS, BRP and TRNs to allow LOS sectors selection and more accurate measurements.
  Extend 11ay/11ad to facilitate non-associated FTM on same channel and other channels.