## Slide 1: Group-addressed GAS
December 2016
Michael Montemurro, BlackBerry
Slide <number>
Date: 2016-12-15
Authors:
Notes: doc.: IEEE 802.11-13/0788r1
July 2013
        Stephen McCann, Blackberry
Page <number>

## Slide 2: Abstract
December 2016
Michael Montemurro, BlackBerry
Slide <number>
Discussion slides for adding group-addressed GAS for PAD
Notes: doc.: IEEE 802.11-13/0788r1
July 2013
        Stephen McCann, Blackberry
Page <number>

## Slide 3: Network Selection Procedures
General process is: Scan/Discover; Select; Connect
The WLAN connection manager performs complex calculations to determine the most preferred network.
  It may take many criteria into account:
    User preferences
    Radio link conditions (e.g. signal quality)
    Application/Service requirements (e.g. local vs remote, Wi-Fi Direct)
    Radio co-existence condition (e.g. Bluetooth, LTE, Radar)
    Location
    Power (e.g. battery level)
    History
Network Selection can be a time critical process.
What triggers a connection manager to re-select a different network?
  Disconnection?, Application/Service?, User Action?, Change in Radio/Application conditions?
December 2016
Michael Montemurro, BlackBerry
Slide <number>

## Slide 4: Service Discovery and Network Discovery
Service discovery could be done in two ways:
Service Invocation/Notification:
  Device performs Service Discovery (based on services “available” in the OS) with Service Discovery procedures.
  Device connects, associates and invokes the services or notifies the OS that services are available.
  Network prioritization takes precedence
Service selection:
  Application/Service running on the device triggers query for services as part of network discovery.
  Network prioritization may be taken into account but is secondary
  How does this work if there are multiple services?
December 2016
Michael Montemurro, BlackBerry
Slide <number>

## Slide 5: STA/AP Requirements
Improve the medium utilization for pre-association service discovery.
Decrease the response time and overhead on the STA and AP in generating and processing service discovery requests/response
December 2016
Michael Montemurro, BlackBerry
Slide <number>

## Slide 6: Proposed Solution Overview
Modify GAS procedures to enable a group-addressed GAS (GA-GAS) request and response frames.
A STA could send a GA-GAS Request
An AP would reply with either a unicast GAS Response or a GA-GAS Response, depending on specific conditions that the AP determines.
December 2016
Michael Montemurro, BlackBerry
Slide <number>

## Slide 7: Proposed Solution – GA-GAS Request
Modify GAS procedures to allow transmission of a GA-GAS Request frame
  Need to determine conditions under which it could be transmitted.
  Restrict transmissions to the case where they are only used when GA-GAS APs are in range?
Restrict GA-GAS procedures to permit only PAD ANQP Requests? (at this time)
Modify GAS Procedures to permit the behavior where an AP only responds to a GAS request when it has a reply. (restrict this to PAD ANQP as well at this time)
December 2016
Michael Montemurro, BlackBerry
Slide <number>

## Slide 8: Proposed Solution – GA-GAS Response
Modify GAS procedures to enable a group-addressed GAS (GA-GAS) response frame. This is time-limited
Add a element that the AP will use to advertise GA-GAS responses (includes enable/disable, schedule information) in Beacons and Probe Response frames.
AP behavior:
  AP monitors PAD requests from STAs
  AP detects that PAD requests (for the same service query) reception frequency exceeds threshold.
  AP enables group-addressed PAD responses (for a period of time (s) at an interval of TUs.
STA behavior:
  STA monitors AP Beacon/Probe Response; if group-addressed PAD responses are enabled; STA listens for GA-GAS PAD responses in addition to regular GAS responses
December 2016
Michael Montemurro, BlackBerry
Slide <number>