## Slide 1: Rate 7/8 (1344,1176) LDPC code
Date: 2017-07-13
Authors:

## Slide 2: Background
Longer LDPC codes with codeword length N=1344 (denoted as 1344-LDPC) for rates 1/2, 5/8, 3/4, and 13/16 [1] have been included in Draft P802.11ay_D0.3 [2]. Performance evaluation shows that for a given code rate, a longer code has ~1dB gain compared to the corresponding short code of length 672 (denoted as 672-LDPC) of the same rates [1].
A short code of length 624 for rate 7/8 obtained by puncturing 11ad 13/16 672-LDPC is adopted in 802.11REVmc [3]. The punctured code is introduced for implementation without changing the core of decoder at a receiver. However, the punctured code has different codeword length as other 11ad codes resulting in impacts on the coding efficiency and the implementation in both transmitter and receiver.
Another short code of length 672 for rate 7/8 is proposed [4] and has been included in D0.3 [2].
Following the same methodology as the short code, the rate 7/8 punctured long LDPC code is proposed [1]. However, the codeword length of this punctured code is N=1248 (denoted as 1248-LDPC), which is different from all other long codes for 11ay.
This contribution is to introduce a rate 7/8 1344-LDPC code with design by taking into account performance and implementation in decoding, padding and blocking.

## Slide 3: Outline
Review of long code proposed in [1]
Discussion of the blocking issue with different codeword lengths
Performance comparison
Discussion of decoding complexity
Summary

## Slide 4: Rate 13/16 LDPC codes in 11ad and for 11ay
Rate 13/16 672-LDPC code in 11ad [7] (matrix H 126 x 672, Z = 42)
29 | 30 | 0 | 8 | 33 | 22 | 17 | 4 | 27 | 28 | 20 | 27 | 24 | 23 |  | 
37 | 31 | 18 | 23 | 11 | 21 | 6 | 20 | 32 | 9 | 12 | 29 | 10 | 0 | 13 | 
25 | 22 | 4 | 34 | 31 | 3 | 14 | 15 | 4 | 2 | 14 | 18 | 13 | 13 | 22 | 24
Rate 13/16 1344-LDPC code for 11ay [1] (matrix H 252 x 1344, Z = 42)
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
Lifting
matrix

## Slide 5: Rate 7/8 1248-LDPC code proposed for 11ay [1]
Rate 7/8 (1248, 1092) LDPC code is derived by puncturing the first 96 parity bits of the rate 13/16 (1344, 1092) LDPC code.
Transmitter does not transmit the punctured bits; receiver set log-likelihood ratios to zero for these bits.
The codeword length of this rate 7/8 LDPC code generated through puncturing is 1248 (rather than 1344 as other LDPC codes [1] proposed for 802.11ay).
The decoding complexity of this 7/8 code is similar to the 13/16 code with additional procedure to insert zero LLR value at the punctured positions before performing decoding.
As shown in the following slides, the rate 7/8 code generated using puncturing increases the redundancy (padding more zeros during encoding and SC blocking in most cases evaluated below) and increases the complexity of SC blocking.

## Slide 6: Rate 3/4 LDPC codes in 11ad and for 11ay
Rate 3/4 672-LDPC code in 11ad [7] (matrix H = 168 rows x 672 columns, Z = 42)
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 |  | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0 | 0 | 0
35 | 19 | 41 | 22 | 40 | 41 | 39 | 6 | 28 | 18 | 17 | 3 | 28 |  |  | 
29 | 30 | 0 | 8 | 33 | 22 | 17 | 4 | 27 | 28 | 20 | 27 | 24 | 23 |  | 
37 | 31 | 18 | 23 | 11 | 21 | 6 | 20 | 32 | 9 | 12 | 29 |  | 0 | 13 | 
25 | 22 | 4 | 34 | 31 | 3 | 14 | 15 | 4 |  | 14 | 18 | 13 | 13 | 22 | 24
Rate 3/4 1344-LDPC code for 11ay [1] (matrix H = 336 x 1344, Z = 42)
Lifting
matrix
35 | 
 | 35
 | 41
41 | 
35 |  | 19 |  |  | 41 |  | 22 |  | 40 | 41 |  | 39 |  |  | 6 | 28 |  | 18 |  |  | 17 |  | 3 | 28 |  |  |  |  |  |  | 
 | 35 |  | 19 | 41 |  | 22 |  | 40 |  |  | 41 |  | 39 | 6 |  |  | 28 |  | 18 | 17 |  | 3 |  |  | 28 |  |  |  |  |  | 
 | 29 | 30 |  |  | 0 |  | 8 |  | 33 |  | 22 | 17 |  | 4 |  |  | 27 |  | 28 | 20 |  |  | 27 |  | 24 | 23 |  |  |  |  | 
29 |  |  | 30 | 0 |  | 8 |  | 33 |  | 22 |  |  | 17 |  | 4 | 27 |  | 28 |  |  | 20 | 27 |  | 24 |  |  | 23 |  |  |  | 
37 |  | 31 |  | 18 |  | 23 |  | 11 |  |  | 21 | 6 |  | 20 |  | 32 |  | 9 |  | 12 |  |  | 29 |  |  |  | 0 | 13 |  |  | 
 | 37 |  | 31 |  | 18 |  | 23 |  | 11 | 21 |  |  | 6 |  | 20 |  | 32 |  | 9 |  | 12 | 29 |  |  |  | 0 |  |  | 13 |  | 
 | 25 | 22 |  |  | 4 |  | 34 | 31 |  |  | 3 | 14 |  |  | 15 | 4 |  |  |  |  | 14 | 18 |  |  | 13 | 13 |  | 22 |  | 24 | 
25 |  |  | 22 | 4 |  | 34 |  |  | 31 | 3 |  |  | 14 | 15 |  |  | 4 |  |  | 14 |  |  | 18 | 13 |  |  | 13 |  | 22 |  | 24
Code
matrix

## Slide 7: Rate 7/8 1344-LDPC code proposed for 11ay
Generation of the rate 7/8 1344-LDPC code based on the 11ad rate 3/4 672-LDPC code (complementary):
Find an optimal lifting matrix (by search to yield the best error rate performance) to be applied to the 11ad 3/4 672-LDPC code matrix. The optimal lifting matrix is shown as below.
Rows #1 and #3 as well as Row #2 and #4 are complementary.
- Applying the optimal lifting matrix to the 11ad rate 3/4 672-LDPC code matrix yields:
- Summing the 1st& 5th, 2nd&6th, 3rd&7th and 4th&8th rows of the matrix 336 rows x 1344 columns, Z=42 above results in the rate 7/8 (1344, 1176) LDPC code matrix (168 rows x 1344 columns, Z=42):
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 |  | 
0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 |  | 0 | 1 | 
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  | 0 | 1 | 0 | 0 | 0 | 0
Row #1
#2
#3
#4
 | 35 |  | 19 | 41 |  | 22 |  | 40 |  | 41 |  | 39 |  |  | 6 |  | 28 | 18 |  |  | 17 | 3 |  | 28 |  |  |  |  |  |  | 
35 |  | 19 |  |  | 41 |  | 22 |  | 40 |  | 41 |  | 39 | 6 |  | 28 |  |  | 18 | 17 |  |  | 3 |  | 28 |  |  |  |  |  | 
 | 29 | 30 |  | 0 |  |  | 8 |  | 33 |  | 22 |  | 17 |  | 4 |  | 27 |  | 28 |  | 20 | 27 |  |  | 24 |  | 23 |  |  |  | 
29 |  |  | 30 |  | 0 | 8 |  | 33 |  | 22 |  | 17 |  | 4 |  | 27 |  | 28 |  | 20 |  |  | 27 | 24 |  | 23 |  |  |  |  | 
37 |  | 31 |  |  | 18 |  | 23 |  | 11 |  | 21 |  | 6 | 20 |  | 32 |  |  | 9 | 12 |  |  | 29 |  |  | 0 |  |  | 13 |  | 
 | 37 |  | 31 | 18 |  | 23 |  | 11 |  | 21 |  | 6 |  |  | 20 |  | 32 | 9 |  |  | 12 | 29 |  |  |  |  | 0 | 13 |  |  | 
25 |  |  | 22 |  | 4 | 34 |  | 31 |  | 3 |  | 14 |  | 15 |  | 4 |  |  |  | 14 |  |  | 18 | 13 |  | 13 |  | 22 |  | 24 | 
 | 25 | 22 |  | 4 |  |  | 34 |  | 31 |  | 3 |  | 14 |  | 15 |  | 4 |  |  |  | 14 | 18 |  |  | 13 |  | 13 |  | 22 |  | 24
Row #1
#2
#3
#4
#5
#6
#7
#8
37 | 35 | 31 | 19 | 41 | 18 | 22 | 23 | 40 | 11 | 41 | 21 | 39 | 6 | 20 | 6 | 32 | 28 | 18 | 9 | 12 | 17 | 3 | 29 | 28 |  | 0 |  |  | 13 |  | 
35 | 37 | 19 | 31 | 18 | 41 | 23 | 22 | 11 | 40 | 21 | 41 | 6 | 39 | 6 | 20 | 28 | 32 | 9 | 18 | 17 | 12 | 29 | 3 |  | 28 |  | 0 | 13 |  |  | 
25 | 29 | 30 | 22 | 0 | 4 | 34 | 8 | 31 | 33 | 3 | 22 | 14 | 17 | 15 | 4 | 4 | 27 |  | 28 | 14 | 20 | 27 | 18 | 13 | 24 | 13 | 23 | 22 |  | 24 | 
29 | 25 | 22 | 30 | 4 | 0 | 8 | 34 | 33 | 31 | 22 | 3 | 17 | 14 | 4 | 15 | 27 | 4 | 28 |  | 20 | 14 | 18 | 27 | 24 | 13 | 23 | 13 |  | 22 |  | 24

## Slide 8: SC Blocking for the 1344-LDPC code and the 1248-LDPC code (QPSK, SC block length of 448)
SC QPSK blocking for codeword length 1344
Bit-to-symbol mapping
Blocking
BLK 1
BLK 2
BLK 3
448
448
448
(symbols)
672
(symbols)
Codeword1
Codeword2
672
Source
word1
Codeword1
1344
(bits)
Encoding
Codeword2
1344
Source
word2
Source
word1
Codeword1
1248
(bits)
Encoding
Bit-to-symbol mapping
Blocking
BLK 1
448
448
448
(symbols)
Codeword2
…
Codeword28
1248
1248
Codeword1
624
(symbols)
Codeword2
…
Codeword28
624
624
Source
word2
…
Source
word28
Note: Every 3 SC blocks are constructed from 2 codewords
(Each block is constructed from 1 or 2 codewords.)
Note: Every 39 blocks are constructed from 28 codewords
(Each block is constructed from 1 or 2 codewords.)
BLK 2
…
BLK 39
SC QPSK blocking for codeword length 1248

## Slide 9: SC Blocking for the 1344-LDPC code and the 1248-LDPC code (16QAM, SC block length of 448)
SC 16QAM blocking with codeword length 1344
Source
word1
Codeword1
1344
(bits)
Encoding
Bit-to-symbol mapping
Blocking
BLK 1
BLK 2
BLK 3
448
448
448
(symbols)
Codeword2
Codeword4
1344
1344
Codeword1
336
(symbols)
Codeword2
Codeword4
336
336
Source
word2
Source
word4
Source
word1
Codeword1
1248
(bits)
Encoding
Bit-to-symbol mapping
Blocking
448
448
448
(symbols)
Codeword2
…
Codeword56
1248
1248
Codeword1
312
(symbols)
Codeword2
…
Codeword56
312
312
Source
word2
…
Source
word56
Note: Every 3 blocks are constructed from 4 codewords.
(each block is constructed from 2 codewords)
Note: Every 39 blocks are constructed from 56 codewords.
(each block is constructed from 2 or 3 codewords.)
BLK 1
BLK 2
…
BLK 39
Codeword3
Codeword3
Source
word3
1344
336
SC 16QAM blocking with codeword length 1248

## Slide 10: SC Blocking for the 1344-LDPC code and the 1248-LDPC code (64QAM, SC block length of 448)
(bits)
Encoding
Bit-to-symbol mapping
Blocking
BLK
448
(symbols)
Codeword1
1344
Codeword2
1344
(symbols)
Codeword1
224
Codeword2
224
Source
word1
Source
word2
Source
word1
Codeword1
1248
(bits)
encoding
Bit-to-symbol mapping
blocking
448
448
448
(symbols)
Codeword2
…
Codeword28
1248
1248
Codeword1
208
(symbols)
Codeword2
…
Codeword28
208
208
Source
word2
…
Source
word28
Note: Each block is constructed from 2 codewords.
Note: Every 13 blocks are constructed from 28 codewords
(each block is constructed from 3 or 4 codewords )
BLK 1
BLK 2
…
BLK 13
SC 64QAM blocking with codeword length 1344
SC 64QAM blocking with codeword length 1248

## Slide 11: Efficiency comparison
Data length (bytes) | Number of symbol block padding bits (regular / puncturing) (rate 7/8, codeword length 1344/1248, block length=448) & blocking overhead (1344/1248) (%) |  | 
 | QPSK | 16QAM | 64QAM
512 | 0 / 384 (0% / 7.1%) | 0 / 384 (0% / 7.1%) | 0 / 384 (0% / 7.1%)
1024 | 448 / 768 (0% / 7.1%) | 1344 / 768 (12.5%/7.1%) | 1344 / 768 (12.5%/7.1%)
2048 | 0 / 640 (0% / 3.1%) | 896 / 1536 (4.5% / 7.1%) | 0 / 1536 (0% / 7.1%)
4096 | 0 / 736 (0% / 1.9%) | 0 / 736 (0% / 1.9%) | 0 / 1632 (0% / 4%)
8192 | 0 / 32 (0% / 0.04%) | 0 / 928 (0% / 1.2%) | 0 / 1824 (0% / 2.3%)
16384 | 0 / 416 (0% / 0.3%) | 0 / 1312 (0% / 0.9%) | 0 / 2208 (0% / 1.4%)
Data length (bytes) | Number of data padding bits (regular / puncturing) (rate 7/8, codeword length 1344/1248) & overhead for coding (1344/1248) (%)
512 | 608 / 272 (12.9%/6.2%)
1024 | 40 / 544 (0.5% / 6.2%)
2048 | 80 / 1088 (0.5% / 6.2%)
4096 | 160 / 1084 (0.5% / 3.2%)
8192 | 320 / 1076 (0.5% / 1.6%)
16384 | 640 / 1060 (0.5% / 0.8%)

## Slide 12: Simulation
In the following slides, simulated packet error rate performance is compared among the rate 7/8 1344-LDPC code proposed in this contribution, the rate 7/8 1248-LDPC code shown in [1] and the rate 7/8 672-LDPC code [4].
The simulations refer to QPSK, 16-QAM and 64-QAM.
AWGN, 11ad conference room channel model.
The LDPC decoder is a layered decoder using 8 iterations.
Data packet length 4096 bytes.
No hardware impairments.
Ideal channel estimation.
MMSE equalization.

## Slide 13: PER (AWGN)

## Slide 14: PER (11ad conf. room)

## Slide 15: PER comparison of rate 7/8 LDPC codes
Consider the performance of the punctured code 1248-LDPC code as the reference. The performance gains (in dB) at 1% PER of various 7/8 LDPC codes are summarized below.
 | 1344-LDPC | 672-LDPC [4]
QPSK | 0.17 | -0.46
16QAM | 0.27 | -0.58
64QAM | 0.21 | -0.35
AWGN
 | 1344-LDPC
QPSK | 0.29
16QAM | 0.31
64QAM | 0.77
11ad conference room

## Slide 16: LDPC Decoder Complexity
The H matrix of 1344-LDPC code proposed in this contribution is composed of 42x42 single diagonal non-zero or null sub-matrix as the rate 3/4 code in 11ad.
1) layered decoding: as for a common QC LDPC code
- each layer (check node) corresponds to 32 variables which can be updated independently
based on the check node message;
- for each layer the check node message is calculated from 32 variable node message.
2) macro-layer decoding: one macro-layer consists two sub-layers. Each sub-layer corresponds to 16 variables the same as a layer of the original 11ad rate 3/4 LDPC code with modification in mapping between check nodes and variable nodes (this is also required for rate 3/4 1344-LDPC).
- within each sub-layer the variables can be updated as done in an 11ad LDPC decoder. Variables
for each sub-layer can be processed independently. Two sub-layers can process in parallel.
- for each macro-layer, with the min-sum decoding algorithm the check node message is calculated
by combining the results including one sign and one min value for each sub-layer.
- the LLR values can be updated macro-layer after macro-layer, and the process of 16 variables per
check node is kept unchanged for each sub-layer.
37 | 35 | 31 | 19 | 41 | 18 | 22 | 23 | 40 | 11 | 41 | 21 | 39 | 6 | 20 | 6 | 32 | 28 | 18 | 9 | 12 | 17 | 3 | 29 | 28 |  | 0 |  |  | 13 |  | 
35 | 37 | 19 | 31 | 18 | 41 | 23 | 22 | 11 | 40 | 21 | 41 | 6 | 39 | 6 | 20 | 28 | 32 | 9 | 18 | 17 | 12 | 29 | 3 |  | 28 |  | 0 | 13 |  |  | 
25 | 29 | 30 | 22 | 0 | 4 | 34 | 8 | 31 | 33 | 3 | 22 | 14 | 17 | 15 | 4 | 4 | 27 |  | 28 | 14 | 20 | 27 | 18 | 13 | 24 | 13 | 23 | 22 |  | 24 | 
29 | 25 | 22 | 30 | 4 | 0 | 8 | 34 | 33 | 31 | 22 | 3 | 17 | 14 | 4 | 15 | 27 | 4 | 28 |  | 20 | 14 | 18 | 27 | 24 | 13 | 23 | 13 |  | 22 |  | 24
32 single diagonal submatrices per row

## Slide 17: Summary
Reviewed the design of rate 7/8 long LDPC codes [1] proposed for 11ay.
Evaluated the PER performance of the proposed rate 7/8 1344-LDPC code and the punctured 1248-LDPC code. The performance of the proposed 1344-LDPC code is up to 0.77 dB better than the punctured 1248-LDPC code [1].
Analyzed the implementation on symbol blocking for different codeword lengths. The rate 7/8 1344-LDPC codes preserves the codeword length unchanged as other relatively lower-rate codes proposed for 11ay and demonstrate benefits with small granularity in mapping between codewords and single carrier symbol blocks as well as with less redundancy to be added during encoding and symbol blocking (for relative long packets).
Discussed decoding complexity.
- Decoding of the punctured code [1] is almost the same as decoding of the rate 13/16 1344-LDPC code.
- The 1344-LDPC code we proposed in this contribution allows decoding as for a common QC LDPC code. Due to row complementary property in the lifting matrix of this code, variables for each sub-layer can be processed independently allowing parallel process of two sub-layers and LLR update is macro-layer by macro-layer. The decoding complexity of this code is comparable to that of the rate 3/4 1344-LDPC code.

## Slide 18: References
[1] 11-16-0676-01-00ay-length-1344-ldpc-codes-for-11ay.
[2] Draft P802.11ay_D0.3.
[3] IEEE 802.11-16/0233, Additional SC MCSs in clause 20 (DMG PHY).
[4] 11-16-1495-01-00ay-rate-78-ldpc-code-for-11ay.
[5] IEEE Std 802.11™-2016.