## Slide 1: Optimized Short SSW frame addressing scheme to reduce the false positive
Date: 2017-01-04
Authors:

## Slide 2: Backgrounds
In [1], It’s proposed to use CRC-16 CCITT to fill the 16 bit addressing field.
The addressing field is still TBD , and we assume it would be as : A(16bits):= CRC16( RA(48bits)||TA(48bits)), whereby the A denotes the Addressing field in the Short SSW frames and RA and TA both denote the addressing field inherent within 11ad SSW frames, CRC16 denotes the CRC 16-CCITT.
It’s also lack of quantitative analysis of the false positive (probability of collision in the context of OBSS environment).
We would like to propose using 16bits dual partial AIDs ( RA-AID(8bit),TA-AID(8bit) to fill up the address field which achieves better false positive probability and efficiency.
 | Packet Type | Addressing | CDOWN | RF Chain ID | Short SSW Feedback | Direction | Reserved | FCS
Bits: | 2 | 16 | 11 | 2 | 11 | 1 | 1 | 4
 | Packet Type | Addressing | CDOWN | RF Chain ID | Short SSW Feedback | Direction | Reserved | FCS
Bits: | 2 | 16 | 11 | 2 | 11 | 1 | 1 | 4
RA
AID1
TA
AID2

## Slide 3: How to calculate the False Positive Rate
The false positive for hashed address calculation within a (P)BSS is based on [3]
(1)
Where n denotes number of STAs per BSS, H equals to 2^m, where m denotes number of bits.
Lemma 1: the false positive probability in OBSS (b>=2), the false positive for hashed address for OBSS with equal number of STAs per BSS, is calculated as
(2)
Where the b denotes the number of BSS, namely the OBSS.
Lemma 2: The false positive for dual AID calculation within OBSS with equal number of STAs is as:
(3)
Assuming p<1% is the good false positive rate which is equivalent of PER <10^(-2)

## Slide 4: Hashed Address vs 16bits dual AIDs
Chart: 
| n=2 | n=4 | n=8 | n=16 | n=32 | n=64
 | 3.0518e-05 | 0.00012207 | 0.00048828 | 0.0019531 | 0.0078125 | 0.03125
 | 0 | 0 | 0 | 0 | 0 | 0
b=1 (Single BSS)
b=2 (3 OBSS)
b=5 (5 OBSS)
b=8 (8 OBSS)
Note: - Blue line is the False Positive Probability for Hashed Address
- Red line is the False Positive Probability for 16bits dual AIDs
Chart: 
| n=2 | n=4 | n=8 | n=16 | n=32 | n=64
m=16 16 | 0.00027466 | 0.0010986 | 0.0043945 | 0.017578 | 0.070313 | 0.28125
m=16 16 | 0.00024414 | 0.00097656 | 0.0039062 | 0.015625 | 0.0625 | 0.25
Chart: 
| n=2 | n=4 | n=8 | n=16 | n=32 | n=64
m=16 16 | 0.00045776 | 0.0018311 | 0.0073242 | 0.029297 | 0.11719 | 0.46875
m=16 16 | 0.00042725 | 0.001709 | 0.0068359 | 0.027344 | 0.10938 | 0.4375
Chart: 
| n=2 | n=4 | n=8 | n=16 | n=32 | n=64
m=16 16 | 9.1553e-05 | 0.00036621 | 0.0014648 | 0.0058594 | 0.023438 | 0.09375
m=16 16 | 6.1035e-05 | 0.00024414 | 0.00097656 | 0.0039062 | 0.015625 | 0.0625

## Slide 5: RX Decoding Efficiency
In comparison, the hashed addresses scheme consumes more time in hashing and matching (the box), the time complexity is linearly depending on the size of the List of MAC addresses O(N) in a general case (note)
On the contrary, the dual AIDs scheme is straight forward matching with less time and memory consumption.
Decoding Sequence with Hashed Address scheme
Decoding Sequence with Dual AID schemes

## Slide 6: Solution: for the AID=0 problem in OBSS
AID =0 problem definition: when DMG PCP/AP assigns the AID to DMG STA, it follows the rule specified in 9.4.1.8 [4]
  1-254 are assigned to STAs
  0 is assigned to PCP/Aps
  255 is assigned to b’cast address
  The 8 MSBs of the AID field to 0
  When operating in the OBSS, the false positive probability will be significantly greater when all PCP/APs are assigned with AID=0
In EDMG, PCP/AP may choose to randomly generate the 8 bits “EDMG BSS AID” applied to the 8 MSBs of the AIDs for both EDMG PCP/APs and EDMG STAs.
When the EDMG PCP/AP transmits or receives the short SSW frames, the AID field for EDMG PCP/AP should be filled with the 8 bits of EDMG BSS AID.
When the EDMG STA transmits or receives the short SSW frames, the AID field for EDMG STA should be filled with the 8 LSBs of the DMG AID field.
The delivery of the EDMG BSS AID:
I.e the EDMG BSS AID could be delivered to STA through EDMG capability information elements or EDMG operation elements:
1
1
6
1
1
8
2

## Slide 7: BSS AID Generation
Option I: The BSS AID (8 MSBs of the EDMG AID field) is randomly generated by AP
Option II: 8 bit BSS Coloring scheme.

## Slide 8: Dual AID Addressing with TA check
Procedure at the receiver
2
4
3
1
5
BSS#2 (OBSS)
BSS#1
Source(TA)
Dest.(RA)
n STAs
Check if the received TA_AID exists in the associated AID list
The false positive probability per transmission is:
, where
No collision condition:
The same AID values as the RA and TA AID pair is not used in any overlapped BSS(s).

## Slide 9: Analysis
False positive probability increases exponentially depending on the number of STAs (n), and the methods based on current proposals may not work for large n (e.g. n>16).
  We think target false positive probability should be less than 1%.

## Slide 10: Benefit of address scrambling
By applying seed to the Addressing, consistent collision can be avoided compared with dual AIDs only. i.e. when SLS is failed, STA can re-try SLS with different seed.
Consistent collision rate with two seed (i.e. the rate that both successive two SLSs are failed) should be square of the collision rate per transmission if the scrambling is properly designed.
[5] 2016-TECH-Panasonic-0017-00-Short SSW addressing

## Slide 11: Proposed method
The addressing is based on Dual AID for the Short SSW addressing fields.
In ISS, Short SSW packet includes Short Scrambled BSSID field, whose value is the 10 LSBs of CRC-16-CCITT of the BSSID.
The BSSID is scrambled with integer addition scrambling before CRC calculation.
[5] 2016-TECH-Panasonic-0017-00-Short SSW addressing

## Slide 12: Integer addition scrambling
Add a scramble pattern to each 16bit-word of RA and TA
  i-th word’ = (i-th word + Pattern) mod 216
    The additions should be integer additions instead of XOR
Suitable for computation with software/hardware
BSSID = 57-89-65-58-2F-17
+
5795
=
Pattern
+
5795
=
+
5795
=
BSSID’= AF-1E-BC-ED-86-AC
Seed | Scramble Pattern (hex) | Seed | Scramble Pattern (hex)
0 | 0000 | 8 | 3CA8
1 | 5795 | 9 | 143D
2 | 2F2A | A | 6BD2
3 | 06BF | B | 4367
4 | 5E54 | C | 1AFC
5 | 35E9 | D | 7291
6 | 0D7E | E | 4A26
7 | 6513 | F | 21BB
Recommended scramble patterns
  Pattern = (0x5795 * seed) mod 215

## Slide 13: Receiver procedure (+ collision rate)
When Assoc.
Construct SS-BSSID table
for SI=0to15
Receives SSSW packet
(1) Check if the received SS-BSSID matches to the current SS-BSSID according to the received seed
Performed in advance (optional)
(2) Check if the received RA AID is own AID
(3) Check if the received TA_AID exists in the associated AID list (optional)
without TA_AID check
with TA_AID check
where
The false positive probability per transmission is:
The rate is independent from the Addressing scheme and the number of STAs. The rate can be seemed as the upper limit.
Combined with some Addressing scheme, additional reduction of collision rate may be achieved.
For example, when we use the dual AID with BSS AID scheme[4], the collision rate will be:
, where
[4] 2016-TECH-Huawei-0050-01-Short SSW frame addressing scheme with Dual AID

## Slide 14: Collision probability analysis
Collision probability will be less than 1% with 10bit SS-BSSID for 8 BSSs and any number of STAs.
0.00%
0.10%
0.39%
0.68%

## Slide 15: Conclusion
We conducted a collision rate analysis and showed that current solutions[1] suffered from significant performance degradation in OBSS environment.
The proposed method which uses Dual AID with TA AID check , and the short scrambled BSSID (SS-BSSID) improves the performance in OBSS, as well as provides means for avoiding consistent collisions.
If the TA/RA is the AP itself, the TA/RA AID field should be filled with the 8 bits of the EDMG BSS AID
 | Packet Type | Addressing | CDOWN | RF Chain ID | Short SSW Feedback | Direction | Reserved | FCS
Bits: | 2 | 16 | 11 | 2 | 11 | 1 | 1 | 4
RA
AID1
TA
AID2

## Slide 16: References
11-16-0416-01-00ay-short-ssw-format-for-11ay

## Slide 17: Straw Poll1/Motion
Do you agree to define in the SFD, the 16 bits of address field within Short SSW frame to contain RA and TA AID fields. If the TA or RA is the AP itself, the TA or RA AID field should be filled with the 8 bits of the EDMG BSS AID . In case of ISS and Unicast, the Short SSW Feedback field should be replaced by the Short Scrambled BSSID(SS-BSSID) field”

## Slide 18: Straw Poll2/Motion
Do you agree to add the following to the SFD “The BSSID values are scrambled with the following formula before the calculation of SS-BSSID in the Short SSW packet.
    scrambled i-th word = (i-th word + scramble pattern) mod 216, where each word is the part of the BSSID which is split by 16 bits, and + is integer addition.
    ”

## Slide 19: Straw Poll3/Motion
Do you agree to add the following to the SFD “Scramble patterns for SS-BSSID calculation are defined as follows:
Scramble pattern = (0x5795 * seed) mod 128
The seed is the scrambler initialization in the PHY header of the Short SSW packet. ”