## Slide 1: WUR Phase Noise Model Study
Date: 2017-01-10
Authors:

## Slide 2: Abstract
This presentation describes a phase noise model for WUR that takes power consumption into account

## Slide 3: Introduction
The power consumption target for a wake-up receiver is much lower than a legacy 802.11 STA
  WUR SG PAR [802.11-16/1045r9]: “The WUR has an expected active receiver power consumption of less than one milliwatt”
In 802.11, a simple phase noise model proposed in [802.11-04/224r1] has been used for a legacy 802.11 STA but without any constraint on power consumption
We believe TGba should have a new phase noise model that takes the power consumption into account

## Slide 4: TGn Phase Noise Model [11-04/224r1]

## Slide 5: Phase Noise Profile of a Ring Oscillator [1]
Example: 65 nm, 75 µW power consumption
[1] O. Khan; B. Wheeler; F. Maksimovic; D. Burnett; A. M. Niknejad; K. Pister, "Modeling the Impact of Phase Noise on the Performance of Crystal-Free Radios," in IEEE Transactions on Circuits and Systems II: Express Briefs , vol.PP, no.99, pp.1-1

## Slide 6: CDF of Integrated Phase Noise [1]
500 iterations
Fc=2.447 GHz
Integration bandwidth
  10 KHz – 2 MHz and 10 MHz
  10 KHz resolution
Statistics
  Min: -13.5dBc
  Max: -0.25dBc
  Mean: -4.24dBc
  Median: -3.6dBc
  Std: 2.87dBc

## Slide 7: Minimum Phase Noise of a Ring Oscillator
Minimum phase noise of a ring oscillator with the minimum power consumption is shown in [2]:
  Definitions
    PNmin: minimum phase noise; Pmin: minimum power dissipation
    f0: oscillation frequency; Δf: offset frequency
    k: Boltzmann constant, T: temperature
  [2] Navid, T. H. Lee, R. W. Dutton, “Minimum Achievable Phase Noise of RC Oscillators”, JSSC 2005
(1)

## Slide 8: Single-Sideband Phase Noise Spectrum in dBc/Hz
The single-sideband phase noise L(fm) (in dBc/Hz) is expressed as follows for small values of c and for 0<=fm<<f0 in [3]
where fm= Δf: offset frequency and L(fm)=PN(Δf).
[3] A. Demir, A. Mehrotra, and J. Roychowdhury., "Phase noise in oscillators: a unifying theory and numerical methods for characterization," Transactions on Circuits and Systems I: Fundamental Theory and Applications, vol. 47, no. 5, pp. 655-674, May 2000.
(2)

## Slide 9: Finding the Constant c for a Given LO Power Consumption
Choose power consumption Pmin
Find constant c that makes PN overlap with PNmin
Example 1:
  f0 = 2.437GHz
  PNmin(Δf) at Pmin=75µW
  PN(Δf) with c = 0.5e-15
  Integrated PN (iPN) =-5.7dBc
    10 KHz ~ 2 MHz

## Slide 10: Example 2: Pmin=20 µW
Parameters
  f0 = 2.437GHz
  PNmin(Δf) at Pmin=20 µW
  PN(Δf) with c = 1.875e-15
  Integrated PN (iPN) =-2.1dBc
    10 KHz ~ 2 MHz

## Slide 11: Conclusions
The phase noise model (Slide 8 eq.(2)) shown in [1] and [3] is a good candidate phase noise model for WUR development in TGba with some margin
The minimum phase noise model (Slide 7 eq.(1)) shown in [2] can be used to estimate the power consumption of a ring oscillator

## Slide 12: References
[1] O. Khan; B. Wheeler; F. Maksimovic; D. Burnett; A. M. Niknejad; K. Pister, "Modeling the Impact of Phase Noise on the Performance of Crystal-Free Radios," in IEEE Transactions on Circuits and Systems II: Express Briefs , vol.PP, no.99, pp.1-1
[2] Navid, T. H. Lee, R. W. Dutton, “Minimum Achievable Phase Noise of RC Oscillators”, JSSC 2005
[3] A. Demir, A. Mehrotra, and J. Roychowdhury., "Phase noise in oscillators: a unifying theory and numerical methods for characterization," Transactions on Circuits and Systems I: Fundamental Theory and Applications, vol. 47, no. 5, pp. 655-674, May 2000.