## Slide 1: On Waking-Up Multiple WUR Stations
Date: 2017-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | 
Russell Huang |  |  |  | 
Thomas Pare |  |  |  | 
James Wang |  |  |  | 

## Slide 2: General use of WUR in WLAN
Wake-up Radio (WUR) WLAN System = Main radio (Regular Wi-Fi radio) + Wake-up Radio (WUR)
  Main radio (802.11): for user data transmission and reception
    User data is transmitted and received by the main radio
    Main radio is off unless there is data to transmit or receive
    WUR wakes up the main radio when there is a packet to receive
  WUR: not for data communication, only serves as a simple switch to “wake-up” the main radio
    WUR is a low-cost low power consumption receiver
    Target power consumption < 1 mW in the active state
    Using Simple modulation scheme such as On-Off-Keying (OOK) and Narrow bandwidth

## Slide 3: Multiple User (MU) Wake-up Signal Transmission
To achieve the similar range coverage as the WLAN, a WUR needs to operate on narrow bands, for example, the channel band-width for wake-up signals can be about 1MHz, 2MHz, 4MHz or 5MHz.
Multi-user format of wake-up signal transmission
  Packet format: Legacy/HT/VHT/HE Preamble + frequency division multiplexing access (FDMA) on/off keying (OOK) modulation
  Legacy/HT/VHT/HE Preamble is for spoofing the Legacy, HT, VHT and HE stations and protecting the wake-up signal transmissions.
MU-Wake-Up Packet

## Slide 4: Cascaded Wake-Up Signal Transmission
When an AP needs to wake up a few WUR stations that are operating on the same channel, AP can use cascaded wake-up sequences transmission.
  The duration field in the SIG filed of the legacy/HT/VHT/HE preamble should be large enough to protected the transmission of all cascaded wake-up signals.

## Slide 5: Advantages of Enabling Multiple User (MU) Wake-up
High efficiency
  Since the wake-up signals is narrow band, it takes long time to transmit. MU wake-up scheme can significantly enhance the spectral efficiency.
  Spoofing preamble does not need to send many times.
Good match with11ax MU transmission
  11ax already introduced OFDMA transmission, which is similar to FDMA MU wake-up signal transmission.
  11ax MU packet can be directly used to deliver data to multiple WUR stations after MU wake-up signals.
Reduce latency
  When there are a lot of WUR stations need to be waked-up and to receive packet from AP, MU wake-up scheme can greatly reduce latency.

## Slide 6: Straw Poll
Do you agree that IEEE 802.11ba shall provide Multiple User wake-up schemes?