## Slide 1: Traffic Filter based Wakeup Service
Date: 2017-01-16
Authors:

## Slide 2: Introduction
This submission discusses the wakeup service operation in a system aspect

## Slide 3: Basic Wakeup Service
The wakeup service is enabled by a request from a STA (WUR STA) [1]
An AP disables the wakeup service autonomously or depending on a request from the STA
When the wakeup service is enabled for the STA, an AP delivers a Wakeup frame to the STA upon meeting TBD condition

## Slide 4: Basic Wakeup Service [11-16/0722r1]
Wakeup Service Request
Beacon {+ WUR Support capability indication}
STA
AP
Wakeup Service Response
Wakeup frame
Trigger frame (e.g., PS-Poll or QoS Null)
Data frame
Ack frame
802.11 Radio
WUR
Wakeup.response primitive is issued for activating 802.11 radio
Wakeup.request primitive is issued upon meeting TBD condition
802.11 Radio
WUR
Wakeup.response primitive is issued for inactivating 802.11 radio
Power On
Power Off
Power On

## Slide 5: Considerations on wakeup frame transmission
When is a Wakeup frame triggered?
  If an AP triggers a Wakeup frame whenever the buffered frames for an STA (WUR mode) exist even though it is a delay insensitive frame, a wakeup frame transmission can overwhelm the wireless medium
  Also, it is vulnerable on a malicious attack from anonymous device
A managing mechanism of excessive wakeup frame transmissions is needed
  The traffic filter service (TFS) defined in IEEE 802.11v-2011 can be a solution [2][3]

## Slide 6: TFS Protocol Overview
An AP/STA negotiates the TFS via TFS Request and Response frames
  A STA can add traffic filters any time after association or delete filters at any time
  An AP may delete filters if it executes the filter action (e.g. wakeup)
AP Operations
  An AP inspects unicast and multicast traffic on behalf of STA which installed filter
  An AP discards unmatched unicast traffic regardless of power states when TFS is enabled
  An TFS Notify frame is delivered before the triggering frame if requested by the STA

## Slide 7: TFS Protocol Overview
A STA delivers filtering patterns to an AP via TFS Request IEs

## Slide 8: TFS Protocol Overview
The TFS Action Code field defines the actions taken at an AP when a frame matches a traffic filter set
Bits | Name | Notes
0 | Delete After Match | Setting this field to 1 for any traffic filter set indicates all traffic filter sets established at the AP for the non-AP STA are deleted when a frame matches any of the traffic filter sets established for the non-AP STA. A value of 0 for this field indicates no deletion of the traffic filter set upon a match.
1 | Notify | Setting this field to 1 indicates the STA is to be sent a TFS Notify frame upon the first frame matching to the traffic filter set or the first frame match after the AP receives a Notify Response frame containing the corresponding TFS ID. Setting this field to 0 indicates the AP does not send TFS Notify frame to the requesting STA.
2-7 | Reserved | All other bits are reserved.

## Slide 9: Traffic Filter based Wakeup Service
The TFS Action Code field has Wakeup Notify bit subfield
  Indicate that a Wakeup frame upon the first frame matching to the traffic filter set is sent or not
Bits | Name | Notes
0 | Delete After Match | Setting this field to 1 for any traffic filter set indicates all traffic filter sets established at the AP for the non-AP STA are deleted when a frame matches any of the traffic filter sets established for the non-AP STA. A value of 0 for this field indicates no deletion of the traffic filter set upon a match.
1 | Notify | Setting this field to 1 indicates the STA is to be sent a TFS Notify frame upon the first frame matching to the traffic filter set or the first frame match after the AP receives a Notify Response frame containing the corresponding TFS ID. Setting this field to 0 indicates the AP does not send TFS Notify frame to the requesting STA.
2 | Wakeup Notify | Setting this field to 1 indicates the STA is to be sent a Wakeup frame upon the first frame matching to the traffic filter set or the first frame match after the AP receives a Notify Response frame containing the corresponding TFS ID. Setting this field to 0 indicates the AP does not send Wakeup frame to the requesting STA.
3-7 | Reserved | All other bits are reserved.

## Slide 10: Traffic Filter based Wakeup Service Example
Wakeup Service Request {+ TFS Request}
STA
AP
Wakeup Service Response {+ TFS Response}
Wakeup frame
Trigger frame (e.g., PS-Poll or QoS Null)
802.11 Radio
WUR
Wakeup.response primitive is issued for activating 802.11 radio
802.11 Radio
WUR
Wakeup.response primitive is issued for inactivating 802.11 radio
Power On
Power Off
Power On
-Wakeup.request primitive is not issued because the Traffic Filter condition is not met
3rd party network entities
-Wakeup.request primitive is not issued because the Traffic Filter condition is met but it is a delay insensitive packet
Malicious packet
Trusted packet (Delay insensitive)
-Wakeup.request primitive is issued because the Traffic Filter condition is met from a delay sensitive packet
Trusted packet (Delay sensitive)

## Slide 11: Summary
TGba should consider a mechanism for managing excessive wakeup frame transmissions
TBD condition that an AP delivers the wakeup frame to the STA upon meeting may consist of
  Traffic filter
  Minimum interval between successive wakeup frames
  Number of retransmitted wakeup frame
  Etc.

## Slide 12: References
[1] https://mentor.ieee.org/802.11/dcn/16/11-16-1445-01-0wur-overall-mac-procedure-for-wur.pptx
[2] https://mentor.ieee.org/802.11/dcn/07/11-07-0737-00-000v-sleep-mode-with-ap-filtering.ppt
[3] https://mentor.ieee.org/802.11/dcn/07/11-07-2148-00-000v-traffic-filtering-and-sleep-mode-presentation.ppt

## Slide 13: Straw Poll
Do you agree that TGba shall provide a mechanism to avoid excessive wakeup frame transmissions?