IEEE P802.11
Wireless LANs

| Proposed 802.11ba Functional Requirements |
| --- |
| Date: 2017-01-16 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Ming Gan | Huawei Technologies | F1-17, Huawei Base, Bantian, Longgang District, Shenzhen, China |  | ming.gan@huawei.com |
| David Xun Yang |  |  | +86-15914117462 | David.yangxun@huawei.com |
| Yunsong Yang |  | 10180 Telesis Court, STE 165, San Diego, CA 92130, U.S.A. |  | yangyunsong@huawei.com |
| Edward Au |  | 303 Terry Fox Drive Kanata, ONT, Canada |  | edward.ks.au@huawei.com |
| Osama Aboul-Magd |  |  | +1-613-287-1405 | osama.aboulmagd@huawei.com |
| Peter Loc |  |  |  | peterloc@iwirelesstech.com |

### Abstract

This submission proposes the 802.11ba Functional Requirements as derived from the 802.11ba PAR [Ref-1] and CSD [Ref-2].

# Introduction

## Purpose

This document proposes requirements for solutions addressing functionality to be provided by the 802.11ba amendment, referred to as the TGba Functional Requirements (FRs).

## Scope

The scope for deriving functional requirements is set by the P802.11ba PAR [Ref-1] and CSD [Ref-2].

The functional requirements as stated in this document cover the following aspects of 802.11ba:

- System performance

- Bands of Operation

- Coexistence

- Compliance to PAR

## Notation

Requirements are identified by a preceding unique number in the format of “TGba Rn” , where n is an integer number representing the ID of the requirements.

# Functional Requirements

## System Performance

### Active receiver power consumption

- The mechanisms defined in the 802.11ba amendment shall enable a wake up receiver to consume less than one milliwatt when the wake up receiver is active.

### Latency of transmission

- The mechanisms defined in the 802.11ba amendment should maintain low latency where the 802.11ba device’s primary connective radio requires.

### Legacy Performance

- Legacy performance shall not be significantly degraded by operation of 802.11ba devices or in their proximity.

### Range of transmission

- The mechanisms defined in the 802.11ba amendment shall enable wake-up radio to work within the same range as the primary connectivity radio.

## Bands of Operation

- The 802.11ba amendment shall define operations for 2.4 GHz and 5 GHz bands.

- The 802.11ba amendment may define operations for the license-exempt sub-1GHz frequency bands.

## Coexistence

- The 802.11ba amendment shall enable coexistence with legacy IEEE 802.11 devices operating in the same band of the wake-up radio.

## Compliance to PAR

- The 802.11ba amendment shall comply with the PAR [Ref-1] and the CSD [Ref-2].

# References

- 11-16-1045-09-0wur-a-par-proposal-wur-sg

- 11-16-0936-04-0wur-a-csd-proposal-for-wake-up-radio-wur