## Slide 1: NDP Short Feedback Design
Date: 2017-01-15
Authors:

## Slide 2: Background (1)
It is well accepted that being able to get a very short simultaneous feedback from a high number of STAs (all STAs) improve the 11ax system and power efficiencies [1], [3]
  Many feedbacks require 1 bit: PS-Poll (power efficiency), Channel Availability (collisions avoidance)
  Other feedbacks could be 2 bit. For example: “How many buffered Bytes for transmission: 0, 1 to 1000, 1000 to 5000, > 5000 ?”
  A short simultaneous resource request feedback (1 or several bits) capable of supporting a high number of STAs is needed for an efficient UL MU simultaneous scheduling in addition to the existing (or enhanced) piggybacked buffer information
  Less overhead for resource request feedback than polling method
  Low and stable latency for resource request feedback, compared to possibly high and unpredictable latency with CSMA-CA in dense environments

## Slide 3: Background (2)
In Nov. 2016, added subclause 25.5.2.7 to the spec: 25.5.2.7 NDP feedback report procedure The NDP feedback report is a mechanism for an HE AP to collect short feedbacks from a very high number of HE STAs, in an efficient manner. The feedbacks (e.g. resource requests) are sent without data payloads in response to a Trigger frame. The feedbacks are not for channel sounding. This mechanism is optional for non-AP STA.
But details of the NDP feedback mechanism are TBD
This contribution propose a signaling technique for the NDP feedback mechanism that can handle a high number of STAs and is power and air time efficient

## Slide 4: How to define the NDP feedback mechanism?
UL MU transmission in response to a trigger frame
Use frequency dimension for many small orthogonal allocations
To avoid collisions, assign orthogonal allocations to users
No data payload (NDP), STAs transmit energy on one orthogonal allocation for feedback
  with spreading gain in time domain for PHY robustness
For minimal changes to the current PHY, we propose
  to use UL MU NDP simultaneous transmissions in response to a trigger frame
  and to define orthogonal allocations (resource block RBs) to multiplex different STAs’ feedbacks
  These orthogonal allocations (RBs) are defined by using different frequency tone sets

## Slide 5: Overview of proposed signaling for Short Feedback
There are 9 RUs of 26 tones in 20 MHz. Each 26 tones RU are sub-divided into four sets of 6 tones.
  6 tones sets are chosen to pack 2 users per 26 tones RU
  6 tones sets have enough frequency diversity per 26 tones RU
One or two bit are assigned to one user feedback response
Two sets of 6 tones are used to transmit 1 bit
Channel estimation is not needed for detection
AP and STAs must have a prior agreement on tone sets and P-matrix spreading to use for a given response

## Slide 6: 4 tones sets per RU-26 for UL Feedback
Tone Set # | Left or Right of DC | Centered on DC
1 | 1:4:21 | -15:4:-7, 4:4:12
2 | 3:4:23 | -13:4:-5, 6:4:14
3 | 2:4:22 | -14:4:-6, 5:4:13
4 | 4:4:24 | -12:4:-4, 7:4:15
4X HE-LTF Tones transmitted
All RUs, except RU centered at DC
RU centered at DC
Notes: Dots represent unallocated tones For all RU-26 except DC, offset count is from leftmost tone.
For RU-26 at DC, offset count is from DC.
6 tones: 3.51 dB ≤ PAPR ≤ 5.21 dB
12 tones: 4.42 dB ≤ PAPR ≤ 6.87 dB

## Slide 7: Proposed feedback schemes
Multiplex different users with P-matrix code (and potentially different tone sets);
Separate different states of the same user with different tone sets.
Two sets of 6 tones are used to transmit 1 bit:
  If bx = 1, send energy on first tone set and quiet on second tone set
  If bx = 0, send energy on second tone set and quiet on first tone set

## Slide 8: Max # of STAs that can simultaneously send the UL Short Feedback
BW | Response = 1 bit |  |  | Response = 2 bit |  | 
 | Nss = 1 | Nss = 2 | Nss = 4 | Nss = 1 | Nss = 2 | Nss = 4
20 MHz | 18 | 36 | 72 | 9 | 18 | 36
40 MHz | 36 | 72 | 144 | 18 | 36 | 72
80 MHz | 74 | 148 | 296 | 37 | 74 | 148
160 MHz | 148 | 296 | 592 | 74 | 148 | 296

## Slide 9: Further discussion on the proposed feedback mechanism (1)
Reuses the 4X HE-LTF sequence [2]
Puncture all tones except for one or two 6 tones set in one 26 tones RU
For a constant nominal power in each 26 tones RU, boost tone power relative to the target RSSI
  10*log10(26/6) = 6.37 dB above target RSSI
  12 tones: 10*log10(26/12) = 3.36 dB above target RSSI
Multiply the punctured HE-LTF sequence by the P-matrix row corresponding to a specific spatial stream (SS)
  Allow multiplexing multiple users
  Recommend using 1x1, 2x2 and 4x4 P-matrix, 1 ≤ Nss ≤ 4
    Corresponding to 1, 2 or 4 time-domain symbols

## Slide 10: Further discussion on the proposed feedback mechanism (2)
Spreading gain from SS improve performance and reliability:
    One symbol, Nss = 1  0 dB 1x1 P-matrix
    Two symbols, Nss = 2  3.01 dB 2x2 P-matrix
    Four symbols, Nss = 3, 4  6.02 dB 4x4 P-matrix
No collisions between STAs
  AP assign to each STA:
    RU-26, a unique SS and multiples sets of 6 tones
      For 1 bit response, assign 2 sets of 6 tones
      For 2 bit response, assign 4 sets of 6 tones

## Slide 11: Feedback Signal Properties
Channel estimation is not required for detection
Detection performance is independent of sequence
  AP is not required to have prior knowledge of feedback sequence
Signal is robust to interference and channel response
Trivial detection, no adaptive threshold adjustment
  Compare sum of power between sets of 6 tones or de-spreading rows of P-Matrix
Detection in unaffected by timing offset
  With the +/-400 ns timing accuracy and a 120 m radius, there is up to 1.6 us of timing offset.
A “No response” from STA can be easily detected
  A “No response” from a STA could mean STA did not received the query, is out of range or the AP did not decode properly the feedback response.
  In interference prone environments, responses from STAs could be missed. AP can identify STAs with “No response” and treats them accordingly

## Slide 12: Example of Detection Algorithm
Processing for each P-matrix row:
  De-spreading
  Sum power per set of 6 tones (four sets of 6 tones for each RU-26)
  Compare powers between corresponding sets for decision
Detection algorithm for b0 (3 outcomes)
  P1 = sum(power in b0 = 1 tone locations)
  P0 = sum(power in b0 = 0 tone locations)
  K = 3; % Suggested decision scaling factor
  ( P1 > K∙P0 )  b0 = 1
  ( P0 > K∙P1 )  b0 = 0
  not( P1 > K∙P0 ) & not( P0 > K∙P1 )  No response

## Slide 13: Simulations

## Slide 14: Flat channel, Nss = 4, probabilities in AWGN
P(NoResp  YES/NO) = 2.29e-2
1 bit, 6 tones: Boost = +6.37 dB, K = 3
2 bits 12 tones: Boost = +3.36 dB, K = 3
Probability of Error are for
6 tones payload with 1 bit
12 tones payload with 2 bits

## Slide 15: 6 tones sequence Channel Sims
1x4 (TX antennas x RX antennas)
Nss = 4
Channel D: SNR is for the ensemble of channel realizations
Timing offset added
  +400 ns of timing error plus round trip delay for 100 m
CFO and Power imbalance added
4 signals are combined equally
Worst case analysis;
  STA #1 reply b0 = 1 and STA #2 to #4 replies b0 = 0
  Select tone locations that maximize crosstalk
    b0 = 1  Tones locations: 1, 5, 9, 13, 17, 21 b0 = 0  Tones locations: 2, 6, 10, 14, 18, 22

## Slide 16: STA #1 Probability Mis & False, Nss = 4, Channel D and uMI-NLOS with CFO & Time Offset
4 STAs with 1 TX antenna per RU26
AP with 4 RX antennas
CP: 1.6 us, Time offset: 1.0667 us
#1 send b0 = 1, #2 to #4 send b0 = 0
#1 to #4 power: [0, +5, +10, +15] dB
#1 to #4 CFO: [-400, +400, -400, +400] Hz
Signal power normalized for the realization ensemble
Time offset is 400ns of timing error plus 100m round-trip
6 tones: Boost = +6.37 dB, K = 3

## Slide 17: Summary
Proposed to define an NDP short feedback report mechanism based on sets of 6 tones in any RU26.
One bit of response require 2 sets
Two bits of response requires 4 sets.
Users are multiplexed in the frequency domain and time domain using P matrix.
The design has the following attributes:
  Interleaving in frequency non-nulls with nulls tones makes the RX detection insensitive to the Channel frequency response
  Detection algorithm is independent of RX level, Interference, P-Matrix size (i.e. number of symbols), number of RX antennas and Sequence
  Feedback response is an affirmative bn = 1 or bn = 0
    AP knows which STAs that did not reply
  For SNR ≥ 0, False detection rate is very small (< 10-6)
  PAPR of 6 tones sequence is between 3.51 to 5.21 dB
The design can be extended to wide BW, i.e. a 242RU to allow each STA to occupy 20MHz.

## Slide 18: References
[1] IEEE 802.11-16/1367r0: NDP feedback report
[2] IEEE 802.11-15/1334r1: HE-LTF sequence design
[3] IEEE 11-16-0xxx-00-00ax-Proposed spec text for NDP feedback report

## Slide 19: Straw poll #1
Do you agree to add to the spec:
The NDP short feedback report design uses sets of 6 tones in any 26RU as defined in the table and diagrams below. Time domain P matrix spreading (2x2 and 4x4) is used to enhance reliability and multiplex users. 1 bit feedback requires two sets – sets #1 and #2 or sets #3 and #4 depending on what sets are allocated to a user. 2 bit feedback require the use of all 4 tone sets. When tone sets #1 and #2 are used to send 1 bit, bit = 1 is sent by sending energy only on tone set #1 with 6dB power boost relative to the signaled target RSSI. bit = 0 is sent similarly using tone set #2. If 2 bits are sent the power boost is 3dB.
Tone Set # | Left or Right of DC | Centered on DC
1 | 1:4:21 | -15:4:-7, 4:4:12
2 | 3:4:23 | -13:4:-5, 6:4:14
3 | 2:4:22 | -14:4:-6, 5:4:13
4 | 4:4:24 | -12:4:-4, 7:4:15
4X HE-LTF Tones transmitted
All RUs, except RU centered at DC
RU centered at DC
Notes:
Dots represent unallocated tones For all RU-26 except DC, offset count is from leftmost tone.
For RU-26 at DC, offset count is from DC.