## Slide 1: Enhanced SLS BF flow for efficient AP-STA access in dense environment
Authors:
Name | Affiliation | Address | Phone | Email
Alexander Maltsev | Intel | Turgeneva 30, Nizhny Novgorod, 603024, Russia | +7 (831) 2969444 | alexander.maltsev@intel.com
Ilya Bolotin | Intel |  |  | ilya.bolotin@intel.com
Andrey Pudeyev | Intel |  |  | andrey.pudeyev@intel.com
Artyom Lomayev | Intel |  |  | artyom.lomayev@intel.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Solomon Trainin | Intel |  |  | solomon.trainin@intel.com
Cheng Chen | Intel |  |  | cheng.chen@intel.com

## Slide 2: Agenda
Problem statement
Legacy SLS beamforming flow
Enhanced SLS and channel access for far away STAs
  Enhanced SLS training in BTI
  Enhanced SLS in Beamforming training allocation
Channel access for far away STAs
Legacy vs. Enhanced SLS comparative analysis
Conclusions

## Slide 3: Problem statement (1/2)
Due to new use cases and scenarios in 11ay now we have two PHY layer issues:
ISSUE 1: Coverage reduction in asymmetrical AP-STA configuration
Current 11ad SLS procedure considers the alternate AP and STA transmit antenna training while the receiver’s antenna pattern is configured to the quasi-omni mode.
Usually STA is equipped with smaller antenna and has less TX power than AP.
Therefore, a “distant” STA, after detecting the DMG Beacon frame (which was sent in directional mode) from AP, can have insufficient link budget for sending a response that will be detected by AP in quasi-omni mode.

## Slide 4: Problem statement (2/2)
ISSUE 2: Collision in dense environment
Current 11ad SLS procedure considers no more than 8 SSW slots per A-BFT interval randomly chosen by STAs.
Collision may occur when several DMG STA choose the same SSW slot. The collision probability becomes higher in dense environments considered in 11ay
11ay mitigates this issue by adding new SSW slots in A-BFT for EDMG STAs. However, this may require an excessive number of SSW slots in case of dense environments and does not resolve the coverage issue for large antenna arrays

## Slide 5: Legacy SLS beamforming flow

## Slide 6
Enhanced SLS and channel access for far away STAs

## Slide 7: Proposed enhanced SLS in BTI (1/2)
During the BTI (or several BTI in case of fragmented TXSS) the AP/PCP performs TXSS transmitting DMG Beacon frames through all sectors available, while the responder’s antenna is configured to a quasi-omni pattern
The TRN-R field can be appended to DMG Beacon frame [1][2]
Responder (EDMG STA) receives DMG Beacon frame in quasi-omni mode and uses the appended TRN-R field to train its own antenna pattern, discovering the best RX sector.
[1] 2015-TECH-Intel-0031-01 Enhanced SLS Beamforming Protocol for MIMO in IEEE 802.11ay
[2] 2016-TECH-Panasonic-0022-01-Fast BSS Discovery Recap

## Slide 8: Enhanced SLS in Beamforming training allocation. STA’s responses
DTI
A-BFT
BTI
BTI
DTI
Beamforming training allocation
Directional allocation
Through the (EDMG) Extended Scheduled element, the AP/PCP can allocate a special Beamforming training allocation in the DTI where the following procedure takes place:
AP/PCP configures its RX antenna to directional mode.
AP/PCP repeats the Sector Sweep in the same order as in the BTI but in the RX mode.
Each responding STA transmits one SSW (or Short SSW) frame in the Initiator’s sector detected as the best one during BTI TXSS.
The responder’s transmission is performed in directional mode using the operating sector trained during BTI TRN-R (some level of TX-RX EDMG STA reciprocity is assumed).
To avoid collisions inside one sector, several time slots (space-time slots) may be assinged for responders’ transmissions.

## Slide 9: Enhanced SLS in Beamforming training allocation. STA’s responses
DTI
A-BFT
BTI
BTI
DTI
Beamforming training allocation
Directional allocation
DTI
A-BFT
BTI
BTI
DTI
Directional allocation
Beamforming training allocation
After transmitting the SSW (or Short SSW) frame the responder starts listening in the operating sector.
AP broadcasts a Sector ACK frame in each sector where it detected any STA transmission (energy detection may be enough).
Sector ACK frame should contain the information about every STA which transmission is discovered in this sector and broadcasting instruction for other STAs in this sector.

## Slide 10: Enhanced SLS flow
DTI
A-BFT
BTI
BTI
DTI
Beamforming training allocation
Directional allocation
Far away STAs

## Slide 11: Channel access for far away STAs in directional allocation (1/2)
The far away EDMG STAs, which managed to associate to the AP through the Enhanced SLS, will still have problems with channel access in DTI since STAs (including PCP/AP) normally use quasi-omni mode for receiving.
We propose to use scheduling through the (EDMG) Extended Schedule element to address this issue by introduction of Directional Allocations.
For each allocation in the (EDMG) Extended Schedule element, the PCP/AP may specify the AP’s receive sector that will use to listen during this allocation:
  Hereby, we refer to this as a directional allocation
  The type of the allocation can be either CBAP or SP.
  Any transaction can take place in this allocation, including additional beamforming and data transmission
DTI
A-BFT
BTI
BTI
DTI
Beamforming training allocation
Directional allocation

## Slide 12: Channel access for far away STAs in directional allocation (2/2)
The STAs behavior in allocations, that do not specify a receive sector, remains the same as legacy
STAs can use the information from the (EDMG) Extended Schedule element to decide to communicate with the PCP/AP in the specific directional allocation corresponding to the sector selected in BTI:
  The STA can use the directional allocations in additional to non-directional allocations to perform any transaction
An alternative method is for the PCP/AP use polling in CBAPs/SPs:
  Polling already defined in 11ad
  Has its own pros/cons compared to scheduling
Required changes
Need to modify the (EDMG) Extended Schedule element and add a field to indicate on which sector the PCP/AP will be listening during each allocation.

## Slide 13
Legacy vs. Enhanced SLS comparative analysis

## Slide 14: Evaluation assumptions: Legacy SLS
Simulations consist of different trials (4000 environment snaps) with several consecutive BIs within a trial (25 BIs used).
All stations in the area have data to transmit and compete for the synchronization opportunities in A-BFT of each BI.
Each station randomly (per BI) select SS slot in the A-BFT.
  The R-TXSS (Responder STA TX sector switching) order within SS slot stays the same for all BIs within a trial.
Collision of two or more STAs in the same space-time resource means that all of them miss the current BI transmission.
In case of collision, no more than RetryLim retransmissions allowed in current A-BFT. If the collision was not resolved during RetryLim retransmissions, random BI back-off is selected.

## Slide 15: Evaluation assumptions: Enhanced SLS
For each trial random uniform STA deployment is modeled. The operating sectors are defined for AP and STAs.
To transmit SSW frame, STA selects the space-time slot in Beamforming SP, corresponding to its operating sector:
  If several timeslots are assigned to one AP sector, then STA randomly selects one to transmit the SSW frame
Collision of two or more STAs in the same space-time resource means that all of them miss the current BI transmission.
In case of collision, random BI back-off is selected.

## Slide 16: Evaluation parameters
Legacy
  Baseline: 8 SS slots, with 8 SSW frames (8 sectors per TX STA)
  Retransmissions within A-BFT – 0 or 2 allowed
  Back-off – disabled or 4 BIs
  Increased number of SS slots: 32 SS slots
Enhanced SLS
  256 sectors per TX/RX AP
  0 or 4 timeslots per sector transmission
  Back-off – disabled or 4 BIs
Performance metrics:
  Throughput: the percentage of missed BIs (due to unresolved collisions during SLS)
  Latency: distribution of the data transmission delays (in BIs)

## Slide 17: Legacy-based SLS performance

## Slide 18: Enhanced SLS performance

## Slide 19: Legacy vs. Enhanced SLS comparison
Mode | SLS duration
Legacy: SSslots=8, RetryLim=0 | 5.9 ms. (BTI + A-BFT)
Legacy: SSslots=32, RetryLim=2 | 8.4 ms. (BTI + A-BFT)
Enh.SLS: APsectors=256, Slots per sector=1 | 9.8 ms. (BTI + Beamforming SP)
Enh.SLS: APsectors=256, Slots per sector=4 | 17.4 ms. (BTI + Beamforming SP)

## Slide 20: Coverage analysis: Legacy vs. Enhanced SLS
For AP coverage analysis the free space LOS environment with O2 absorption in 60 GHz band was assumed.
Enhanced SLS enlarges the mmWave coverage exploiting AP large antenna arrays capabilities both in Downlink (AP->STA) and Uplink (STA->AP) operation. The Enhanced SLS coverage is limited only by FCC EIRP constraint (about 270m in DL mode), while Legacy SLS coverage (about 27m) is limited by STA antenna gain and transmit power, which are usually much lower comparing to AP.
Parameter | Value |  |  |  |  |  | 
Number of AP ant. elements | 8 | 16 | 32 | 64 | 128 | 256 | 512
AP transmit power, dBm | 10 | 10 | 13 | 16 | 19 | 22 | 25
Number of STA ant. elements | 8 |  |  |  |  |  | 
STA transmit power, dBm | 10 |  |  |  |  |  | 
Receive sensitivity, dBm | -78 (0 MCS) |  |  |  |  |  | 
Only 27 meters coverage for Legacy SLS
EIRP limit = 43 dBm

## Slide 21: Conclusions based on simulation results
Legacy 11ad approach with 8 SS slots in A-BFT cannot be used for dense scenarios: the BI miss percentage can be up to 60% for 50 STAs in the hotspot area
The BI back-off is inefficient in terms of resource usage in case of low collision probability
Both increased number of SS slots (Legacy-based) or proposed Enhanced SLS provide reasonable 2-3% of BI miss probability in case of dense environment (50 STAs)
The overall SLS duration for the Enhanced SLS approach is comparable with the Legacy-based (on the overall BI length)
The Legacy-based approach with increased number of SS slots may give the same BI miss probability, but only the Enhanced SLS can provide significant coverage increase

## Slide 22: Straw Poll
To deal with asymmetric DMG antenna configurations, the 11ay specification shall define an enhanced SLS protocol that enables beamforming training between an AP or PCP and non-AP or non-PCP STAs that includes the following steps:
adding TRN-R subfields to DMG Beacon frames transmitted in the BTI;
beamforming training between the PCP/AP and non-PCP/non-AP STAs (as shown in slide 8-9);
scheduling of directional allocations in the DTI (as shown in slides 11-12)