## Slide 1: High Level MAC Concept for WUR
Date: 2017-01-12
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com

## Slide 2: Abstract
We consider 3 high level MAC concepts that are essential for WUR

## Slide 3: Enabling WUR Mode and WUR Parameter Negotiation
Define WUR mode request/response frame to enable WUR operation and negotiate parameters for WUR transmission
  For frequency band and channel negotiation
  For STA ID allocation in wake-up packet
  For indication of required time for turning on 802.11 radio
  For indication of periodic WUR receiver on/off schedule
  For other TBD indications
  Define WUR mode element to carry the information and may be carried in other frame exchange
WUR Request
AP
STA
WUR Response

## Slide 4: Integration with Current Power Save Protocols
Enable integration with current power save protocols with little or no change
  Define a signaling for a STA to indicate to an AP when the STA enters a new WUR power-save state (i.e. WUR state)
    WUR state: 802.11 radio is off, WURx is on, and the STA waits for a wake-up packet
    The signaling needs to be differentiated from the indication that the STA simply informs the AP to stop sending packets and enters doze state such as the PM bit
  After the STA receiving a wake-up packet and turning on 802.11 radio, the STA uses the signaling methods defined for the existing power save protocol (e.g. PS-Poll or U-APSD) to solicit packets from the AP
WUR Request
AP
STA
WUR Response
Inform the AP that the STA is entering the WUR state
Wake-up Packet
Data
WUR Signaling
WURx on
802.11 radio on
802.11 off
WURx off
WURx
802.11
802.11 radio on
WURx off
PS-Poll or
Trigger (U-APSD)

## Slide 5: Discussion of Existing Submissions
In [1], WUR request/response is proposed for STA to inform AP that STA turns off 802.11 radio and turns on WUR radio
This is similar to the proposal of WUR signaling with the following difference
  We think the primary usage of WUR request/response is for general parameters/capability exchange and setup
  We think WUR request can be one form of WUR signaling but WUR response may not be required
    Recall that for the current power save protocol, the AP does not send additional response frame except Acknowledgement when the AP receives a packet with PM bit equal to 1 from the STA

## Slide 6: Basic Operation of WUR
Wake-up packet transmission
  An AP transmits a wake-up packet when there is a need to wake up the STA
Acknowledgement
  The AP does not expect immediate acknowledgement from the STA after transmitting the wake-up packet
  Any first packet received from the STA after the wake-up packet transmission is considered as the acknowledgement for the wake-up packet
Retransmission
  After transmitting a wake-up packet, the AP waits for a timeout interval for the acknowledgement, which could be any frame from the STA
    AP can proactively send packets required response to the STA to get acknowledgement (e.g. Trigger frame by 11ax)
  If an acknowledgement is not received before the timeout interval, the AP may retransmit a wake-up packet after the timeout interval
AP
STA
Wake-up Packet
WURx on
Time for turning on 802.11 radio
PS-Poll or
Trigger (U-APSD)
Data
802.11 radio on
802.11 off
WURx off
WURx
802.11
Ex:

## Slide 7: Discussion of Existing Submissions
Proposed basic procedure has been discussed in [1-3] with alternative of immediate response for wake-up packet acknowledgement discussed in [2-3]
  Due to the additional power consumption and cost for enabling transmission capability on non-AP STA, we think the proposed basic procedure fits better with the motivation of TGba
  Stringent latency requirement can be met by enabling repeating transmission of wake-up packet to significantly increase the reliability
  Non-stringent latency requirement can be met by regular wake-up packet retransmission procedure
PER | PER with one repeat | PER with two repeats
0.1 | 0.01 | 0.001
0.2 | 0.04 | 0.008
0.3 | 0.09 | 0.027
0.4 | 0.16 | 0.064

## Slide 8: Conclusion
We consider the following 3 high level MAC concepts that are essential for WUR
  Enable WUR mode and WUR parameter negotiation
  Integration with current power save protocols
  Basic operation of WUR
    Wake-up packet acknowledgement
    Wake-up packet retransmission

## Slide 9: Reference
[1] 11-16-1445-00 Overall MAC Procedure for WUR
[2] 11-16-1460-01 WUR MAC Consideration
[3] 11-16-1470-00 Wake-up and Data Exchange Sequences