## Slide 1: Explanations for CR on 27.5.2.7 NDP feedback report
Date: 2017-01-15
Authors:

## Slide 2: Background (1)
It is well accepted that being able to get a very short simultaneous feedback from a high number of STAs (all STAs) improve the 11ax system and power efficiencies [1], [3]
  Many feedbacks require 1 bit: PS-Poll (power efficiency), Channel Availability (collisions avoidance)
  Other feedbacks could be 2 bit. For example: “How many buffered Bytes for transmission: 0, 1 to 1000, 1000 to 5000, > 5000 ?”
  A short simultaneous resource request feedback (1 or several bits) capable of supporting a high number of STAs is needed for an efficient UL MU simultaneous scheduling in addition to the existing (or enhanced) piggybacked buffer information
  Less overhead for resource request feedback than polling method
  Low and stable latency for resource request feedback, compared to possibly high and unpredictable latency with CSMA-CA in dense environments

## Slide 3: Background (2)
In Nov. 2016, added subclause 25.5.2.7 to the spec: 25.5.2.7 NDP feedback report procedure The NDP feedback report is a mechanism for an HE AP to collect short feedbacks from a very high number of HE STAs, in an efficient manner. The feedbacks (e.g. resource requests) are sent without data payloads in response to a Trigger frame. The feedbacks are not for channel sounding. This mechanism is optional for non-AP STA.
But details of the NDP feedback mechanism are TBD
Contribution 44r0 proposes a signaling technique for the NDP feedback mechanism that can handle a high number of STAs and is power and air time efficient
This contribution proposes to define a new trigger type for NDP feedback report and the procedure for an HE non-AP STA to know, based on the trigger frame, if it can respond and what parameters to use to respond

## Slide 4: How to define the NDP feedback mechanism?
UL MU transmission in response to a trigger frame
Use frequency dimension for many small orthogonal allocations
To avoid collisions, assign orthogonal allocations to users
No data payload (NDP), STAs transmit energy on one orthogonal allocation for feedback
  with spreading gain in time domain for PHY robustness
For minimal changes to the current PHY, we propose
  to use UL MU NDP simultaneous transmissions in response to a trigger frame
  and to define orthogonal allocations (resource block RBs) to multiplex different STAs’ feedbacks
  These orthogonal allocations (RBs) are defined by using different frequency tone sets

## Slide 5: Overview of proposed signaling for Short Feedback
There are 9 RUs of 26 tones in 20 MHz. Each 26 tones RU are sub-divided into four sets of 6 tones.
  6 tones sets are chosen to pack 2 users per 26 tones RU
  6 tones sets have enough frequency diversity per 26 tones RU
One or two bit are assigned to one user feedback response
Two sets of 6 tones are used to transmit 1 bit
Channel estimation is not needed for detection
AP and STAs must have a prior agreement on tone sets and P-matrix spreading to use for a given response

## Slide 6: Proposed feedback schemes
Multiplex different users with P-matrix code (and potentially different tone sets);
Separate different states of the same user with different tone sets.
Two sets of 6 tones are used to transmit 1 bit:
  If bx = 1, send energy on first tone set and quiet on second tone set
  If bx = 0, send energy on second tone set and quiet on first tone set

## Slide 7: Max # of STAs that can simultaneously send the UL Short Feedback
BW | Response = 1 bit |  |  | Response = 2 bit |  | 
 | Nss = 1 | Nss = 2 | Nss = 4 | Nss = 1 | Nss = 2 | Nss = 4
20 MHz | 18 | 36 | 72 | 9 | 18 | 36
40 MHz | 36 | 72 | 144 | 18 | 36 | 72
80 MHz | 74 | 148 | 296 | 37 | 74 | 148
160 MHz | 148 | 296 | 592 | 74 | 148 | 296

## Slide 8: Trigger frame proposal
We propose to define a new trigger type for NDP feedback report
  This is the cleanest solution, as specific common info field parameters are needed for this mechanism and as this mechanism should be generic and work for multiple types of feedbacks
We propose that this trigger type contains all the information so that:
  STAs can know if they are scheduled
  STAs can know on which allocation they can transmit their response
  STAs can know what is the type of feedback that is requested and how many bits for the feedback

## Slide 9: Proposed design for the trigger frame
No per user info field, all information is common
Use information in common info field and trigger dependent common info field.

## Slide 10: Scheduling the STAs
The trigger frame identifies the group of STAs that can respond:
This is done by defining a range of consecutive AIDs, by including in the trigger frame:
  AID start
  And the parameters to know how many AIDs are scheduled (NAIDs)
The STAs whose AID is between AID start and AID start + NAIDs are scheduled
This allows:
  Unique allocation per AID
  No need for assigning the allocation in a static manner with any other frame exchanges
  AID start allows to define different groups of STAs and target the AID range that associated STAs are using

## Slide 11: Deriving parameters for transmission of the response
The response follows the UL MU operation
The parameters of the trigger-based PPDU are derived from the trigger frame, especially each AID has a unique combination of:
  RU allocation
  RU tone set
  NUM_STS
These are calculated based on AID and parameters from trigger frame: feedback size, BW, number of users per set of tones and RUoffset
The RUoffset enables to rotate the users on the different RUs so that they don’t experience always the same channel conditions.

## Slide 12: Power control
TargetRSSI is included in the trigger dependent common info field
This enables power control with the same target for all STAs

## Slide 13: Feedback types
We propose to define types of feedback, and a field to identify the type
We define the resource request type
Based on the PHY design under consideration, we can have 1 or 2 bits of feedback. We propose to define the meaning of each bit value.
b0 Value | Description
0 | Resource request with buffered bytes for transmission between 1 and 200
1 | Resource request with buffered bytes for transmission above 200
b0 Value | b0 Value | Description
0 | 0 | No resource request
0 | 1 | Resource request with buffered bytes for transmission between 1 and 200
1 | 0 | Resource request with buffered bytes for transmission between 201 and 3000
1 | 1 | Resource request with buffered bytes for transmission above 3000

## Slide 14: Summary
We propose to progress on the definition of the NDP feedback report procedure
  New trigger type
  Parameters to identify the scheduled STAs
  Parameters for scheduled STAs to derive the parameters for the response
  Resource request type

## Slide 15: Straw Poll 1
Do you agree to modify the spec following the comment resolutions in document 17-073r0?

## Slide 16: Straw Poll 2
Do you agree to define a new NDP feedback report trigger frame variant and that the STAs scheduled by a NDP feedback report trigger frame variant are identified by a list of AIDs:
  This list of AIDs is defined to be between AID start and AID start + NAIDs
  The trigger frame includes the AID start parameter and the needed parameters to calculate NAIDs

## Slide 17: Straw Poll #3
Do you agree that the RU allocation, RU tone set allocation and starting_STS_num for the NDP feedback response from an HE non-AP STA are calculated based on common parameters in the new NDP feedback report trigger frame variant

## Slide 18: References
[1] IEEE 802.11-16/1367r0: NDP feedback report
[2] IEEE 802.11-15/1334r1: HE-LTF sequence design
[3] IEEE 11-17-0044-00-00ax-NDP short feedback design