## Slide 1: SRP-based SR Summary and Update
Date: 2017-1-16
Authors:
Name | Affiliation | Address | Phone | Email
James Wang | Mediatek |  |  | James.wang@mediatek.com
Ron Porat | Broadcom |  |  | Ron.porat@broadcom.com
Matt Fischer | Broadcom |  |  | Matthew.fischer@broadcom.com
Yongho Seok | Newracom |  |  | Yongo.seok@newracom.com

## Slide 2: Outline
This document provides a high level summary of the proposed SRP based SR solution for 11ax
Document 1476/09 provides the full set of details.

## Slide 3: SRP-Based SR Concept Re-cap
11ax SR STA identifies SR Opportunities from a RXVECTOR parameter SPATIAL_REUSE and/or contents of a trigger frame MPDU from a received PPDU(s)
The 11ax STA is allowed to initiate an SR transmission for the duration of an ongoing PPDU if the following SRP conditions are met:
    within a SR decision window, verification of the received PPDU is from an OBSS
    an SR PPDU is queued for transmission at the SR STA
    medium contention follows the SRP_PPDU-based spatial reuse backoff procedure
    employs an adjusted transmit power level, designed to avoid interfering with the reception of the ongoing PPDU at the recipient, for the SR transmission

## Slide 4: SRP Proposed Solution
Currently the SRP field exists in all preamble formats but is defined only for trigger based transmission
Our goal is to provide maximum utilization of this feature with minimum implementation impact, maintaining simplicity of the solution while still enabling 11ax deployments to fully benefit from this new information in every packet header.
Two more cases are added:
  SRP in UL transmissions – this is similar in concept to trigger based SRP with the trigger frame replaced by beacons – STA measure the path loss to the recipient (AP) based on hearing beacons (requires minimal memory)
  SRP in DL transmission – this is limited two fold:
    Only AP can take advantage
    Can only be based on min. path loss to the entire BSS
    So effectively this is a form of AP coordination where AP (especially in managed networks) transmit based on the principle of avoiding interference to entire OBSS

## Slide 5: Trigger Frame and HE Trigger-Based PPDU
SR Opportunity identified from a trigger frame or from a HE-trigger-based PPDU
UL STA
AP
SR initiator
OBSS
Transmission
SR responder
HE Trigger-Based PPDU
DSRP_PPDU
HE Trigger-based PPDU
Duration from Common Info field
TSRP_PPDU (HE trigger based PPDU)
Duration from LSIG
Idle
Trigger frame MPDU
Trigger Frame
TX PowerSR Initiator < SRP – RSSItrigger frame
TX PowerSR Initiator < SRP – minimum RX sensitivity
(AP out of range)

## Slide 6: UL HE SU PPDU or HE MU PPDU
SR Opportunity identified from an uplink HE SU PPDU or HE MU PPDU
UL STA
AP
SR initiator
OBSS
Transmission
SR responder
HE UL SU PPDU or HE MU PPDU
ULSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
TX PowerSR Initiator < SRP – highest received power level of all beacons of the same BSS color received within the previous 100ms

## Slide 7: DL HE SU PPDU or HE MU PPDU
SR Opportunity identified from a downlink HE SU PPDU or HE MU PPDU
SR Initiator is restricted to AP only
AP
Non-AP STA
AP (SR initiator)
OBSS
Transmission
SR responder
HE SU PPDU or HE MU PPDU
DLSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
TX PowerSR Initiator < SRP – highest received power level of all OBSS PPDUs of the same BSS color received during the previous 500 ms

## Slide 8: Summary
This document and the accompanying detailed description in document 1476/09 provide the complete definition of our proposed SRP based solution for 11ax
The SRP field provides a uniquely new accurate information on the links in a specific deployments that enables optimization and maximization of the spatial reuse especially in managed networks (enterprise, stadium)