## Slide 1: SRP-Based SR Operation
Date: 2017-01-15
Authors:

## Slide 2: Abstract
An overview of the SRP Based Spatial Reuse Mechanism
Details of the SRP Based Spatial Reuse mechanism are found in:
Document 11-16-1476r14
CID too many to mention …

## Slide 3: SRP SR Basic Operation
HE SRP Capable STA identifies an SR Opportunity from an SRP PPDU:
  RXVECTOR parameter SPATIAL_REUSE and/or
  Trigger Frame Common Info Spatial Reuse field
The HE STA is allowed to initiate an SR Transmission for the duration of the ongoing SRP PPDU (SRP Opportunity) if the following SRP conditions are met:
  within a preceding SRP Decision Window, a reverse direction PPDU is detected with the same OBSS Color
    Allowing SR Transmission interference to be estimated
  an SR PPDU is queued for transmission at the SR STA
  Backoff reaches zero during the SRP Opportunity
    To reduce the probability of SR Transmitter collisions
  Transmit power level is adjusted to meet the SRP parameter condition so that interference at the ongoing receiver location is avoided

## Slide 4: Current Status (D1.0)
Spatial Reuse field exists
  In HE SIGA field of all HE PPDU formats
  In Trigger frame Common Info field
Spatial Reuse field contents defined
  For just a few cases
  Need to complete the transmission content behavior description
Some Spatial Reuse values undefined
  SR_DELAY, SR_RESTRICTED – mentioned, but value not defined
Recipient behavior not described
  Need definition of behavior

## Slide 5: Basic Case Description First
I.e. Trigger and trigger-based PPDU sequence
  This is the simplest, basic case
  Following description of components of SRP will refer to this case
  SRP components include:
    Transmitter SRP field contents (slide 6,7)
    Behavior for recipient of PPDU, based on SRP field contents
      Rules for determining when an SR Transmission can be made (slide 8)
      TX Power for SR transmitter (slide 8)
      Backoff for SR transmitter (slide 9)
      Duration of SR transmission when allowed (slide 10)
      Acknowledgement transmission rules (slide 11)

## Slide 6: SRP Field for Transmitter Trigger (1)
DSRP_PPDU
  Definition: PPDU which contains at least one Trigger MPDU
DSRP_PPDU SIGA SRP field:
  SR_DELAY = recommended value
    Lets recipient know that a trigger MPDU with full SRP parameter values is present in the payload
  Numerical value ok
    TXPower + Acceptable Receiver Interference
    E.g. allows SRP during trigger PPDU, e.g. Trigger+DATA
  SR_DISALLOW ok, prevents SRP on the Trigger PPDU, but does not prevent SRP during the following trigger-based PPDU

## Slide 7: SRP Field for Transmitter Trigger (2)
Trigger MPDU Common Info Spatial Reuse field:
  Numerical value
    TXPower + Acceptable Receiver Interference
    AP dictates Target RSSI for Trigger-based PPDU(s) that are response(s) to the Trigger
    AP dictates the MCS for all Trigger-based PPDUs
    AP knows current interference level at the AP location
    Therefore, AP can calculate expected SINR of Trigger-based PPDU
    AP can place this “acceptable receiver interference” into the Trigger MPDU Common Info field, UL Trigger-based PPDU responders will copy the SRP value from the Trigger Common Info into the UL Trigger-based PPDU PHY SRP field
  Never SR_DELAY
  SR_DISALLOW ok

## Slide 8: SR STA SRP Check
  SR STA definition: a STA that receives DSRP_PPDU
  Must determine if an SRP Opportunity exists
  Assume that SIGA SRP = SR_DELAY
  SR STA decodes payload, finds Trigger, examines Spatial Reuse field in Common Info
    Numerical value means SRP Op is possible if conditions can be met
    SR STA checks TX Power condition based on measured RSSI of DSRP_PPDU, assumes reciprocal path loss
    I.e. if AP transmitted Trigger was received at SR STA location with RSSI of X, then SR STA assumes that SR STA transmission would arrive at AP location with RSSI of X
    Therefore, SR STA can determine estimated level of interference with Trigger-based PPDU, for any given TX power
    SRP parameter in Trigger-based PPDU provides maximum interference allowed

## Slide 9: SR STA Backoff
If Interference condition can be met by SR STA upon transmission
  Backoff must be performed
  Multiple SR STA might exist, without backoff, they would transmit simultaneously
  Backoff is just continuation of existing backoff
    Simple, and reflects fact that even under non-SRP conditions, different STA will see different Medium Condition and count different backoff countdown

## Slide 10: SR STA SR Transmission
If backoff expires, SR STA transmits, provided that the transmission does not exceed the duration of the SRP PPDU
  To decode Trigger Common Info field, full PPDU has been decoded and medium is BUSY for the duration of the DSRP_PPDU
    Rules proposed make this explicit
  I.e. backoff will not expire until sometime during the Trigger-based PPDU transmission
    PHY Header of Trigger-based PPDU must be received first
    Confirmation of COLOR of DSRP_PPDU and Trigger-based PPDU occurs

## Slide 11: SR PPDU Acknowledgement
Acknowledgement of SR PPDU can cause interference
  Acknowledging STA must check local SR conditions before responding
  Normal ACK ignores all medium indications
  Responding STA must be able to distinguish SR PPDU from Normal PPDU
    Need indication within transmitted SR PPDU that it is an SR PPDU
    Provided within A-Control
  Recipient must check SR condition locally before deciding to respond with ACK to avoid causing interference to reception of original Trigger-based PPDU

## Slide 12: DSRP_PPDU and Trigger-based PPDU
SR Opportunity from DSRP_PPDU
AP
SR initiator
BSS_B
SR responder
HE Trigger-Based PPDU
DSRP_PPDU
HE Trigger-based PPDU
Duration from Common Info field
Trigger frame MPDU
Trigger Frame
TX PowerSR Initiator < SRP – RSSItrigger frame
BSS_G
Non-AP STA
Trigger must appear SIFS before the HE trigger-based PPDU. Margin for SIFS is allowed by defining a quantity that is the SRP Decision Window.

## Slide 13: TSRP_PPDU, Trigger not Identified
SR Opportunity from TSRP_PPDU
AP
SR initiator
SR responder
HE Trigger-Based PPDU
IDLE or PPDU with same Color
Trigger Frame
TX PowerSR Initiator < SRP – INTFlevel
HE Trigger-based PPDU
Duration from LSIG
If preceding PPDU detected with same Color, not identified as Trigger, e.g. SR parameter not SR_DELAY and payload not correctly decoded, INTFlevel = RSSIPPDU
If a preceding PPDU (within ~ SIFS) with same Color IS identified as Trigger, then the case is DSRP_PPDU
If IDLE detected before TSRP_PPDU, INTFlevel = MEAS_PWRMAXIMUM where MEAS_PWR is the power measured during the idle time
PPDU
BSS_B
BSS_G
Non-AP STA

## Slide 14: UL HE SU PPDU or UL HE MU PPDU (1)
SR Opportunity identified from an uplink HE SU PPDU or HE MU PPDU
HE UL SU PPDU or HE MU PPDU
ULSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
TX PowerSR Initiator < SRP – highest received power level of all beacons of the same BSS color received within the previous 100ms
Given that PPDU is UL, then the intended recipient is an AP – if we can identify the AP by color and if we have observed a Beacon corresponding to this AP, then we can estimate SR STA interference
IDLE
IDLE
BSS_B
BSS_G
SR initiator
SR responder
Non-AP STA
AP

## Slide 15: UL HE SU PPDU or UL HE MU PPDU (2)
SR Opportunity identified from an uplink HE SU PPDU or HE MU PPDU
HE UL SU PPDU or HE MU PPDU
ULSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
TX PowerSR Initiator < SRP – INTFlevel
Given that PPDU is UL, then the intended recipient is an AP –use preceding PPDU to estimate SR STA interference to AP recipient – preceding in the SRP Decision Window ~= SIFS
CTS, BA, ACK or PPDU with same Color
PPDU
If preceding PPDU has same Color or is CTS, BA or ACK, then INTFlevel = RSSIPPDU
Response Frame
BSS_B
BSS_G
SR initiator
SR responder
AP
Non-AP STA

## Slide 16: DL HE SU PPDU or HE MU PPDU
SR Opportunity identified from a downlink HE SU PPDU or HE MU PPDU
SR Initiator is restricted to AP only
DL HE SU PPDU or HE MU PPDU
DLSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
CTS
PPDU
TX PowerSR Initiator < SRP – INTFlevel
If preceding PPDU is CTS, then INTFlevel = RSSIPPDU
CTS provides estimate of SR STA interference to DL receipient – SR TX not allowed if CTS is not present – i.e. not ending in the SRP Decision Window ~= SIFS
BSS_B
BSS_G
AP = SR initiator
SR responder
AP
Non-AP STA
CTS

## Slide 17: Precedence of SRP vs OBSS PD SR
OBSS PD is based on an assumption
  That the average intra-BSS path power is greater than the average inter-BSS path power
  Average assumed is not always true
  Degree of failure of assumption unknown
SRP provides measured information on an active link
  Uses measured path power to estimate interference
  Does not rely on global average assumptions
  Information is known, interference is estimable
Whenever SRP information is available and STA is capable, OBSS_PD should be DISABLED

## Slide 18: Straw Poll 1
Do you support the use of SRP in the DSRP_PPDU case, i.e. Trigger followed by UL Trigger-based PPDU?
  Y
  N
  A

## Slide 19: Straw Poll 2
Do you support the use of SRP in the TSRP_PPDU case, i.e. HE Trigger-based PPDU preceded by IDLE or by PPDU with color match of Trigger-based PPDU?
  Y
  N
  A

## Slide 20: Straw Poll 3
Do you support the use of SRP in the ULSRP_PPDU case 1, i.e. HE UL SU PPDU or HE UL MU PPDU preceded by IDLE?
  Y
  N
  A

## Slide 21: Straw Poll 4
Do you support the use of SRP in the ULSRP_PPDU case 2, i.e. HE UL SU PPDU or HE UL MU PPDU preceded by CTS, BA or ACK, or by PPDU of same color as HE UL SU PPDU or HE UL MU PPDU?
  Y
  N
  A

## Slide 22: Straw Poll 5
Do you support the use of SRP in the DLSRP_PPDU, i.e. HE DL SU PPDU or HE DL MU PPDU preceded by CTS and only allowed for AP?
  Y
  N
  A

## Slide 23: Straw Poll X
Do you support the adoption of 11-16-1476r17 as the resolution for CIDs related to SRP?
  Y
  N
  A