## Slide 1: Broadcast TWT TIM
Date: 2017-01-16
Authors:

## Slide 2: Abstract
Coordinated MU DL and Triggered MU UL are the first step toward a more scheduled behavior in 802.11
The inclusion of such scheduling is intended to make 802.11 systems more well behaved
  E.g. fewer collisions, less MAC overhead
Alignment between MU DL, MU UL and PS wake times is the next step forward for power savings
TWT should be used for aligning PS STA wake times with MU DL and MU UL operations
TIM Use for BTWT is defined, but has problems

## Slide 3: CID 8108
Broadcast TWT - a non-AP STA that is participating in Broadcast TWT will wake for TWT SPs and then check trigger frames to see if the STA is identified in a trigger. If there is more than one trigger for an SP, the STA will wake for multiple triggers and by the end of the SP, it is possible that the STA has not been identified and therefore, has wasted power checking each trigger. It would be more efficient for power consumption if the STA had a clue as to whether any trigger in the SP was going to identify it. | Add a TIM of some sort to be associated with each Broadcast TWT so that a participating STA can wake at the beacon and read the TWT-TIM to see if it should be waking for any of the triggers associated with this broadcast TWT within this beacon interval. The TIM could also be included at the start of each TWT SP, say, within a beacon-like frame, e.g. measurement pilot frame or something else.

## Slide 4: TIM for Trigger Frame is Not Well-Coordinated
Trigger frames today:
  Trigger frame timing is indicated in Beacon with Broadcast TWT
    Provides timing of major trigger phase sequences
    Cascade Indication used to indicate the presence of additional “minor” triggers within a sequence
  A STA waking to find Broadcast trigger frame indication(s) in the Beacon cannot know if the triggers for any particular time will include this STA
    Opportunistic Power Save defines use of TIM at start of BTWT SP
    PS STA must wake for start of every BTWT SP to see if it is named
    With each BTWT, PS STA is waking unnecessarily as it is unlikely to be named as a triggered/served STA in all BTWT

## Slide 5: 27.14.3.1 AP operation for opportunistic power save
Opportunistic power save mechanism has the objective for an AP to split a beacon interval into several periodic broadcast TWT SPs and to provide, at the beginning of each SP, the scheduling information to all non-AP STAs. Based on this information, the non-AP STAs may opportunistically go to doze state until the next TWT SP.
This is still not as efficient as desired and has some technical problems as described next:

## Slide 6: Problem 1
When exactly, does the TIM appear?
  D1.0 says “at the beginning of each SP”
  BTWT periodicity can be < BI
  So, which Trigger is the TWT SP start?
  First Trigger after Beacon?

## Slide 7: Problem 2
BTWT ID values
  0 = all STA
  Non-zero = per STA signup
Possible need for more than one “all STA” BTWT

## Slide 8: Problem 3
STA wake times:
  Typically, a STA already wakes at TBTT for Beacon reception
  Current language suggests that STA must:
    Wake for TBTT to check BTWT IE values in Beacon
    Then schedule additional wake times for all beginning BTWT SP to find TIM for each one
    The more the BTWT indicated, the more the wake requirement
  Would be nice to find all BTWT information at this one wake time
  STA can then schedule future wake times

## Slide 9: Problem 4
For any HE non-AP STA for which their associated AP set their corresponding bit in the traffic indication virtual bitmap field of the TIM element to 0, the AP shall neither send unicast or multicast frames to those STAs, nor trigger those STAs for UL MU transmissions during the TWT SP and, unless otherwise specified, until the next TWT SP.
Difficult to enforce the multicast provision, because multicast group membership determination is above L2

## Slide 10: Problem 5
How long is the TIM indication valid?
  There is a series of Triggers for each BTWT
  When does a STA need to check for a new TIM?
  i.e. when is the next “start” of this SP?

## Slide 11: Proposed Change
Add STA bitmap to Broadcast TWT
  To allow PS STA to efficiently wake and sleep

## Slide 12: Additional Information for PS STA
For improved PS operation
Add STA list to Broadcast TWT indication
  Add list of STA that might be addressed by a trigger in the Broadcast TWT indication
    E.g. a bitmap, reuse the TIM format
  Add an indication that the list is present
    Add a bit to the TWT control field “TWT Bitmap Present”
  A STA not listed in the bitmap is guaranteed to not be triggered
    And therefore may choose to doze during that trigger period
  A STA listed in the bitmap might be triggered
    And therefore should be awake during that trigger period

## Slide 13: Modified TWT Information Element
TWT TIM optionally added to TWT IE
TWT TIM length indicates length of TWT TIM Bitmap Control plus Partial Virtual TWT Bitmap
TWT TIM is a subset of TIM IE
 | Element ID | Length | Control | Request Type | Target Wake Time | TWT Group Assignment | Nominal Minimum Wake Duration | TWT Wake Interval Mantissa | Broadcast TWT ID | TWT Channel | NDP Paging (optional) | TWT TIM
Octets: | 1 | 1 | 1 | 2 | 8 or 0 | 9 or 3 or 0 | 1 | 2 | 0 or 1 | 1 | 0 or 4 | 0 or variable
 | TWT TIM Length | TWT TIM Bitmap Control | Partial Virtual TWT TIM Bitmap
Octets: | 1 | 1 | variable

## Slide 14: TWT TIM Present Indication
TWT IE Control Field is modified to include a TWT TIM Present bit
If TWT TIM Present = 1, TWT TIM included in the TWT IE
  Length, Bitmap Control, Partial Virtual Bitmap
If TWT TIM Present = 0, no TWT TIM present in the TWT IE
 | B0 | B1 | B2 | B3 | B4 | B5 B7
 | NDP Paging Indicator | Responder PM Mode | Broadcast | Wake TBTT Negotiation | TWT TIM Present | Reserved
Bits: | 1 | 1 | 1 | 1 | 1 | 3

## Slide 15: TWT TIM Fields
TWT TIM Length
  Length of the TWT TIM Bitmap Control and Partial Virtual TWT TIM Bitmap fields
TWT TIM Bitmap Control
  Similar interpretation as TIM IE Bitmap Control field
    Bit 0 = Identification of Broadcast TWT SP
      When bit 0 = 1, the associated TWT SP is broadcast – i.e. the TWT SP is for all associated STAs
    Bits 1 through 7 are the same as TIM Bitmap Control, defining the bitmap offset
Partial Virtual TWT TIM Bitmap
  Same definition as TIM IE Partial Virtual Bitmap

## Slide 16: Straw Poll 1
Do you support a modification that optionally allows a TWT TIM field as defined in slides 13, 14, 15 to be included as part of the TWT IE?
  Yes
  No
  Abstain

## Slide 17: References
[1] 802.11-2016.pdf
[2] Draft P802.11ax_D1.0.pdf