## Slide 1: Channel Width Selection Within TXOP
Date: 2017-1-14
Authors:
Name | Affiliation | Address | Phone | email
Oren Kedem | Intel | Israel | +972-3-9205787 | Oren.Kedem@intel.com

## Slide 2: Terminology
Non-EDMG duplicate format – duplicated 2.16GHz PPDU transmitted over multiple bands.
Channel Width information – Indicate which channels are being occupied by PPDU either EDMG PPDU or in non-EDMG duplicate PPDU transmission.

## Slide 3: Purpose and definitions
Present the implications of available options for TXOP Owner to set/change PPDU channel width during TXOP.
Provide recommendation for the above rules

## Slide 4: PPDU Channel Width Alternatives
What are the TXOP Owner options to set the PPDU channel width during TXOP ?
Options are ?
  Remain constant throughout the TXOP as indicated in the Channel BW subfield in the DMG CTS that establishes the TXOP
  PPDU Channel Width during TXOP could be reduced.
  PPDU Channel Width during TXOP could be increased

## Slide 5: Channel Width Information
Current SFD supports the below
EDMG Frames carry the Channel Width information via the Compressed BW subfield in L-Header or BW subfield in A-Header.
RTS, DMG CTS, DMG DTS and DMG CTS-to-Self are transmitted in non-EDMG duplicate format and has channel width indication (Channel BW subfield in L-Header).
Other PPDUs transmitted in non-EDMG duplicate format doesn’t carry the Channel Width information.
  For example, EDMG STA that receives DMG BlockAck cant know its channel width since it may be:
    Transmitted as single channel PPDU
    Transmitted in several channels in non-EDMG duplicate format.

## Slide 6: CCA consideration
For robust CCA sensing, both peers should transmit with the same Channel Width
Below rule is already motioned in SFD
  An ACK or BlockAck frame shall be sent over a Channel width equal to the channel width of the frame the ACK or BA are sent in response to
The above rule should be generalized and extended:
  A PPDU sent as response to a frame within TXOP, shall be sent over the same channel width of the frame it sent in response to.
TXOP Responder shall keep the same channel width of the TXOP owner when responding or when utilizing Reverse Direction

## Slide 7: Reducing channel width
TXOP Owner may want to reduce its channel width as result of interferences it encounters on secondary channels.
  Since in that case both the interferer and the interfered are experiencing bad performance.
  Reducing the Channel Width can be done independently by the station as long it signals the new Channel Width in transmitted PPDU
  Third station who sets its NAV according to RTS/CTS on secondary will not be aware of the termination of the NAV due to the reduction of Channel Width
  However, DMG PPDUs transmitted in non-EDMG duplicate format doesn't carry the channel width information to the peer.
  SFD should allow STA to reduce the channel width during TXOP

## Slide 8: Alternatives
Issue to be addressed
If TXOP Owner reduces its channel width when it transmits a non-EDMG duplicated frames, the responder could not know which channel width it should utilize in its response
Alternative 1:
  Extend the L-Header definition to include Channel Width in non-EDMG duplicate format for all frames.
Alternative 2:
  Limit the EDMG STA not to reduce its PPDU channel width in case PPDU is transmitted in non-EDMG duplicate format.

## Slide 9: Alternative 1
Extend the L-Header definition to include Channel Width for PPDUs transmitted in non-EDMG duplicate format.
CPHY PPDU
  Same as in RTS/CTS, reserved bits 22 and 23 shall be both set to 1 and the Scrambler Initialization field shall include the Channel BW field as indicate in SFD.
SC PPDU
  Frame should keep its compatibility format (Length fields should not be changed).
  Need additional Reserve bit to indicate new definition of L-Header for non-EDMG duplicate mode
  Last-RSSI subfield shall indicated the Channel BW information in case reserved bit 47 is set.
Since this option require the use of additional Reserve bit, it is less recommended

## Slide 10: Alternative 2
Since a responder of a frame should know the channel width of the received frame (CCA reasons):
  TXOP Owner wishes to reduce the PPDU channel width during TXOP, shall reduce it only when it transmits EDMG PPDU.
  Reducing the PPDU channel width shall not be done on DMG frames sent in non-EDMG duplicate format.

## Slide 11: Increasing channel width – consideration
TXOP Owner may want to increase its channel width to get more throughput, however;
  Sensing the Secondary while receiving in Primary is not reliable due to AGC activated on Primary. (Secondary may be attenuated)
  Current channel access defines that grabbing the secondary could be done only with both peer CCA not busy.
  Only method to negotiate the channel width is via RTS/DMG-CTS exchange.
  There are no means for a station to increase its current Channel Width independently (i.e. no responder CCA on secondary).
  In case TXOP Owner wants to increase the TXOP channel width it should initiate additional RTS/DMG CTS in the TXOP

## Slide 12: Additional RTS/CTS exchange

## Slide 13: Increasing channel width - constraints
In case TXOP channel width is increased with additional RTS/CTS exchange, the following should be required
  Additional RTS/DMG CTS during TXOP shall exploit only the rest of the TXOP duration.
  Additional RTS/DMG CTS sent during TXOP shall be sent after CCA sensing during PIFS time on secondary channels and shall be capped with the Channel Width achieved by the first RTS/CTS that establishes the TXOP
  TXOP Responder is required to be ready on performing CCA sensing while on receive during TXOP on all channels indicated in the RTS that establishes the TXOP.
  Allowing the TXOP Owner to increase its channel width result with:
    Tight constraints on the responder CCA
    Not efficient as it requires RTS/CTS renegotiation
    Risk the TXOP since it require non active time of PIFS.
In result of the above, allowing TXOP Owner to increase the TXOP Channel Width is not recommended.

## Slide 14: Summary and recommendation
Same as in 11ac, we recommend to allow TXOP Owner to reduce its Channel Width during TXOP but not allowing it to increase it.
TXOP Owner shall reduce the PPDU Channel Width only with EDMG PPDU to enable the Channel Width information to be delivered to the TXOP Responder.

## Slide 15: Motions
Do you agree to include in SFD the following:
  TXOP Owner may reduce the PPDU occupied channel width only when transmitting EDMG PPDU.
  A TXOP owner shall not increase the PPDU occupied channel width within the same TXOP.
15

## Slide 16: Backup

## Slide 17: Alternative 1 - Details
  SFD shall extend the CPHY L-Header definition by setting the reserved bits 22 and 23 both set to 1 and the Scrambler Initialization field to include the Channel BW field to all DMG frames transmitted in non-EDMG-duplicate format
SFD shall allocate Reserve bit 47 to indicate the existence of Channel BW subfield in the L-Header Last RSSI subfield as described below.
17
SC L-Header Bit field |  |  |  |  |  | Definition
Reserve bit 46 | Reserved bit 47 | Last RSSI subfield |  |  |  | 
 |  | B0 | B1 | B2 | B3 | 
0 | 0 | Last RSSI |  |  |  | DMG PPDU frame format
0 | 1 | Reserved | Channel BW |  |  | Non-EDMG Duplicate Format When Reserve bit 47 is set, 3 LSB includes the Channel BW field indicates the bandwidth of the PPDU as defined in Table 5.
1 | 0 | IsSC | IsSiso | GI/CP Length |  | EDMG PPDU frame definition
1 | 1 | Reserved |  |  |  |