## Slide 1: Utilization of the Ack Type Subfield in a Multi-STA BlockAck Frame
Date: 2017-01-16
Authors:

## Slide 2: Introduction
We have discussed the issue that arises from the long length of the multi-STA BlockAck frame.
  To reduce the length of the frame, we adopted the function to omit the Block Ack Starting Sequence Control and the Block Ack Bitmap subfields using the Ack Type subfield.
Only when all MPDUs in an A-MPDU are successfully received, the Block Ack Starting Sequence Control and the Block Ack Bitmap subfields can be omitted.
  If the reception of one MPDU fails, all Per STA Info subfields in the multi-STA BlockAck frame should include its Block Ack Starting Sequence Control and Block Ack Bitmap subfields.
  This is because MPDUs of multiple TIDs can be in any order in an A-MPDU and the recipient does not know which TID of an MPDU is included in the A-MPDU.
This contribution proposes a condition to utilize the Ack Type subfield to reduce the length of the multi-STA BlockAck frame.

## Slide 3: Multi-STA BlockAck frame [1]
When the Ack Type subfield is 1, the corresponding Block Ack Starting Sequence Control and the Block Ack Bitmap subfields are not present.
Ack Type 1 contexts
  TID < 8 or TID = 15
    Acknowledges successful reception of a single MPDU
  TID = 14
    Acknowledges successful reception of all MPDUs in the eliciting A-MPDU
 | Per AID TID Info | Block Ack Starting Sequence Control | Block Ack Bitmap
Octets: | 2 | 0 or 2 | 0, 4, 8, 16 or 32
 | B0 B10 | B11 | B12 B15
 | AID | Ack Type | TID
Bits: | 11 | 1 | 4
* Per STA Info field format

## Slide 4: Multi-TID A-MPDU [1]
When constructing a multi-TID A-MPDU
  A multi-TID A-MPDU may contain multiple A-MPDU subframes with the EOF subfield set to 1 and the MPDU Length subfield set to nonzero value.
  If the QoS Data frame or Action frame solicits an immediate Ack frame, the EOF subfield shall be set to 1 in a nonzero length MPDU delimiter that precedes the QoS Data frame or Action frame.
When receiving a multi-TID A-MPDU
  An HE STA shall respond with a Multi-STA BlockAck frame that contains
    Per STA Info field indicating an Ack (Ack Type: 1)
      For each successfully received MPDU that is preceded by an MPDU delimiter whose EOF is 1
    Per STA Info field indicating a BlockAck (Ack Type: 0)
      For each TID of a successfully received MPDU that is preceded by an MPDU delimiter whose EOF is 0

## Slide 5: Utilization of the Ack Type subfield (1)
It is implied that the TID of an MPDU with the EOF subfield set to 1 is unique in an A-MPDU.
The MPDU delimiter and the MPDU each can be checked using the CRC and FCS fields, respectively.
If the unsuccessful MPDU has the corresponding EOF subfield set to 1, it is certain for the recipient that it received all other MPDUs of different TIDs except the unsuccessful MPDU.
MPDU
(TID: 1)
MPDU
delimiter
EOF: 0
MPDU Length: nonzero
A-MPDU
A-MPDU subframe
MPDU
(TID: 1)
MPDU
delimiter
…
MPDU
(TID: 2)
MPDU
delimiter
MPDU
(TID: 2)
MPDU
delimiter
…
MPDU
(TID: 3)
MPDU
delimiter
EOF: 1
MPDU Length: nonzero

## Slide 6: Utilization of the Ack Type subfield (2)
Therefore, the recipient can send a multi-STA BlockAck frame without the Block Ack Starting Sequence Control and Block Ack Bitmap subfields.
For example,
MPDU
(TID: 1)
MPDU
delimiter
EOF: 0
MPDU Length: nonzero
A-MPDU
A-MPDU subframe
MPDU
(TID: 1)
MPDU
delimiter
…
MPDU
(TID: 2)
MPDU
delimiter
MPDU
(TID: 2)
MPDU
delimiter
…
MPDU
(TID: 3)
MPDU
delimiter
EOF: 1
MPDU Length: nonzero
MAC
Header
BA Control
Per AID TID Info
(TID: 1)
Block Ack Starting Sequence Control
Block Ack Bitmap
Per AID TID Info
(TID: 2)
Block Ack Starting Sequence Control
Block Ack Bitmap
* Current acknowledgment
MAC
Header
BA Control
Per AID TID Info
(TID: 1)
Per AID TID Info
(TID: 2)
* Proposed acknowledgment

## Slide 7: Discussions
A STA that has the All Ack Support capability also has the capability to receive the multi-STA BlockAck frame of the proposal.
The proposed utilization of the Ack Type subfield can be additionally used to reduce the length of the multi-STA BlockAck frame.

## Slide 8: References
[1] Draft P802.11ax D1.0

## Slide 9: Straw Poll
Do you agree with the scheme to reduce the length of the multi-STA BlockAck frame in this submission?
  Y
  N
  A