## Slide 1: HE-FTM Measurement Phase
Date: 2016-10-24
Authors:

## Slide 2: Abstract
We present a TDMA based sounding which allowed a large number of STAs to perform range measurement while taking advantage of the full available BW, allowing MIMO and avoiding the near far problem of using the P-matrix.

## Slide 3: Sounding Phase Protocol Design Considerations
Design considerations for any ranging protocol
  Operate in the MU mode to allow efficient medium usage by having large number of STAs to range using the same TF and DL NDP without performance degradation as in other methods.
  Full BW measurement - Accuracy is highly dependent on the BW
  Minimize the multi-path induced errors by making use of all transmission chains (MIMO)
  Insensitive to the near-far problem by avoiding mixing the Tx chains of different STAs in the same symbol interval (P-matrix multiplexing within the single STA)

## Slide 4: Suggested FTM Measurement phase – with staggered NDP
NDP
SIFS
SIFS
Staggered NDP
Trigger
Frame
SIFS
Responder
or AP
STA
1
STA
2
STA
3
NDP
SIFS
NDP
SIFS
NDP
NDPA
SIFS

## Slide 5: HE-FTM Measurement
Each STA sends an NDP
    Insensitive to the near-far problem by avoiding mixing of Tx chains from different STAs in the same symbol interval (P-matrix multiplexing limited to a single STA)
    Lower overhead as a single TF and single DL sounding NDP are used by a large number of STAs.
The order of NDPs is set by the AP in the trigger frame
AP sends a single NDP frame to all STAs

## Slide 6: Concerns about Staggered NDP
The staggered uplink sounding NDP transmission will require the STAs to take turns to occupy the medium
The medium could be potentially observed to be idle by a third party STA
  if the third party STA doesn’t hear the TF, and also is far away from the STAs sending UL sounding NDP, then the third party STA may occupy the medium, such that the following transmissions of UL/DL NDP may suffer.

## Slide 7: Concerns about Staggered NDP (Cont’d)
To provide more protection for the UL sounding NDP transmission, MU-RTS/CTS in 11ax can be reused (AP implementation dependent)
The likelihood of the scenario is low:
  Require a STA to not observe the TF transmitted at low MCS.
  Activation of the MU-RTS/CTS is implementation dependent
  The loss of medium is offset by gain due to lower overhead for the entire measurement:
    Single DL NDP serves large number of clients
    Single TF frame serves large number of clients

## Slide 8: MU-RTS/CTS Protection
SIFS
SIFS
Responder
or AP
STA
1
STA
2
STA
3
NDP
SIFS
SIFS
NDP
NDP
NDP
Trigger
Frame
SIFS
RTS
CTS
CTS
CTS
SIFS
NDPA
SIFS

## Slide 9: Compressed NDP optimization
NDPA
SIFS
SIFS
Compressed NDP
Trigger
Frame
MU-NDP
SIFS
SIFS
Responder
or AP
STA
1
STA
2
STA
3
MU-NDP
MU-NDP
NDP

## Slide 10: Compressed NDP Optimization
Compressed NDPs
  Removing all redundant preambles (legacy+signaling)
  Solving near-far problem
    Keeping HE-STF for AGC purpose
    Time domain multiplexing
  Preamble after each HE-STF is like in the regular NDP case
  Still the P matrix is according to the number of Tx antenna similar to any MIMO transmission
The order of preambles is according to the trigger frame
Responder send NDP frame to all STAs

## Slide 11: Summary
We’ve demonstrated use of NDP based sounding that:
  Supports 11ax MU mode featuring:
    Full BW measurement
    Full MIMO measurement
    Insensitivity to near-far problem
    Medium efficient by supporting a large number of STAs in a single measurement sequence, and by this minimizes the overhead
Propose to reuse the MU-RTS/CTS in 11ax to avoid the third party STAs occupying the medium during the uplink sounding

## Slide 12: Appendix: Air Time Comparison
Assume 6 STAs each with 2 Tx antennas and 2xLTF+1.6CP
Staggered NDP
  6SIFS+6HE_NDP_header+6HE_STF+6HE_LTF = 6*(16+28+4+16) = 384us
Compressed NDP
  SIFS+HE_NDP_header+6HE_STF+6HE_LTF = 16+28+6*(4+16) = 164us
Compressed NDP uses about 60% less air time for the UL sounding interval