## Slide 1: Clarification on TRN Subfield Definition for MIMO
Date: 2017-02-01
Authors:

## Slide 2: Introduction
This presentation raises as issue with TRN subfield definition for MIMO with NSS > 2 voted in [1] and proposes resolution.

## Slide 3: Motion #147
Do you agree to add the following to the draft:
  The basic TRN field has the structure:
  {GaiN, -GbiN, GaiN, GbiN, GaiN, -GbiN}
  where N is 128, 192, 256, 512 for channel bonding 1, 2, 3, 4 respectively and i defines the spatial stream number.
Result: motion passed.

## Slide 4: Motion #150
Do you agree to add the following to the draft:
  EDMG TRN subfield for CB = 1, 2, 3, 4 and MIMO NSS = 1, 2, … 8, shall have a structure shown below (slide #9 of 16/1636r0). The GaN/GbN sequence length is defined as N = 128 * CB. All sequences GaN/GbN are defined in the draft.
Result: motion passed.
NSS | TRN subfield: 1, 3, 5, … 2M-1 | TRN subfield: 2, 4, 6, …, 2M
i = 1, 2 | {+GaiN, -GbiN, +GaiN, +GbiN, +GaiN, -GbiN} | 
i = 3, 4 | {+GaiN, -GbiN, -GaiN, -GbiN, +GaiN, -GbiN} | 
i = 5, 6 | {+GaiN, -GbiN, +GaiN, +GbiN, +GaiN, -GbiN} | {-GaiN, +GbiN, -GaiN, -GbiN, -GaiN, +GbiN}
i = 7, 8 | {+GaiN, -GbiN, -GaiN, -GbiN, +GaiN, -GbiN} | {-GaiN, +GbiN, +GaiN, +GbiN, -GaiN, +GbiN}
Table 1: Proposed EDMG TRN subfields definition for MIMO.

## Slide 5: TRN Definition Issue
For MIMO case with NSS > 2:
  Motions #147 and #150 define different TRN subfield structure, however both use the same Golay sequences set;

## Slide 6: Proposed Resolution
It is proposed to consider the basic TRN subfield definition in Motion #147 and generalize it for the case of MIMO with NSS > 2.
The generalization uses the same approach as adopted for EDMG-CEF definition.

## Slide 7: Proposed Resolution (Cont’d)
The TRN subfield definition for NSS ≤ 2 can be written as follows:
  TRNibasic = {GaiN, -GbiN, GaiN, GbiN, GaiN, -GbiN};
  If one defines Gui2N = {-GbiN, GaiN} and Gvi2N = {GbiN, GaiN};
  Then TRNibasic = {GaiN, Gui2N, Gvi2N, -GbiN};
  It has similar structure as EDMG-CEF, [2];
The definition of TRN subfield for NSS > 2 is based on orthogonal matrix P:
  +1, +1, +1, +1
  +1, -1, +1, -1
  +1, +1, -1, -1
  +1, -1, -1, +1

## Slide 8: Proposed Resolution (Cont’d)
For MIMO with 1 ≤ NSS ≤ 2:
  TRNi = TRNibasic, i = 1, 2;
For MIMO with 3 ≤ NSS ≤ 4:
  TRNi = {+TRNibasic, +TRNibasic}, i = 1, 2;
  TRNi = {+TRNibasic, -TRNibasic}, i = 3, 4;
For MIMO with 5 ≤ NSS ≤ 8:
  TRNi = {+TRNibasic, +TRNibasic, +TRNibasic, +TRNibasic}, i = 1, 2;
  TRNi = {+TRNibasic, -TRNibasic, +TRNibasic, -TRNibasic}, i = 3, 4;
  TRNi = {+TRNibasic, +TRNibasic, -TRNibasic, -TRNibasic}, i = 5, 6;
  TRNi = {+TRNibasic, -TRNibasic, -TRNibasic, +TRNibasic}, i = 7, 8;

## Slide 9: Straw Poll
Do you agree to add the following to the draft:
  The EDMG-TRN subfield for MIMO with NSS > 2 shall be defined as shown on slide #8;

## Slide 10: References
11-17-0186-00-00ay-a-compendium-of-motions-related-to-the-contents-of-the-draft-amendment-for-tgay
Draft P802.11ay_D0.1