## Slide 1: Feedback of Short SSW Packet Based Sector Sweep in DTI
Date: 2017-02-22
Authors:

## Slide 2: Problem Statement
Channel measurement feedback of sector sweep is required for the BRP setup subphase of SISO BF and the SISO phase of SU/MU-MIMO BF [1].
Channel measurement feedback data for sector sweep in DTI can be carried in Channel Measurement Feedback element and optionally in EDMG Channel Measurement Feedback element.
Unlike SSW frame, Short SSW packet contains CDOWN value, but does not contain Sector ID and Antenna ID.
Neither Channel Measurement Feedback element nor EDMG Channel Measurement Feedback element is enough to carry channel measurement feedback data for sector sweep using Short SSW packet.

## Slide 3: Proposal
Modify EDMG Sector ID field of the EDMG Channel Measurement Feedback element to carry part of channel measurement feedback data for sector sweep using Short SSW packet.
  Additional changes on Channel Measurement Feedback element and DMG Beam Refinement element are also necessary.
Sector Sweep in DTI | Channel Measurement Feedback element | EDMG Channel Measurement Feedback element
SSW frame based | SNR Sector ID Order (for sector sweep involving non-EDMG STAs) | EDMG Sector ID Order including TX sector IDs (for sector sweep involving EDMG STAs only)
Short SSW packet based | SNR | EDMG Sector ID Order including CDOWN values (for sector sweep involving EDMG STAs only)
For proposed changes on Channel Measurement Feedback element, DMG Beam Refinement element and EDMG Channel Measurement Feedback element, please refer to the document (IEEE 802.11-17/0219r2) for details.

## Slide 4: SP
Do you agree to incorporate the proposed changes on Channel Measurement Feedback element, DMG Beam Refinement element and EDMG Channel Measurement Feedback element as shown in IEEE 802.11-17/0219r2 into the next draft 11ay specification?
  Y
  N
  A

## Slide 5: Reference
[1] Candidate Draft P802.11ay_D0.2