## Slide 1: Link Adaptation Feedback for Combating Interferences
Date: 2017-03-06
Authors:

## Slide 2: Problem statement (1/3)
Interferences cause throughput drop and even link loss
Time
Throughput with legacy link adaptation
Time
Throughput knowing presence of interference
Interference
Low average
throughput
High average
throughput

## Slide 3: Problem statement (2/3)
Unlike noise, interferences usually concentrate in part of frequency or time
  Narrow band interference (NBI) e.g. clock harmonics and Bluetooth
  On-off interference (OOI) e.g. microwave oven, Bluetooth, and USB bus
Freq
Time
…
Freq
Time
…
Narrow band interference
On-off interference
MPDU corrupted by interference

## Slide 4: Problem statement (3/3)
Reducing MCS doesn’t help
  Narrow band interference still corrupts the same percentage of signal
  On-off interference causes a vicious cycle: with lower MCS, MPDU duration becomes longer and more vulnerable to interference
Freq
Time
…
On-off interference
On-off interference
MPDU corrupted by interference

## Slide 5: Solutions
DCM and short MPDU are efficient for NBI and OOI
However, Tx doesn’t even know the presence of interference at Rx
Freq
Time
…
Freq
Time
…
Narrow band interference
On-off interference
Duplicated DCM copies
Survived MPDU

## Slide 6: Adaptation via feedback
Link adaption feedback can tell transmitter to use DCM and shorter MPDU for combating narrow band interference and on-off interference, respectively
CID 9619, “The HE-MCS defined in 28.5 varies depending on DCM. The HE link adaptation mechanism should also include a recommendation of the DCM.”

## Slide 7: Link adaptation feedback
Currently, link adaptation parameters i.e. Nss and MCS are piggybacked in Aggregated Control subfield of HE variant HT control field in MAC header

## Slide 8: Available feedback field
Control Information subfield of link adaptation still has 9 reserved bits currently

## Slide 9: Feedback for DIM
Use 1 reserved bit for Rx to recommend DCM
  Combat NBI by sending data over two sets of tones
NSS
HE-MCS
DCM
Reserved
Bits:
3
4
1
8
B0
B2
B3
B6
B7
B8
B15

## Slide 10: Feedback for short MPDU
Use 1 reserved bit for Rx to recommend short MPDU duration (SMD)
  Combat OOI by shortening MPDU duration e.g. down to 0.2 ms
  Indicate the presence of OOI such that Tx knows RSSI is not reliable for link adaptation
NSS
HE-MCS
DCM
SMD
Reserved
Bits:
3
4
1
1
7
B0
B2
B3
B6
B7
B8
B9
B15
MPDU 1
MPDU 2
…
MPDU 64
A-MPDU

## Slide 11: Summary
Reducing MCS is not efficient to combat interference
Tx needs to tell Rx about the presence of interference
A-Control field still has 9 bits available for link adaptation
Propose to use 1 reserved bits for DCM and 1 reserved bit for short MPDU duration

## Slide 12: Straw Poll 1
Do you support using one reserved bit in Control Info subfield of HE link adaptation for DCM?
  For example
Y: N: A:
NSS
HE-MCS
DCM
…
Bits:
3
4
1
B0
B2
B3
B6

## Slide 13: Straw Poll 2
Do you support using one reserved bit in Control Info subfield of HE link adaptation for short MPDU duration?
  Short MDPU duration is shorter than 0.2 ms
  For example
Y: N: A:
NSS
HE-MCS
SMD
…
Bits:
3
4
1
B0
B2
B3
B6