## Slide 1: WUR Beacon
Date: 2017-03-12
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com

## Slide 2: Abstract
We consider WUR Beacon in this presentation

## Slide 3: WUR Beacon
Enable periodic WUR Beacon from AP to STA in WUR mode
  To maintain STA connectivity with the AP, when STA’s primary connectivity radio is off. This is useful for mobile STAs such as phones.
  To maintain time synchronization with the AP for a STA when the STA is in the WUR state for a long period of time. This is useful for periodic WUR receiver on/off.
  Size of the WUR Beacon needs to be controlled due to low PHY rate (discussed later)
  Expect a large periodic interval to reduce overhead
    The interval can be signaled in WUR response during negotiation. [5]
  WUR Beacon needs to be differentiated from wake-up packet
AP
STA
WUR beacon
WUR Beacon Interval
WUR beacon
WUR Beacon Interval
WUR beacon
WURx on
802.11 off
WURx
802.11
Example:
WURx off
WURx on
WURx off
WURx on

## Slide 4: Discussion of Slides in IEEE
Motivations for WUR Beacon have been widely discussed in IEEE [1,2,3,4]
  To remain connected with AP [1,2,3]
  To maintain synchronization [2]
  To enable low power AP scanning [4]
[1,4] discusses possibility of simply monitoring any transmission from AP
  Since transmission from AP is unpredictable, relying on existing wake-up packet transmission from AP does not help a STA to set the criteria of determining it is out of range
  If a STA chooses to wake up primary connectivity radio after not observing any activity from AP for a fixed period, then the STA can not turn primary connectivity radio off for a long time.
We think it is useful to define WUR Beacon

## Slide 5: Timing drift analysis for WUR Beacon
We assume TSF timing accuracy of +-100 ppm for the analysis based on the current TSF timing accuracy requirement in the spec [10].
  Consider both AP and STA sides clock drift, the maximum drift is +-200 ppm.
  Larger TSF size increases the overhead under low PHY rate [6]
  Smaller TSF size limits the maximum correctable timing drift.
A table that summarizes the tradeoff is shown in the next slide.

## Slide 6: Timing drift analysis for WUR Beacon
The size of TSF will depend on the maximum WUR Beacon Interval
  TSF size = 3 bytes looks like a reasonable choice based on the analysis
  Note that the maximum legacy beacon interval is around 65s
TSF size (N) | 1 byte | 2 bytes | 3 bytes | 4 bytes
Overhead under 250 kbps [6] | 32us | 64us | 96us | 128us
Maximum correctable drift with TSF size of N | ±128us | ±32768us | ≈±8*10^6us | ≈±2*10^9us
Corresponding time that creates the maximum correctable drift without receiving WUR Beacon | 0.64s | 164.84s | ≈4*10^4s | ≈10^7s
Number of missed WUR Beacons if interval is 500 ms [8] | 1 | ≈320 | ≈8*10^4 | ≈2*10^7
Number of Missed WUR Beacons if interval is 10s [10] | 0 | ≈16 | ≈4000 | ≈10^6

## Slide 7: Overhead of WUR Beacon
Assume 250 kbps [6]
Payload (this is just an example)
  MAC Header:
    Packet Type: 4 bits
    AP ID: 24 bits
  Frame Body:
    TSF: 24 bits
    Other fields: TBD
    Elements in the Current Beacon: Not applicable
  FCS: 8 bits
Without TSF, the length is 144 us. With TSF, the length is 240 us.
Assume that the overhead is acceptable once we have a larger WUR Beacon interval than the regular beacon (e.g. 1s or 10s compared to 100ms)
  Note that according to [9], the measured Beacon duration is 976us on average

## Slide 8: Alternative Solution: Periodic Primary Connectivity Radio Wake Up
Benefits of WUR Beacon can also be achieved by periodic primary connectivity radio wake up to receive legacy beacon
  Specifically, STA wake up primary connectivity radio once every x seconds
We think that the cost of this alternative approach is higher in terms of power consumption. Specifically, follow similar comparison of [7]
  With WUR Beacon, STA maintains average 100uW power consumption
  Without WUR Beacon, every x seconds, STA goes through
    Time to wake up primary connectivity radio: 5mW for 10 ms[8]
    Listen time to accommodate drift: 55mW[8] for 0.2ms*x
    Potential listen time for AP channel access of sending Beacon: 55mW[13] for 15ms[12]
    Listen time for receiving Beacon: 110mW[8] for 3.1ms
x | 0.5 | 1 | 10 | 100 | 1000
Additional average power consumption | ≈1600 uW | ≈800uW | ≈90uW | ≈19uW | ≈12uW
Average drift under 100ms WURx wake up period | 0.05ms | 0.1ms | 1ms | 10ms | 100ms
% of 100ms WURx wake up period | 0.05% | 0.1% | 1% | 10% | 100%

## Slide 9: Conclusion
We consider defining WUR Beacon
  For maintaining connectivity between STA and AP
  To carry timing information for synchronization purpose
  To carry other TBD information
  To be differentiated from wake up packet
  With consideration of controlling overhead
  The WUR Beacon interval should be configurable

## Slide 10: Straw Poll 1
Do you support the following?
  Define WUR Beacon

## Slide 11: Straw Poll 2
Do you support the following?
    WUR Beacon can carry timing information (ex. TSF) to help the STA, that turns off the primary connectivity radio, to maintain synchronization
  Deferred

## Slide 12: Straw Poll 3
Do you support the following?
  WUR Beacon interval can be indicated in WUR Mode element

## Slide 13: Reference
[1] 11-16-1445-00 Overall MAC Procedure for WUR
[2] 11-16-1504-00 Discussion of WUR Packets Design
[3] 11-16-1217-00 WUR-based Broadcast Reference Signal
[4] 11-16-1501-00 AP Discovery using WUR
        [5] 11-17-0071-00 High Level Mac Concept for WUR
[6] 11-16-0341-00 LP-WUR (Low-Power Wake-Up Receiver) Follow-Up
[7] 11-15-1307-02 Low-Power Wake-Up Receiver (LP-WUR) for 802.11
[8] 11-14-0980-16-00ax-simulation-scenarios
[9] 11-11-1413-03-00ai-real-air-time-occupation-by-beacon-and-probe
[10] 802.11-2016